## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 12
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Exam 1 Graded
Exam 1 Statistics
  Average: 75.87
  Median: 80
  Max: 100 (2)
  Bimodal distribution
Chart: Exam 1 - Histogram
| 41-50 | 51-60 | 61-70 | 71-80 | 81-90 | 91-100
 | 3 | 5 | 0 | 8 | 9 | 6
Chart: Exam 1 - Per Problem Average Score (Normalized)
| Prob1 | Prob2 | Prob3 | Prob4 | Prob5 | Prob6 | Total
 | 0.73978 | 0.84301 | 0.70968 | 0.86774 | 0.6 | 0.7471 | 0.75871

## Slide 3: Outline
Physical memory
  Characteristics and parameters
  Types
  Constraints and tradeoffs
  In LC-3b

## Slide 4: What Is Memory?
Component that remembers one or more values
  Registers
  SRAM (Static RAM)
  DRAM (Dynamic RAM)
  Non-volatile RAM (typically abbreviated NVM)
  Disk
  CAM
Our systems are mostly memory
Exciting times
  Packaging changes
  Device changes
  Interface changes
4
Notes: 4

## Slide 5: What Is Memory in this Picture?
5
uPC
Logic
n
p
z
IR
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Notes: 5

## Slide 6: What Is Memory Used For?
Persistent data
  How much is in your bank account?
Code
  Your application
  Operating system, etc.
Intermediate computation
  A = B + C
  D = A * 4
6
Notes: 6

## Slide 7: Accessing Memory
Access by address
  UT Austin, 201 E 24th St., POB 6.248, Austin, TX, 78712
  Computers use binary addresses
    Easy to represent and operate on
Access by content
  Screaming down the hall “who’s got the scissors”
  Google “I’m feeling lucky”
  Your own memory
  CAM (Content-Addressable Memory)
Both methods useful
  Address: when you know where what you want is
  Content: when you know what you want but not sure where it is
Notes: 7

## Slide 8: Abstract View of Memory
Address
n
CE (Chip Enable)
WE (Write Enable)
k
How large?
Content
<= (2n * k) bits
Notes: 8

## Slide 9: How Much Memory?
As much as you need and no more (expensive)
How much do you need?
  How big is your OS?
    Windows / macOS 512MiB+ (need >2GiB)
    Seems to be growing with time
  How big is your data?
    Tools / Simulators that need tens to hundreds of GiBs
    There are analytics tools that need many TiBs
    Scientific computing needs PiB of memory
How much can I get?
  Cost?
  Available capacities
  System capability
9
Notes: 9

## Slide 10: Early days SRAM  Magnetic Core Memory
Magnetic Core memory
  A set of memory planes of ferromagnetic rings
  Each ring can have magnetic flux circulating one way or the other
  Enough current through the ring can flip polarity
  Write: passing half that current through both a single X and Y wire …
  Read: try to write 0 and see if any pulse on Sense line
  Destructive reads! Read flips to 0, so have to rewrite any 1s
  Only single bit accessed per plane

## Slide 11: How much memory can fit in a chip?
Common chip size is order of 100 mm2
Core memory:
  Density ~1 bit per mm2
  So can have ~100 bits per “chip” in today’s world!
SRAM
  .0588 um2 per bit in 14nm process technology
  So can have >1 billion bits
Is 1 billion bits a lot?
  Just ~128MiB, not enough for even just Windows
Denser memories needed

## Slide 12: Memory Layout Across One Chip
16b
8
3b address
16
Notes: 12

## Slide 13: Memory Layout Across Two Chips
16b
8
3b address
High
8
Low
8
Notes: 13

## Slide 14: Multiple Memory Chips
X8
high
8
X8
low
8
16
MDR
15:1
CE
CE
WE
WE
0
logic
MAR
Notes: 14

## Slide 15: Issue
LC-3b, like many machines, is byte-addressable
However, LC-3b word is 16b (2 bytes)
What does this imply?
A
0
B
1
C
2
D
3
4
5
6
7
8b

## Slide 16: A Specific Memory does not always contain the “High” or “Low” byte
1
0
3
2
5
4
7
6
9
8
11
10
13
12
15
14
x8
x8
*((uint16_t)0)
*((uint16_t)3)
Note: LC3b doesn’t have unaligned memory operations
  It is byte addressable but LDW and STW are word aligned!

## Slide 17: Methods For Dealing with Alignment
ISA
  Don’t allow unaligned accesses (Alpha)
  Software deals with it
  Issues?
Hardware
  Processor-centric
  Memory sub-system centric
Notes: ISA needs to read multiple words and insert the correct bits into the correct parts of the words
painful certainly. Common?

## Slide 18: Hardware Alignment

## Slide 19: Memory Layout Across Four Chips
16b
8
3b address
[15:
12]
4
[7:4]
[11:8]
[3:0]
Notes: 19

## Slide 20: Memories of Specific Generation Typically Store Same Number of Bits (tech dependent)
As RAM output gets wider, RAM height gets shorter
  Same number of bits per RAM!
32M
x4
16M
x8
8M
x16
Notes: 20

## Slide 21: Narrower RAMs Enable Greater Capacity Given Constant Total Width
8M x 16
32M x 4
32M x 4
32M x 4
32M x 4
Notes: 21

## Slide 22: More Memory
x8
8
x8
8
addr
MAR
CE
CE
WE
WE
0
logic
x8
8
x8
8
CE
CE
WE
WE
Any Problems?
Notes: 22

## Slide 23: Separate CE (two “ranks”)
x8
8
x8
8
addr
MAR
CE
CE
WE
WE
0
logic
x8
8
x8
8
CE
CE
WE
WE
1
16
Notes: 23

## Slide 24: What makes a good memory?
Is it just capacity and cost?
What else could it be?

## Slide 25: What’s a memory cell anyway?

## Slide 26: Small-capacity memories just use logic
SR flip-flop / latch
D flip-flop / latch
How big (how many transistors)?

## Slide 27: Small-capacity memories just use logic
SRAM
  Static RAM (holds value while power is on)
  Densest logic-only memory
  6 carefully laid-out transistors
word line
=

## Slide 28: Example memory: SRAM Array
word line 0
word line 1
b0
b0
b1
b1
b2
b2
b3
b3
word line 2
word line 3
Sense Amplifiers
Word decoder

## Slide 29: Example memory: SRAM
From Intel:
  200 – 300 f2 per cell for high-performance
    f2 is a unit of area – feature-size squared
    Limited by transistors and wires
  Can go down to ~120 – 150 f2 for high density
    What does cell size have to do with performance?
    Small transistor drive less current – switch lines more slowly

## Slide 30: Important SRAM notes
SRAMs are very carefully laid out – amortize costs over many bits (8Kb or more usually)
In large arrays, the latency of access is dominated by the latency of the wires!
  Therefore, the larger the memory, the slower it is (generally)
Things are more complex in reality

## Slide 31: When logic is too expensive, use different physics
Early days – magnetic core memory
  Smaller than vacuum tube logic
  Not small by today’s standards

## Slide 32: DRAM uses transistors and capacitors

## Slide 33: DRAM uses transistors and capacitors
33
What happens when you read?
Notes: 33

## Slide 34: DRAM uses transistors and capacitors
34
What happens when you read?
Infineon 80nm
Notes: 34

## Slide 35: DRAM Refresh
Capacitor holding value leaks, eventually you will lose information (everything turns to 0)
How do you maintain the values in DRAM?
35
Notes: 35

## Slide 36: Simplified DRAM Internal Structure
Will discuss details of DRAM architecture in another lecture!
36
Row
Column
RAS
CAS
Addr
Notes: 36

## Slide 37: DRAM is still kind of big
Current DRAM cell is 6f2, and f is around 20nm
  So, 416Mb per mm2
  In reality, a lot of area is “lost” to supporting (peripheral) circuits
But DRAM scaling is challenging
  More problems as dimensions shrink – 10nm will be 4x density, but really hard to achieve
How can we do better?
  Use even denser memories
  Reduce peripheral circuits
  Go vertical – store in 3D

## Slide 38: FLASH Memory
Relies on quantum tunneling!
A floating (insulated) second gate (~4f2 today)
Learning to count electrons
  Multi-level cells

## Slide 39: NAND FLASH (reduce wires and periphery)
Access entire page at a time
But, only allow one to possibly affect the read
Have to program and erase together

## Slide 40: Go vertical

## Slide 41: Even that’s not densest
Magnetic disks and tapes win that right now
  ~100nm2 per cell (< “1f2” today)
  Stack multiple platters in disks
  Tape is thin and wrapped

## Slide 42: And even that may not be densest
3D crossbar memories
  Resistive storage
  Sense the current
  No access transistors!
  But, really dense still in research
    Periphery is large
    Reliability is a problem
DNA storage
  Science stage
  May never be good for computing
  Why?
Holograms
...

## Slide 43: Bottom line -- tradeoffs
Can’t get the cost/capacity we want at the latency we want
So use multiple technologies at once
Memory
Cheap
Efficient
Dense (high capacity)
Fast
Reliable