## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 13
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Reminder: Exam 1 only counts for 14% of total grade!
  Stay focused!
  Come see me during office hours for any concerns
Lab 3 due this weekend
Graduate Lab will be posted soon
  Will give you a taste of what it is like to do research in computer architecture

## Slide 3: Last time: Physical Memory
Can’t get the cost/capacity we want at the latency we want
So use multiple technologies at once
Memory
Cheap
Efficient
Dense (high capacity)
Fast
Reliable

## Slide 4: Outline
Virtual memory intro review
Page-based virtual memory basics
VAX address translation
Demand paging

## Slide 5: Virtual Memory: an illusion of infinite private memory
Virtual memory consists of
  Address translation
    Provides the illusion of a large, uniform, protected address space to each process
      Addresses in program remain the same (virtual addresses)
      Actual physical address is different
    Program-transparent way to share RAM between processes
  Demand paging (caching)
    Using memory as a cache for disk
    Transparently move data between RAM and disk to give the illusion of a large memory
Provides the basic underlying structure needed to multitask the entire computer

## Slide 6: Abstract Virtual Memory
Magic Virtual
Memory Module
(Memory
Management
Unit)
User 1
User 2
User n
Relocatability?
Scalability?
addr1
data
addr2
data
Permissions
Translate address
  fetch from disk

## Slide 7: Different Names in Different Places
Programmer uses text-based names
  int array[100];
Compiler maps names to flat, uniform space
  Starting point is relative, size specified (see next slide)
Assembler maps uniform space to virtual addresses
  Mechanical transformation
Processor instructions use virtual addresses, translates to physical addresses
Compiler
Assembler
ISA
instructions
Address
mapping
Symbolic
address
Relative
address
Virtual
Address
Physical
Address
Virtual
Address
Processor

## Slide 8: Processes, threads, and contexts
Need mechanism for managing memory spaces and multitasking
A process is a unit of management for the OS to determine memory and I/O resources
  Each process has its own virtual memory space
    A process has a hardware context associated with it
A thread is a unit of management for compute time
  A process may have multiple threads
  All threads in a process share same process context (same virtual address space)
  Each thread has its own execution context:
    Registers, condition codes, stack, …

## Slide 9: Separate Address Space per Process
1
Process 1
Page Table
1
Process 2
Page Table
1
Process 3
Page Table
OS
pages
Page table - one per process
contains an entry for each user page
Page frame table - one for the whole system
contains bookkeeping info about each page frame
in the physical memory (free?, user name)
Physical Memory

## Slide 10: VAX Virtual Memory
VAX == Virtual Address Extension
  Extended PDP-11
32b address space, byte addressable
Single family of machines that had different performance and amounts of memory but all ran the same programs
VAX pages are 512 bytes (small)

## Slide 11: VAX View Of Memory
P0 (Program) Region
P1 (Control) Region
System Region
(Reserved)
Process space
System-wide space
PT
Virtual page #
Byte offset
0
0
P0 Region
0
1
P1 Region
1
0
System space
unused
1
1
0
230
231
232
User Stack
User Heap
User Code
Kernel

## Slide 12: VAX Page Tables
One for each region (P0, P1, System)
  Why?
Each page table stored sequentially in System memory
PTE: Page Table Entry
PO Length Register and PTE used for ACV (Access Control Violation) checks
PTE used for TNV (Translation Not Valid) checks
PTE for Page 0
0
PTE for Page 1
1
PTE for Page 2
2
PTE for Page L-1
L-1
L
P0 Base Reg
P0 Length Reg
In Process Context

## Slide 13: VAX Page Table Entry (PTE)
V
Protection
field
M
Reserved
Physical frame number
Valid?
Do I have the right to read/write?
Modified?
20
0
How many pages of physical memory?
How much physical memory?
{NO, R, R/W}{K,E,S,U}
(81 possibilities in 4 bits?)
31
30:27
26
Kernel
Executive
Supervisor
User

## Slide 14: Abstract VAX Virtual Memory
0
Virtual page num
Byte offset
VA
VPageNum < P0LR? Else ACV fault!
Read appropriate PTE
V
Protection
PFN
V
Protection
PFN
V
Protection
PFN
P0BR
0
3. Allowed access? Else ACV fault!
4. Page resident? Else TNV fault!
OK! Construct physical address
PFN
Byte offset
P0LR
<
V
Protection
V
Protection
PFN
Page table
8
0
9
29
P0
31

## Slide 15: But, page tables take up too much space
Let’s say each process wants 128MB worth of pages
  Each process needs 256K pages (512B / page)
  Each page table size = 256K PTEs * 4B/PTE = 1MB
Let’s say we have 100 processes
  100MB just for page tables!
We don’t need all tables and all entries at the same time!

## Slide 16: Page Tables in Virtual Memory!
Use same paging mechanism for page tables!
Page page tables, don’t waste memory
But, how do we find physical location?

## Slide 17: How Is It Possible to Put PTEs in Virtual Memory???
If you put a page table entry in virtual memory, you need a second page table entry to get to the first page table entry
  Aren’t you in an infinite loop???
So, page table entries must live in another kind of virtual memory
  PTEs of VM1 live in VM2, PTEs of VM2 live in VM3, etc.
At some point, a PTE must live in physical memory!

## Slide 18: User Page Tables Have System Virtual Memory Addresses
Virtual memory
Physical memory
What sort of address is SBR?

## Slide 19: Translation Overview
A = X implies LD X
Need to find the PTE of page containing X (PTE(X))
  Use P0BR to determine virtual address of PTE(X)
    But, PTE(X) is virtual address!
      Use SBR to determine physical address of PTE(PTE(X))
      Read PTE(PTE(X)) to determine physical page/permissions of PTE(X)
        Check permissions
        Create physical address
  Read PTE(X) to determine physical page/permissions
    Check permissions
    Create physical address
  Read X using physical address

## Slide 20: Important notes
PTEs always hold physical frame numbers
  PTE(X) points to physical memory
  PTE(PTE(X)) also points to physical memory
  It’s the virtual page numbers that can point to PTEs and then require some translation
Page tables in VAX always contiguous in memory
  For every segment, including the system segment
There is one system page table (shared by all processes)
The system page table is in physical memory
  If not, you can’t find it

## Slide 21: Specific Example: Step-by-Step 9b virtual address, 8 physical pages
00
01
01010
x4
+
x4
+
100 00100
V
Per
001
001
V
Per
010
VA of X
System Region PTE
PTE of page containing X
10
01
00100
100100000
P0BR
10000000
SBR
00100
010
01010
VA of PTE of Page containing X
(in System Region)
X in physical memory
PA of System Region PTE
PA of PTE of page containing X
PA of X

## Slide 22: Support for Paging the Page Table
Page tables only contain physical addresses
  page of PT in memory contains memory or disk addresses
  page of PT on disk contain only disk addresses
    page in PT cannot be moved to disk before all its pages in memory are moved to disk
Special “untranslated” addressing mode required if page tables are traversed in software
  Sparc: Translation disabled processor state
  Alpha: Special kseg segment whose addresses are not translated. PT’s mapped to kseg
Protection mode in processor necessary to maintain integrity of translation process
  Don’t let a user process modify the page table, only trusted code

## Slide 23: Demand Paging

## Slide 24: Storage Hierarchies
Storage is hierarchical in the order (away from the CPU) of
  increasing latency ti ti < t i+1
  increasing size si & decreasing cost ci si ≤ s i+1, ci ≥ c i+1
  decreasing transfer bandwidth bi bi ≥ b i+1
  increasing natural unit of transfer xi xi ≤ x i+1
Level 0: Registers
Level 1: Caches
Level 2: Main Memory (Primary Storage)
Level 3: Disks (Secondary Storage)
Level 4: Tape Backup (Tertiary Storage)
CPU
Cache
$
Memory
Cache
$
Level 1
(L1 $)
LLC
Disk
…

## Slide 25: Hierarchical Storage
Each level memoizes values stored at lower levels of storage to avoid full latency cost when accessing
Effective Access time Ti = hi ti + (1- hi) ti+1
  where hi is the ‘hit’ ratio, the probability of finding the desired data memoized at level i
Given good locality of reference (i.e., small working set), hi » 1 Þ Ti » ti
Balanced system gives the best of both world
  The performance of higher-level storage
  The capacity of lower-level low-cost storage.

## Slide 26: Details: RAM vs. Disk
Disks much cheaper than RAM (consumer prices below)
  Disk currently about $90 2TB
  FLASH currently $90 206GB
  DRAM currently $90 for 16GiB DDR3 1866MHz
  Disk >100X cheaper than DRAM, FLASH right in between
Disks much slower than RAM
  Disks (a fast one)
    4.2ms read seek time, 100MiB/sec sustained rate
  FLASH
    Read time ~10us, 2GiB/sec sustained rate
  Memory DDR2
    50ns – 100ns to read a block of memory
    ~15GiB/s sustained rate
  Disks 4-5 orders of magnitude longer latency, 15-25 times less bandwidth FLASH right in between
Careful with prices though – not always just technology

## Slide 27: Disk As Another Memory Hierarchy Level
Disks huge compared to RAM
  Can we use disks as backing store to RAM?
  Make RAM look as big as disk but as fast as RAM?
    What caches did for RAM
Do it manually or automatically?
Relies on locality
Memory is a Cache for Disk
Important for sharing
  May be more than one program resident on computer at a time
  Aggregate program demands may be more than RAM

## Slide 28: Demand Paging with Page Tables
Translation determines if page is in memory
On page fault (page not valid), bring page into memory
  OS finds empty page frame in memory (free list)
  OS finds page on disk
  OS reads page into memory
Write backs of modified pages?
  When done?
Free page lists
  FIFO or LIFO? Something else?
1
Process 1
Page Table
1
Process 2
Page Table
1
Process 3
Page Table
OS
pages
Physical Memory

## Slide 29: Replacement Policy
When referenced page is not in primary memory, must be brought in from secondary memory
If no free page frame available, a page needs to be thrown back to secondary memory
  which page should be replaced?
Generally Least Recently Used (LRU) policy used
  replacement policy in software

## Slide 30: Implementing an LRU analog (not recently used)
Field in PTE maintained by software
  1 - not a candidate for replacement
  i.e., recently referenced
  0 - a candidate for replacement
  i.e., not recently referenced
How is table updated when there is a
page fault or a TLB miss?
Algorithm:
Pointer to last examined page maintained
If the examined entry is 1, it is turned to 0 and the
pointer is incremented by 1, otherwise found victim
0
1
1
0
0
1
1
0

## Slide 31: Required Support for Virtual Memory
Page table
  presence bit
    present Þ primary memory address
    missing Þ secondary memory address or “doesn’t exist”
  protection bits: “read only”
  usage bits: accessed?, dirty?
Page fault
  synchronous exception in case of missing page or protection violation
Translation mechanism
Swapping Store and I/O
  separate from file store
Page fault handler
  free page lists for primary and secondary memory

## Slide 32: Caching vs Demand Paging
CPU
CPU
cache
primary
memory
primary
memory
secondary
memory
caching demand paging
cache entry page-frame
cache block (~32B) page (~4k bytes)
cache miss (0.1% to 20%) page miss (~.001%)
cache hit (~1 cycle) page hit (~100-300 cycles)
cache miss (~100-300 cycles) page miss(~15M cycles)
a miss is handled in a miss is handled either in
hardware software or hardware