## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 14
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Final Exam Schedule confirmed
  Dec 14 (Fri), 7-10pm, ECJ 1.214 (Not this classroom!)
This week only: Pritesh traveling on Friday
  No Discussion Section on Friday
  Please attend the Thursday one or Office Hours
Lab 4 and Grad Lab will be posted soon

## Slide 3: Virtual Memory: an illusion of infinite private memory
Virtual memory consists of
  Address translation
    Provides the illusion of a large, uniform, protected address space to each process
      Addresses in program remain the same (virtual addresses)
      Actual physical address is different
    Program-transparent way to share RAM between processes
  Demand paging (caching)
    Using memory as a cache for disk
    Transparently move data between RAM and disk to give the illusion of a large memory
Provides the basic underlying structure needed to multitask the entire computer

## Slide 4: Abstract Virtual Memory
Magic Virtual
Memory Module
(Memory
Management
Unit)
User 1
User 2
User n
Relocatability?
Scalability?
addr1
data
addr2
data
Permissions
Translate address
  fetch from disk

## Slide 5: VAX User Page Tables Have System Virtual Memory Addresses
Virtual memory
Physical memory

## Slide 6
P0LR vs P1LR Length Checking
P0 (Program) Region
P1 (Control) Region
System Region
(Reserved)
0
230
231
232
User Stack
User Heap
User Code
Kernel
PT
Virtual page #
Byte offset
29
9

## Slide 7: More reading about VAX Virtual Memory System
(optional)
Nice overview of basic concepts
  http://pages.cs.wisc.edu/~remzi/OSTEP/vm-vax.pdf
VAX Architecture Reference Manual:
  http://bitsavers.trailing-edge.com/pdf/dec/vax/archSpec/EY-3459E-DP_VAX_Architecture_Reference_Manual_1987.pdf
  Chapter 4: Memory Management
  Too much details, but useful for specific information

## Slide 8: Support for Paging the Page Table
Page tables only contain physical addresses
  page of PT in memory contains memory or disk addresses
  page of PT on disk contain only disk addresses
    page in PT cannot be moved to disk before all its pages in memory are moved to disk
Special “untranslated” addressing mode required if page tables are traversed in software
  Sparc: Translation-disabled processor state
  Alpha: Special kseg segment whose addresses are not translated. PT’s mapped to kseg
Protection mode in processor necessary to maintain integrity of translation process
  Don’t let a user process modify the page table, only trusted code

## Slide 9: Memory Segmentation
Alternative to Paging
  Provide location independence and protection of memory regions
Segments have a base and a bound
Can be used to implement virtual memory
Can be used to implement memory protection
Can be combined with paging

## Slide 10: Simple Base and Bound Translation: Location independence + Protection
Load X
Program
Address
Space
Bound
Register
Effective Addr
Register
Base Pointer
Register
+
<
Bound
Violation
Absolute
Address
for X
Main Memory
current
segment
Assumptions?

## Slide 11: Simple Base and Bound Translation: Location independence + Protection
Load X
Program
Address
Space
Bound
Register
Effective Addr
Register
Base Pointer
Register
+
<
Bound
Violation
Absolute
Address
for X
Main Memory
current
segment
Assumptions?
    Contiguous physical address
    Contiguous virtual address
    Same permissions for entire space

## Slide 12: Separate Areas for Program and Data
Load X
Program
Address
Space
Main Memory
data
segment
Data Bound
Register
Effective Addr
Register
Data Base
Register
Program Bound
Register
Program
Counter
Program Base
Register
+
<
Bound
Violation
+
<
Bound
Violation
This permitted sharing of program memory
program
segment

## Slide 13: What about more segments?
Why just program and data?
How about text, heap, and stack?
What about finer-grained protection?
Add segment registers/identifiers to architecture

## Slide 14: Segmentation can Lead to Memory Fragmentation
OS
Space
16 K
24 K
24 K
32 K
24 K
user 1
user 2
user 3
free
free
OS
Space
16 K
24 K
16 K
32 K
24 K
user 1
user 2
user 3
user 5
free
user 4
8 K
OS
Space
16 K
24 K
16 K
40 K
24 K
user 1
free
user 5
free
user 4
User 4 & 5
arrives
User 2 & 3
leaves
As users come and go, the storage is “fragmented”.
Problems? Solutions?
(External Fragmentation)
Notes: May chave a time when I cannot get a large job in because there is no continuous space, though there may be disjoint space.

## Slide 15: Paged Memory Systems
Relaxes the contiguous allocation requirement
0
1
2
3
0
1
2
3
Address Space
of User-1
Page Table
of User-1
processor generated address
offset
page number
Hardware looks up the address of the
base of the page in the page table
small page size Þ large page table
Large page size Þ small page table

## Slide 16: Demand Paging

## Slide 17: Storage Hierarchies
Storage is hierarchical in the order (away from the CPU) of
  increasing latency ti ti < t i+1
  increasing size si & decreasing cost ci si ≤ s i+1, ci ≥ c i+1
  decreasing transfer bandwidth bi bi ≥ b i+1
  increasing natural unit of transfer xi xi ≤ x i+1
Level 0: Registers
Level 1: Caches
Level 2: Main Memory (Primary Storage)
Level 3: Disks (Secondary Storage)
Level 4: Tape Backup (Tertiary Storage)
CPU
Cache
$
Memory
Cache
$
Level 1
(L1 $)
LLC
Disk
…
(access by processor)
(access by OS)

## Slide 18: Hierarchical Storage
Each level memoizes values stored at lower levels of storage to avoid full latency cost when accessing
Effective Access time Ti = hi ti + (1- hi) ti+1
  where hi is the ‘hit’ ratio, the probability of finding the desired data memoized at level i
Given good locality of reference (i.e., small working set), hi » 1 Þ Ti » ti
Balanced system gives the best of both world
  The performance of higher-level storage
  The capacity of lower-level low-cost storage.

## Slide 19: Details: RAM vs. Disk
Disks much cheaper than RAM (consumer prices below)
  Disk currently about $90 2TB
  FLASH currently $90 206GB
  DRAM currently $90 for 16GiB DDR3 1866MHz
  Disk >100X cheaper than DRAM, FLASH right in between
Disks much slower than RAM
  Disks (a fast one)
    4.2ms read seek time, 100MiB/sec sustained rate
  FLASH
    Read time ~10us, 2GiB/sec sustained rate
  Memory DDR2
    50ns – 100ns to read a block of memory
    ~15GiB/s sustained rate
  Disks 4-5 orders of magnitude longer latency, 15-25 times less bandwidth FLASH right in between
Careful with prices though – not always just technology

## Slide 20: Disk As Another Memory Hierarchy Level
Disks huge compared to RAM
  Can we use disks as backing store to RAM?
  Make RAM look as big as disk but as fast as RAM?
    What caches did for RAM
Do it manually or automatically?
Relies on locality
Memory is a Cache for Disk
Important for sharing
  May be more than one program resident on computer at a time
  Aggregate program demands may be more than RAM

## Slide 21: Manual Technique: Overlays for Running Programs Larger than Memory
Programmer manages a part of secondary store by overlaying it repeatedly over primary store
Assuming instruction can address all storage on the drum
  programmer keeps track of addresses in main memory and initiates an I/O transfer when program accesses addresses not in main memory
  automatic initialization of I/O transfers by software address translation
    Brookner’s interpretive coding, 1960
First method too difficult, second too slow!
40k bits
main
640k bits
drum
central
store

## Slide 22: Demand Paging (Atlas 1962)
Secondary
(Drum)
32x6 pages
Primary
32 Pages
512 words/page
Central
Memory
User sees 32 x 6 x 512 words
of storage
“A page from secondary
storage is brought into the
primary storage whenever
it is (implicitly) demanded
by the processor.”
Tom Kilburn
Primary memory as a cache
for secondary memory

## Slide 23: Atlas Demand Paging Scheme
Page address compared against all 32 PAR’s
match, normal access
otherwise, page fault
  instruction interrupted, state saved
  input transfer initiated by consulting page table
    free page always kept
  PAR updated
  if no free page left, page out a page
    selection by usage learning program!
    selected page written to first empty page on drum
  page table updated to point to new location on drum
CPU
Addr Decode
PAR
Mem
Drum

## Slide 24: Demand Paging with Page Tables
Translation determines if page is in memory
On page fault (page not valid), bring page into memory
  OS finds empty page frame in memory (free list)
  OS finds page on disk
  OS reads page into memory
Write backs of modified pages?
  When done?
Free page lists
  FIFO or LIFO? Something else?
1
Process 1
Page Table
1
Process 2
Page Table
1
Process 3
Page Table
OS
pages
Physical Memory

## Slide 25: Replacement Policy
When referenced page is not in primary memory, must be brought in from secondary memory
If no free page frame available, a page needs to be thrown back to secondary memory
  which page should be replaced?
Generally Least Recently Used (LRU) policy used
  replacement policy in software

## Slide 26: Implementing an LRU analog (Not Recently Used)
Field in PTE maintained by software
  1 - not a candidate for replacement
  i.e., recently referenced
  0 - a candidate for replacement
  i.e., not recently referenced
How is table updated when there is a
page fault or a TLB miss?
Algorithm:
Pointer to last examined page maintained
If the examined entry is 1, it is turned to 0 and the
pointer is incremented by 1, otherwise found victim
0
1
1
0
0
1
1
0

## Slide 27: Required Support for Virtual Memory
Page table
  presence bit
    present Þ primary memory address
    missing Þ secondary memory address or “doesn’t exist”
  protection bits: “read only”
  usage bits: accessed?, dirty?
Page fault
  synchronous exception in case of missing page or protection violation
Translation mechanism
Swapping Store and I/O
  separate from file store
Page fault handler
  free page lists for primary and secondary memory

## Slide 28: X86 Virtual Memory
Built up over time, but end result pretty clean
  Some segment baggage, but fairly ignorable
  IBM Power similar, but segments more prominent

## Slide 29: Separate Address Space per Process
1
Process 1
Page Table
1
Process 2
Page Table
1
Process 3
Page Table
OS
pages
Page table - one per process
contains an entry for each user page
Page frame table - one for the whole system
contains bookkeeping info about each page frame
in the physical memory (free?, user name)
Physical Memory

## Slide 30: x86 (IA-32) Translation
32b
32b
32b
8b
Page
Directory
Page Table
Actual frame
VA
10b
10b
12b
CR3
http://www.ibm.com/developerworks/linux/library/l-memmod/
How big is a page?
How big is the page table?
CR3, page directory and
page table all physical addresses

## Slide 31: Paging the Page Table
Page Table of
the page table
pages of the
page table
pages
page in secondary memory
page in primary memory
page does not exist
p1 p2 d
Base of the
Page Table of
the page table
p1
d
p2
effective address
processor
register
Could page out data pages that aren’t being used
  Swapped out process?
  Page table entry has “memory/disk” bit, address in memory/disk
Can page table be swapped out to disk?
  Pointer in page directory needs to point to disk location!
  Page directory has “memory/disk” bit, address in memory/disk

## Slide 32: x86 (IA-32) Translation – Larger Pages?
32b
32b
32b
8b
Page
Directory
Page Table
Actual frame
VA
10b
10b
12b
CR3
Physical address
http://www.ibm.com/developerworks/linux/library/l-memmod/

## Slide 33: x86 (IA-32) Translation – Larger Pages
32b
32b
32b
8b
Page
Directory
Page Table
Actual frame
VA
10b
10b
12b
CR3
Physical address
22b
Huge-Page Table
4MB

## Slide 34: x86-64 (IA32e) Translation – More Flexibility
Announced by AMD in 2000, shipped in April 2003
  Intel followed in March 2004, compatible with AMD64 (called it EMT64 at first), then extended to a degree and called IA-32e
Allows 4KiB, 2MiB, or 1GiB pages
Uses 64-bit addresses
  But only 48 bits of information currently used
  Part of the address space is not used
    (0x00008000 00000000 – 0xffff7fff ffffffff)
  High addresses for OS use
  Low addresses for user processes

## Slide 35: X86-64 Translation
48b
64b
64b
8b
Page
Directory
Pointer
Table
Page Directory
Actual frame
VA
9b
9b
12b
CR3
64b
Page
Map
9b
64b
EA
How big is a page?
64b
9b
Page Table

## Slide 36: X86-64 Translation
48b
64b
64b
8b
Page
Directory
Pointer
Table
Page Directory
Actual frame
VA
9b
9b
12b
CR3
64b
Page
Map
9b
64b
EA
2MiB pages
9b
Page Table
21b

## Slide 37: X86-64 Translation
48b
64b
8b
Page
Directory
Pointer
Table
Actual frame
VA
9b
9b
12b
CR3
64b
Page
Map
9b
64b
EA
1GiB pages
9b
Page Table
30b

## Slide 38: What’s in an x86 PTE?
Physical frame number (how many bits?)
Pointer to start of another translation level or frame (1b)
OS use
  Pseudo-LRU information and other (3b right now)
  Present in physical memory or not (1b)
Protection
  User or supervisor (kernel) (1b)
  Read-only or writeable (1b)
  Execute disable (1b)
SW -> HW information
  Uncacheable (1b)
  Must be write through (1b)
HW -> SW information
  Accessed (1b)
  Dirty (1b)
Reserved bits
  Handful for future extension

## Slide 39: Accelerating Address Translation

## Slide 40: Translation Lookaside Buffers (TLB) Caching the Address Translation
Address translation is very expensive!
  How many memory references to do a single load?
  Instruction and Data memory accesses!
Translation Look-aside Buffers (TLB) remember
the most recent translations
page no. offset
Permit tag phy add
mux
physical page
address
Offset
small associative
memory
New instructions: TLB invalidate, TLB flush

## Slide 41: A TLB Miss
Software (MIPS)
  TLB miss causes an exception
    operating system walks page tables and reloads TLB
Hardware
  Memory management unit (MMU) walks page tables and reloads TLB
    Multi-level page table (SPARC, x86)
    Hashed, inverted page table (PowerPC)
  Page fault handler invoked when page (either data or PT) is missing

## Slide 42: Virtual Memory Flow Chart
Virtual
Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
OS read disk
Update Table
Protection
Check
Physical
Address
miss
hit
succeed
fail
denied
permitted
Protection
Fault

## Slide 43: Optimizations
Copy-on-Write (COW)
  When OS needs to copy a page
    Instead of copying right away, just map it into target address space
    Mark it as Read-Only in both address spaces
    If both address space only read the page, no further action
    If one tries to write, trap into OS, and lazily copy
      Allocate new page
      Copy data
      Map new page to writing process
Demand zeroing
  Want to zero out new pages (for security)
    Mark new page as inaccessible
    When process reads or writes, trap into OS, and lazily zero out page
Writeback of dirty pages
  Lazily write back when page is actually being repurposed

## Slide 44: What did we learn?
Virtual memory gives the illusion of isolated “infinite” memory
  Address translation + protection provides isolation
  Address translation + demand paging enables “infinite” memory
Address translation
  Segments (base + bound)
  Pages are lots of smallish, fixed-size segments
  Page table per process allows linear virtual address translated to physical frame + offset (in hardware)
  OS maintains page table and notifies HW where to find it
    Only page table pointer updated on context switch
  VAX vs. x86
Privileges
  Can’t have regular processes messing with pages tables or segment registers/values
Demand paging