## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 15
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Lab 4 posted
  Will cover Interrupts and Exceptions today to help with the lab

## Slide 3: Last time: Virtual Memory
Virtual memory gives the illusion of isolated “infinite” memory
  Address translation + protection provides isolation
  Address translation + demand paging enables “infinite” memory
Address translation
  Segments (base + bound)
  Pages are lots of smallish, fixed-size segments
  Page table per process allows linear virtual address translated to physical frame + offset (in hardware)
  OS maintains page table and notifies HW where to find it
    Only page table pointer updated on context switch
  VAX vs. x86
Privileges
  Can’t have regular processes messing with pages tables or segment registers/values
Demand paging

## Slide 4: Interrupts

## Slide 5: Definitions
Our definitions
  Interrupt: an event external to the processor that alters the normal flow of instructions
    Disk, network, keyboard
  Exception: an event internal to the processor that alters the normal flow of instructions
    Page fault, arithmetic exception
Note: these definitions are not universally accepted
Notes: 5

## Slide 6: Others’ Definitions
Intel (http://www.intel.com/cd/ids/developer/asmo-na/eng/microprocessors/ia32/xeon/19250.htm?page=2)
  Interrupt: An exception that comes from outside of the processor. There are two kinds of exceptions: local and external. A local exception is generated from a program. External exceptions are usually generated by external I/O devices and received at exception pins.
PowerPC Architecture
  Interrupts “allow the processor to change state as a result of external signals, errors, or unusual conditions arising in the execution of instructions”
PowerPC 604
  Everything is an exception
68K
  Everything is an exception
VAX
  Interrupts: device, software, urgent
  Exceptions: faults, traps, aborts
Notes: 6

## Slide 7: Terms
Synchronous vs. Asynchronous
  Synchronous: event happens in same place in instruction stream every time (assuming same data)
    Basically synonymous with exceptions
  Asynchronous: event can happen at any point
    Basically synonymous with interrupts
Maskable vs. Unmaskable
  Interrupts/exceptions can be individually masked
    E.g., misaligned access causes an exception or not?
User requested
  Users can call TRAP instructions that are handled by the exception handling mechanisms
Notes: 7

## Slide 8: Why?
Don’t want to waste time waiting for rare events
  There are a lot of things to do
    Special hardware to do those things?
      Expensive, infrequent -> antithesis of “optimize the common case”
    Software?
      Cost-effective, how to do it?
Can switch program being run
  When to switch?
  How to switch?
Notes: 8

## Slide 9: When Do You Call the Handler? Where Do You Restart?
Interrupts
  Instruction is allowed to complete before interrupt handler executed (why?)
  Interrupt handler returns to the following instruction
Exceptions
  Instruction causing exception cannot complete without help
    Must call handler before instruction completes
  Exception handler returns to the instruction that caused the exception
Notes: 9

## Slide 10: Interrupts in a Processor
Processor
Chipset
PCI
keyboard
disk
network
Notes: 10

## Slide 11: What Happens After An Interrupt/Exception Occurs?
Call handler
What if there are multiple interrupts/exceptions?
How many handlers?
  Can you have just one?
  What does it need to do?
    Poll state to determine which interrupt/exception occurred
    Poll in priority order
  How can you determine which handler to go to more efficiently?
    Vector to appropriate handler as specified by the specific interrupt/exception
Notes: 11

## Slide 12: Vectoring To Interrupt/Exception Handlers
Temporarily disable new interrupts
Enter supervisor mode at jump to handler
  Needed to fix problems
  But, priority for exception handling generally inherited from the original program
Interrupt/Exception saves PC of interrupted stream into special register
  Other appropriate state may be saved
Constructs index into interrupt/exception vector
  Uses interrupt/exception number as index
Jumps to that location in the interrupt/exception vector
  Often another jump right afterwards to the interrupt/exception handling code
  Re-enable new interrupts
Notes: 12

## Slide 13: Handlers
DSI/ISI (Data/Instruction Storage Interrupt) handler
  Page fault handler
    Allocate page frame, read data from disk (if necessary), swap page back, update page table
External Interrupt
  Poll all possible causes
    Keyboard, disk, network
  Copy into appropriate memory/buffer
Decrementer (timer)
  Switch to new process
  Do LRU bit flipping for page reclamation
  Etc.
Program
  TRAPs: debugger may replace instructions with TRAPs
    Use saved PC to figure out where you are
    How do you resume?
Notes: 13

## Slide 14: Nested Exceptions
One interrupt/exception occurs when another is already active
Priority maintained
Can fundamentally do it
  Subroutine calls within subroutine calls
  Handlers need to save appropriate state
Notes: 14

## Slide 15: Interrupts vs. Exceptions Summary
Interrupts |  | Exceptions
External | CAUSE | Internal to running program (process)
Usually, when convenient | WHEN HANDLED | Usually, when detected
Depends on event | PRIORITY | Same as running process
System | CONTEXT | Process
Usually | MASKABLE | Usually not

## Slide 16: CACHES

## Slide 17: Memory, Cache, Processor
17
Living Room
Notes: 17

## Slide 18: An Early Word on Memory Hierarchy
“4.1. Ideally one would desire an indefinitely large memory capacity … We are therefore forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less quickly accessible.”
Burks, Goldstine, and von Neumann, "Preliminary discussion of the logical design of an electronic computing instrument," 1946
.

## Slide 19: Cray-1 Solution: Register File Hierarchy
Only 8 vector, 8 scalar, 8 address registers
  Electrical/address space considerations
Working set is often larger for scalar/address
  vector operations could be “chained”
    pipelined: while later part of vector read, beginning can be operated on
Have additional explicitly-addressed RAMs further away than registers
19
Notes: 19

## Slide 20: Cray-1: More Registers
20
Single-
Ported
Memory
(320 MW/
sec)
64 (78?)
T-Registers
64 (78?)
B-Registers
S registers
A registers
Scalar
FU’s
Address
FU’s
Provide operations to explicitly move
data between S/T and A/B registers
Notes: 20

## Slide 21: DSPs and Stream Processors: Explicit Memory Hierarchy
DSPs: Scratchpad memory
GPUs: “Shared memory”
Sony Cell Broadband Engine (PS3): Local store
Stream Processors: Stream register file (SRF)
DRAM
Local
SRAM
Registers
ALUs
DRAM and local SRAM use different addresses (and/or instructions)
under explicit SW control. Often hard/impossible to get right

## Slide 22: Want Automatic Management
Backing registers or scratchpad nice, but
  explicit management is painful
  often cannot tell statically what will be reused
  register files got larger
    backing registers needed to get correspondingly larger
  code portability suffers too
Caches
  Cray never believed in them (“Caches are for wimps!”)
22
Notes: 22

## Slide 23: Caches: Automatic Management of Fast Storage
Assumptions:
  Memory access (~100ns) >> cache access (~1ns)
    Cache is smaller, faster, and more expensive than memory
  Programs exhibit temporal locality
    If an item is referenced, it will tend to be referenced again soon
Can you do this between memory and disk???
Memory hierarchy gets deep
  Today, 3 levels of on-chip caches are common
  Also between memory and disk/SSD
23
CPU
Cache
$
Memory
Notes: 23

## Slide 24: How Things Have Progressed
1995 low-mid range Hennessy & Patterson, Computer Arch., 1996 | 200B 5ns | 64KB 10ns | 32MB 100ns | 2GB 5ms
2009 low-mid range www.dell.com, $449 including 17” LCD flat panel | ~200B 0.33ns | 8MB 0.33ns | 4GB <100ns | 750GB 4ms
2015 mid range | ~200B 0.33ns | 8MB 0.33ns | 16GB <100ns | 256GB 20-100us
CPU
Cache
$
Memory
Disk/SSD
Notes: 24

## Slide 25: Basic Cache Issues
Naming
  What do you call things?
Placement
  Where in the cache is data placed?
  Or, how can I find my data?
Replacement
  Given more than one place to place, where is data placed?
  Or, what to kick out?
Write Operations
  When should memory be updated?

## Slide 26: Examples
What do you call things (Naming)
  Computers use addresses
  Grocery store based on categories
    Alphabetize?
Where do you put something (placement)?
  Lots of space: “Everything has its place”
    Grocery store
  “Not everything has its place”
    Counter space
    Where do you put things?
      Place anywhere? Ok, if small kitchen
      Place in specific locations (larger kitchen)
        Easier to find, can run out of space faster
What do you do when you run out of space (replacement)?
  What do you move?
  Where do you put what you move?
Meat
Starch
Veg

## Slide 27: How much does a cache help?
Model!
Program with n loads
SpeedupB-over-A = TA / TB
TA = 100 * n
TB = (HR * 1 + (1 – HR) * (100 + 1) ) * n
  HR (Hit Rate) = (# of accesses found in cache) / (total # of accesses)
  Miss Rate = 1 - HR
CPU
Mem
100 cycles
CPU
Mem
1 cyc
$
100 cycles
A:
B:
HR | T_A | T_B | Speedup
1 | 100 | 1 | 100.00
0.99 | 100 | 2 | 50.00
0.9 | 100 | 11 | 9.09
0.5 | 100 | 51 | 1.96
0.1 | 100 | 91 | 1.10
0.01 | 100 | 100 | 1.00
0 | 100 | 101 | 0.99

## Slide 28: Basic Cache Issues
Naming
  What do you call things?
Placement
  Where in the cache is data placed?
  Or, how can I find my data?
Replacement
  Given more than one place to place, where is data placed?
  Or, what to kick out?
Write Operations
  When should memory be updated?

## Slide 29: Baseline Cache & Memory
4 cache locations
  Data + address tag
  Also called cache-line
16 memory locations
For now, assume cache location size == memory location size
Cache is smaller than memory (obviously)
  Thus, not all memory locations can be cached at the same time
Assume each memory location can only reside in one cache-line
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
00
01
10
11

## Slide 30: Cache Placement, Part 1
Use memory address as a name
Apply a function to the name to generate a cache address to access
What are reasonable functions?
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
cache
func
00
01
10
11

## Slide 31: Function to Address Cache
Cache expensive; use it efficiently
  For “normal” access patterns use as much of the cache as possible
Simplest function is a subset of address bits
  CA = ADDR[3],ADDR[2]
  CA = ADDR[3],ADDR[1]
  CA = ADDR[3],ADDR[0]
  CA = ADDR[2],ADDR[1]
  CA = ADDR[2],ADDR[0]
  CA = ADDR[1],ADDR[0]
Any other functions?
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
cache
func
00
01
10
11

## Slide 32: Direct-Mapped Cache
Address cache with lowest order address bits
Very simple
  Only one place to look

## Slide 33: Example: Direct-Mapped Cache
For (i = 0; i < 4; ++i) {
  A += mem[i];
}
For (i = 0; i < 4; ++i) {
  B *= (mem[i] + A);
}
Assume mem == 0b1000
ldb Ra, 0b1000
ldb Rt, 0b1001; add Ra , Ra , Rt
ldb Rt, 0b1010; add Ra , Ra , Rt
ldb Rt, 0b1011; add Ra , Ra , Rt
ldb Rb, 0b1000; cache hit?
a
a
b
c
d
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
Addr[1:0]
00
01
10
11
=
Hit?
a
c
b
d
1000
1010
1001
1011

## Slide 34: Do We Need All Those Address Tag Bits?
a
a
b
c
d
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
Addr[1:0]
00
01
10
11
a
c
b
d
1000
1010
1001
1011
=
Hit?
[3:2]

## Slide 35: Do We Need All Those Address Tag Bits?
a
a
b
c
d
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
Addr[1:0]
00
01
10
11
a
c
b
d
1000
1010
1001
1011
=
Hit?
10
10
10
10
[3:2]

## Slide 36: Reminder: Abstract View of Memory
Address
n
CE
WE
k
Content

## Slide 37: One Possible Direct-Mapped Cache Implementation
Cache state is RAM!
Implement cache as a single SRAM
Need appropriate comparators
Memory is implemented as a DRAM
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
a
00
01
10
11

## Slide 38: One Possible Direct-Mapped Cache Implementation
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
a
00
01
10
11
Cache
SRAM
2
addr_tag + valid + data
Mem
(DRAM)
4
data
Cache state is RAM!
Implement cache as a single SRAM
Need appropriate comparators
Memory is implemented as a DRAM

## Slide 39: Conflicts
What if our access pattern is mostly contiguous but not completely?
For (I = 0; I < 3; ++I) {
  A += mem[i];
}
A += mem[5];
Assume mem == 0b1000
ldw Ra, 0b1000
ldw Rt, 0b1001; add Ra , Ra , Rt
ldw Rt, 0b1010; add Ra , Ra , Rt
ldw Rt, 0b1101; add Ra , Ra , Rt
…….
ldw Rb, 0b1001; cache hit?
a
a
b
c
d
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
Addr[1:0]
00
01
10
11
b
10
a
c
b
d
10
10
10
11

## Slide 40: Sets
Each cacheable memory location is mapped to a set of cache locations
A set is one or more cache locations
Generally (but not always) set size is a power of 2
Total number of cache-lines is divisible by number of sets
  Otherwise, waste some cache-lines
Thus, for this example, expect set sizes of 1, 2, 4
Direct mapped is set size == 1!
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
00
01
10
11

## Slide 41: Sets
Each cacheable memory location is mapped to a set of cache locations
A set is one or more cache locations
Generally (but not always) set size is a power of 2
Total number of cache-lines is divisible by number of sets
  Otherwise, waste some cache-lines
Thus, for this example, expect set sizes of 1, 2, 4
Direct mapped is set size == 1!
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
00
01
10
11

## Slide 42: 2-Way Set-Associative
Each set is 2 entries big
Which addr bits select set?
Either entry can store any cache-line that maps to that set
For (I = 0; I < 3; ++I) {
  A += mem[i];
}
A += mem[5];
Assume mem == 0b1000
ldw Ra, 0b1000
ldw Rt, 0b1001; add Ra , Ra , Rt
ldw Rt, 0b1010; add Ra , Ra , Rt
ldw Rt, 0b1101; add Ra , Ra , Rt
ldw Rb, 0b1001; cache hit?
Set 1
Set 0
0
1
1000
1001
1010
1101

## Slide 43: Can Same Structure Implement a 2-Way Set-Associative Cache?
a
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
a
00
01
10
11
Cache
SRAM
2
addr_tag + valid + data
Mem
(DRAM)
4
data
Finding the right tag?

## Slide 44: One Possible 2-Way Set-Associative Cache Implementation
Cache is simply RAM
Implement 2-way set-associative cache as a two SRAMs
Similar to Banked Memory
  But use same address for both
  Double bandwidth
Cache
0
1
Cache
SRAM
addr_tag + v + data
0
1
Cache
SRAM
addr_tag + v + data

## Slide 45: 4-Way Set-Associative (Fully Associative for a 4-entry cache)
Each Set 4 entries big
Every entry can store any cache-line that maps to that set
ldw Ra, 0b0000
ldw Rt, 0b0100
ldw Rt, 0b1000
ldw Rt, 0b1100
ldw Rb, 0b1000; cache hit?
Tags?
0
0000
1000
0100
1100

## Slide 46: Set-Associative vs. Direct Mapped
What are the tradeoffs?
Set-Associative Pros
  Generally higher hit rate
  Better utilization of cache resources
Direct-Mapped Pros
  Simpler
  Faster

## Slide 47: Locality again
So far: temporal locality
What about spatial?

## Slide 48: Example: Block Size (Cache-Line Size) of 2 (Direct Mapped Cache)
ldb Ra, 1000
ldb Rb, 1001
ldb Rc, 1010
ldb Rd, 1011
a
a
b
c
d
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Memory
Cache
addr
Addr[2:1]
00
01
10
11
a:b
c:d
=
Hit?
[3]
What is total cache size?
Which addr bits used?

## Slide 49: Cache Naming and Placement
Cache namespace is the same as the memory namespace
Cache placement will be as below for:
  b bits in a memory address
  2n-way set-associative cache
  S sets (s = log2S)
  L bytes of data in a cache line (l = log2L)
  Cache size?
tag
index
offset
0
l
l+s
b-1

## Slide 50: Terms: Types of Misses
Compulsory
  First access
Conflict
  Cache is not associative enough
Capacity
  Cache is not big enough, forced to make room
50
Notes: 50

## Slide 51: What To Do On Miss?
Put into cache or not?
  Any reason not to put into cache?
Difference between loads and stores?
51
Notes: 51

## Slide 52: Replacement Policy
Which block should be replaced?
  Direct mapped?
  Associative caches?
Replacement Policy
  least-recently-used (LRU)
    difficult to implement perfect LRU
  Random
  FIFO (uncommon)
  LIFO (uncommon)
52
Notes: 52