## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 17
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Last time
Grad Lab
  We will look into LRC resources
  Perhaps get started with Virtual Machines in the meantime?
Caches
  Set-associative caches

## Slide 3: Terms: Types of Misses
Compulsory
  First access
Conflict
  Cache is not associative enough
Capacity
  Cache is not big enough, forced to make room
How to determine miss type:
  Compulsory
    no choice (first time seen or coherence invalidation)
  Capacity
    Simulate fully-associate cache with capacity, line size, and alloc/replacement policy; is miss – capacity miss
  Conflict
    Simulate given cache, if miss but not capacity miss, then conflict
3
Notes: 3

## Slide 4: What To Do On Miss?
Put into cache or not?
  Any reason not to put into cache?
Difference between loads and stores?
4
Notes: 4

## Slide 5: Replacement Policy
Which block should be replaced?
  Direct mapped?
  Associative caches?
Replacement Policy
  Least Recently Used (LRU)
    difficult to implement perfect LRU
    Need log2(n!) bits to represent state for n-way set-associative structure
  Least Frequently Used (LFU)
  Random
  FIFO (uncommon)
  LIFO (uncommon)
  Optimal?
    Belady’s algorithm: Replace most distant reuse in the future
      [IBM Journal, 1966]
5
Notes: 5

## Slide 6: One Implementation of Hardware LRU
6
0 1 2 3
3 0 0 0 0
2 0 0 0 0
1 0 0 0 0
0 0 1 1 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 6

## Slide 7: One Implementation of Hardware LRU
7
0 1 2 3
3 0 0 0 0
2 0 0 0 0
1 1 0 1 1
0 0 0 1 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 7

## Slide 8: One Implementation of Hardware LRU
8
0 1 2 3
3 0 0 0 0
2 1 1 0 1
1 1 0 0 1
0 0 0 0 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 8

## Slide 9: One Implementation of Hardware LRU
9
0 1 2 3
3 1 1 1 0
2 1 1 0 0
1 1 0 0 0
0 0 0 0 0
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 9

## Slide 10: One Implementation of Hardware LRU
10
0 1 2 3
3 0 1 1 0
2 0 1 0 0
1 0 0 0 0
0 0 1 1 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 10

## Slide 11: One Implementation of Hardware LRU
11
0 1 2 3
3 0 1 0 0
2 1 1 0 1
1 0 0 0 0
0 0 1 0 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Notes: 11

## Slide 12: One Implementation of Hardware LRU
12
0 1 2 3
3 0 1 0 0
2 1 1 0 1
1 0 0 0 0
0 0 1 0 1
j
k
4-way set
when the i’th block is referenced
row i is set to 1
column i is set to 0
the row containing all 0’s is the LRU block
example: b0, b1, b2, b3, b0, b2
Row with lowest binary value is LRU!
Notes: 12

## Slide 13: Pseudo-LRU
Achieve close to LRU performance with far simpler policy and fewer state to track
Tree-based Pseudo-LRU
  (n-1) bits organized as tree for n-ways
  Bits point to path to victim (left or right)
  Upon cache access, ensure bits along path are pointing “the other way”
Not Recently Used (NRU)
  1 bit per cache line
  Set bit to 0 on cache hit
  Set all bits to 1 when all bits are 0
  Replace line with 1

## Slide 14: Tree-based Pseudo-LRU Example (4-way)
0
0
0
1
1
0
A
0
1
1
A
B
1
0
1
A
C
B
0
0
0
A
C
B
D
1
1
0
E
C
B
D

## Slide 15: General Rule: Bigger == Slower
How big should the cache be?
  Too small and too much memory traffic
  Too large and cache slows down execution (high latency)
Make multiple levels of cache
  Small L1 backed up by larger L2
  Today’s processors typically have 3 cache levels
15
CPU
Cache
$
Memory
Cache
$
Level 1
(L1 $)
Level 2 (L2 $)
Notes: 15

## Slide 16: How much does a cache hierarchy help?
n load instructions
Total time T: Add up fraction of instructions at particular level multiplied by access latency at that level
T = ( h1*1 + (1-h1)*h2*(1+10) + (1-h1)*(1-h2)*(1+10+100) ) * n
  h1: hit rate at L1$
  h2: hit rate at L2$
CPU
Cache
$
Memory
100 cycles
Cache
$
L1 $
1 cycle
L2 $
10 cycle

## Slide 17: Inclusive Caches vs. Exclusive Caches
Inclusive Caches
  Every block in a level also exists in the next level
  When fetching a block, place it in all cache levels
  (-) Duplication of data in hierarchy
  (-) more effort to maintain inclusion
  (+) cache coherence in multiprocessors easier
    Only track in last-level cache
Exclusive Caches
  Blocks contained in cache levels are mutually exclusive
  (+) More efficient utilization of cache space
  (+) More flexibility in replacement / placement
  (-) More blocks/levels to keep trace of for cache coherence
Non-Inclusive Non-Exclusive cache
  No guarantees for inclusion or exclusion

## Slide 18: Virtual or Physical Addresses for Caches?
TLB look up takes time
  For both instructions and data addresses
CPU
Virtual
Cache
Memory
TLB
VA
VA
PA
CPU
Physical
Cache
Memory
TLB
VA
PA
PA

## Slide 19: Issues with Virtual Caches
Synonym: a word that means the same as another word
  Virtual cache can have two copies of same physical data
Homonym: words with same spelling but different meaning
  One virtual page maps to two physical page
  Solutions: Add ASID with tag, use physical tags, flush on context switch
VA1
VA2
PA
VA
PA1
PA2

## Slide 20: Virtually-Indexed Physically Tagged (VIPT) Caches
Best of both worlds!
Tag
Index
Offset
VPN
Page Offset
TLB
Cache
PFN
(phys) Tag
=
Data
VA

## Slide 21: VIPT Cache
Can concurrently look up TLB and cache using VA bits
  Compare tag (physical) against TLB output later
Cache Index bits need to fit in Page Offset
  Page offset same in VA and PA!
  Constraints on cache configuration
    Cache size <= Page size * Associativity
  If Cache size larger than (page size * assoc), can cause synonyms
  Solutions?
    Ensure mapping of overlapping bits are the same in S/W (early SPARC)

## Slide 22: Virtual or Physical Caches
VIVT: Fastest, but can have synonyms and homonyms
VIPT: Fast, no homonyms
  Mostly used in L1 caches
PIVT: ?
PIPT: Slower, but no synonyms or homonyms
  Used in lower level caches

## Slide 23: Other cache optimizations
Latency
  Anything other than levels?
Hit rate
  Reduce misses
Conflict misses
  Associativity tradeoffs
  Victim cache
Compulsory misses
  Cache line size
  Prefetch
Capacity misses
  Replacement policies

## Slide 24: Critical Word First
Memory bus is generally one or two words wide
  Pentium 4 is 64b wide, 32b words
Cache-line fills require multiple words over bus
A simple cache-fill would always start on word 0
If you have an 8 word cache-line, and you miss on the 5th word, with a 1 word bus, you need to wait for the 5th word
  Why not start on the 5th word?
Design logic to do so

## Slide 25: Caches can be specialized for data and instructions
Memory is read for every instruction
  Lots of spatial locality
    instructions tend to follow one another
  Lots of temporal locality
    Programs have loops
    Programs are often not that big
Can have a special cache just for instructions
  Reduce conflicts with data
  Perhaps longer cache lines
  Can have very high hit rate if data doesn’t evict instructions
All processors today (almost) have separate ICache and DCache

## Slide 26: Prefetching
Issue loads that will miss early (before demand)
Done by
  User (prefetch instructions)
  Compiler (prefetch instructions)
  Hardware (look for patterns)
Huge amount of research
  Still on-going
  Will cover some examples in later lectures (if time permits)

## Slide 27: Victim Caches
Associative caches expensive
Sometimes associativity necessary to get reasonable hit rate
  Some memory access patterns need associativity
  But perhaps on a small number
Combine a large direct-mapped cache with a small fully-associative cache
  Fill fully-associative with conflicts from direct-mapped cache
[Jouppi, ISCA 1990]

## Slide 28: Placement/replacement optimizations
Dead block prediction
LRU-stack location
Blend LRU and LFU
Inter-reference intervals
…

## Slide 29: Re-Reference Interval Prediction (RRIP)
[Jaleel+, ISCA 2010]

## Slide 30: Re-Reference Interval Prediction (RRIP)
[Jaleel+, ISCA 2010]

## Slide 31: Re-Reference Interval Prediction (RRIP)
Insert into “long” re-reference interval and promote on hit
[Jaleel+, ISCA 2010]

## Slide 32: Re-Reference Interval Prediction (RRIP)
[Jaleel+, ISCA 2010]

## Slide 33: Cut down on tag lookup?
Predict where the data is
E.g., way prediction
  [Powell+, MICRO 2001]
  Predict way; only 1 tag comparison performed that cycle
  If miss:
    Check other ways in set
    Go to next level if not found

## Slide 34: Cache Control Instructions
Enable control over placement and replacement
PowerPC example:
  dcbt: data cache block touch
  dcbtst: data cache block touch for store
  dcbz: data cache block zero
  dcbst: data cache block store
    Stores dirty data back to memory
  dcbf: data cache block flush

## Slide 35: Does SW care about cache (is it microarch)?
Recall: If architectural state changes are unaffected  uarch
So, despite cache control instructions and prefetch a cache (for now) is uarch
  We’ll revisit when we talk about parallelism

## Slide 36: What did we learn? Caches: Automatic Management of Fast Storage
Assumptions:
  memory access (~100ns) >> cache access (~1ns)
    Cache is smaller, faster, more expensive than memory
  Programs exhibit temporal locality
    If an item is referenced, it will tend to be referenced again soon
  Programs exhibit spatial locality
    If an item is referenced, the next item in memory is likely to be accessed soon
36
CPU
Cache
$
Memory
Notes: 36