## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 18
Prof. Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Still working out Grad Lab on LRC
  misc/scratch space?
  Haven’t tested out dependencies yet
  Has anyone tried it out yet?

## Slide 3: Victim / Next-Victim Replacement Policy
Mark each cache line in set as either (need 2-bits per line):
  Victim (V)
  Next-Victim (NV)
  Other (O)
On cache miss:
  Replace line marked as Victim
  Line marked as NV is now Victim
  Randomly select NV from Os
On cache hit:
  If line was V, line becomes O. NV->V, randomly select NV from Os
  If line was NV, line becomes O. Randomly select NV from Os
  If line was O, no action

## Slide 4: Recap: Issues with Virtual Caches
Synonym: a word that means the same as another word
  Virtual cache can have two copies of same physical data
Homonym: words with same spelling but different meaning
  One virtual page maps to two physical page
  Solutions: Add ASID with tag, use physical tags, flush on context switch
VA1
VA2
PA
VA
PA1
PA2

## Slide 5: Recap: Virtually-Indexed Physically Tagged (VIPT) Caches
Best of both worlds! (Physical and Virtual caches)
Tag
Index
Offset
VPN
Page Offset
TLB
Cache
PFN
(phys) Tag
=
Data
VA

## Slide 6: Example
L1-D cache design
  64KB 4-way set-associative
  64B cache block
  Address breakdown?
Virtual address
  32-bit address space
  4KB page size
  VIPT design?

## Slide 7: Processor
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control

## Slide 8: System
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control

## Slide 9: System
Regs
cache
MAR
MDR
S
shift
A
B
ALU
Control
DRAM
MAR
MDR

## Slide 10: A Simple Bus
Device 1
Device 2
Device 3
Priority
Arb Unit
Notes: 10

## Slide 11: What Is A Bus?
Shared data transport
  Point-to-point connections traditionally not a bus
Requires
  Data
  Address/control
Traditionally parallel (multiple wires) but lately some have become serial
  USB: Universal Serial Bus
  SATA
  …
Notes: 11

## Slide 12: Why Serial (vs. Parallel)?
Serial links transmit less data per clock cycle than parallel links
But, serial links can be clocked faster than parallel links
  Ultimately achieve higher data rate!
Why?
  Clock skew between channels not an issue
  Connection requires less space (less wires) allowing extra space for better isolation of link from its surrounding
  Crosstalk is less of an issue
  Also, cheaper to implement (fewer pins)

## Slide 13: A few important issues
Using the shared bus safely
Designing the bus
Interrupts
Memory mapped I/O and caches?
Multiple users?

## Slide 14: Bus Characteristics
Arbitration: who gets bus
  Central
  Distributed
Transfer of data on bus
  Asynchronous: notify when you are done
  Synchronous: every transfer takes the same amount of time
Bus tenure
  Pending
  Split transaction
Notes: 14

## Slide 15: Centrally Arbitrated
Device 1
Device 2
Device 3
Priority
Arb Unit
Policies for determining scheduling
Bus Request / Bus Grant
Notes: 15

## Slide 16: Central Arbitration Example
Notes: 16

## Slide 17: Central Arbitration
Each device has separate line
Requires central arbiter
  May become bottleneck
As system scales larger (more nodes):
  Latency increases
    Info collection time
    Decision time
    Transmit time (of decision)
  Throughput decreases
    Throughput depends on bandwidth and utilization of bus
    Arbiter response time can have impact on bus utilization

## Slide 18: Daisy-Chain Arbitration
Simple
Not fair
Slow
Bus
Arbiter
Device 1
Device 2
Device n
Grant
Release
Request
Grant
Grant
Lowest priority
Highest priority

## Slide 19: Distributed Arbitration
Each device decides on its own whether its allowed to use the resource
  May have information from other devices
Potential problems?
Examples
  Dinner table
  Ethernet
Notes: 19

## Slide 20: Distributed Arbitration
Each device decides on its own whether its allowed to use the resource
  May have information from other devices
Potential problems?
  Collisions
    Must have some way to detect and resolve collisions
      collision detection
Examples
  Dinner table
  Ethernet
    Carrier Sense Multiple Access / Collision Detection (CSMA/CD)
Notes: 20

## Slide 21: Asynchronous
Handshaking protocol
  Identify start and end of each phase of the bus protocol
Not tied to a clock
  Can assert requests and grants at any time
Benefits?
  Hint: some new memory controllers for PCs are asynchronous
Notes: 21
.

## Slide 22: The Handshake Protocol
Processor reading memory
Processor asserts ReadReq signal and sends the address over the shared bus:
1. Mem sees the Readreq, reads the address and sets Ack.
2. Processor sees the Ack line is set and releases the ReadReq and data lines.
3. Mem sees that ReadReq is low and drops Ack to acknowledge that.
4. Mem places the data on the data lines and raises DataRdy.
5. Processor sees DataRdy, reads the data from the bus and raises Ack.
6. Mem sees the Ack signal, drops DataRdy and releases the data lines.
7. Processor sees DataRdy go low, drops Ack which indicates that transmission is over.
What is missing?
Proc
Mem
Notes: 22

## Slide 23: Synchronous Bus
All transfers take the same amount of time
  If less time required, waste the time
Bus cycle fixed
Tend to be short buses (minimize clock time)
Tend to be similar speed devices
Notes: 23

## Slide 24: Synchronous Bus
Cycle 1 after address grant submit address
Cycle 3 after address grant, return data
Issues?
Notes: 24

## Slide 25: Synchronous vs. Asynchronous
Synchronous communication is implicit
  Know when something is supposed to be there
Asynchronous is explicit
  Everything signaled
Synchronous reduces handshaking
  But there is more handshaking than you might expect in a real system
    Bus request, bus grant, data asserted, data received
Asynchronous runs as fast as part can run
  But still need to get back into synchronous domain
Notes: 25

## Slide 26: Bus Tenure: Pending
Hold onto resource until you’re done
Wasteful, but simple
Notes: 26

## Slide 27: Bus Tenure: Split Transaction
Allow other transfers to go when you’re not ready
Applicable to all buses (address and data)
Can be out-of-order or in-order
  What support is needed for out-of-order bus transactions?
Notes: 27

## Slide 28: Single-Bus Computer
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Disk
Notes: 28

## Slide 29: DMA
Block copy without with minimal processor assist
Processor issues DMA command
  Start source address
  Start destination address
  length
DMA Engine performs move transparently
  Completion notification
    None
    Poll
    Interrupt
Can it be done in a single-bus computer?
Notes: 29

## Slide 30: Bus Organization in Modern Computers
CPU
Memory
Controller
Memory
PCI
Really multiple independent buses:
DMA is easy
Increased parallelism
Really multiple independent buses in memory as well: channels
Notes: 30

## Slide 31: From buses to networks
Buses are great, but:
  Signal integrity difficult with many “bus drops”
  Lowers speed
Point-to-point connections offer highest speed, but:
  Too many end-points for everything to connect to everything
Interconnection networks
  Take multiple hops to get from place to place (node to node)
  See next slide
Can combine buses and various networks in a hierarchy

## Slide 32: Interconnection network topologies
Network topology = how nodes are connected to one another
Topology considerations:
  Diameter (maximum hops between any two nodes)
  Bi-section bandwidth (minimum BW between any two “halves”)
  “Embedding” / packaging
  Cost of links (some more expensive than others)
  Routability
Uni- and bi-directional rings
2D mesh
2D torus
“Folded” Clos a.k.a. fat tree
Direct
Indirect

## Slide 33: Network Topologies Comparison
Topology | Aggregate BW | Bisection BW | Latency | Cost | Best at
Ideal | O(N) | O(N) | O(1) | O(N) | ALL
Bus | O(1) | O(1) | O(1) | O(N) | Latency, Cost
Fully Connected | O(N) | O(N) | O(1) | O(N^2) | BW, Latency
Ring | O(N) | O(1) | O(N) | O(N) | BW, Cost
Mesh | O(N) | O(sqrt(N)) | O(sqrt(N)) | O(N) | BW, Cost
Hypercube | O(N) | O(N) | O(logN) | O(NlogN) | BW
Trade-off of Bandwidth, Latency, and Cost: Pick two
Hypercube:
Notes: Aggregate BW: how many hosts can simultaneously send messages
Bisection BW: how many links have to break before the network is cut in two halves. If the network is segmented into two equal parts, the BW between the two parts. Worst-case segmentation.
Latency: number of hops required from source to destination
Cost: required number of switches or network interfaces
Tree: Bisection bandwidth O(1) before fat tree. O(n) with fat tree? Latency O(logN)
Butterfly: Latency: O(k) bandwidth: O(2^k)

## Slide 34: Multi-state Logarithmic Network Example: Omega Network
Each block is 2x2 switch (crossbar)
  Can be generalized (K x K)
Switch settings can be determined solely be destination
Latency: O(logN), Cost: O(NlogN)
0
1
E.g., route from 101 to 010

## Slide 35: Interrupts

## Slide 36: Interrupts vs. Exceptions Summary
Interrupts |  | Exceptions
External | CAUSE | Internal to running program (process)
Usually, when convenient | WHEN HANDLED | Usually, when detected
Depends on event | PRIORITY | Same as running process
System | ASSOCIATED WITH | Process
Usually | MASKABLE | Usually not

## Slide 37: What about peripherals and caches?
Cache coherence protocol
Three state MSI Protocol
  Modified, Shared, Invalid
Modified must be written back on replacement
Shared can be overwritten without writeback
Invalid if entry is not valid or if data not in cache

## Slide 38: Basic Coherence
I/O write to memory, invalidates shared cache copy
Cache must “snoop” memory bus to see memory accesses
What if cache copy is in modified state???
d
c
a
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
a
CPU
a
c
I
I
I
I
S
d
e

## Slide 39: MSI Protocol (writeback cache)
M
S
I

## Slide 40: MSI Protocol (writeback cache)
M
S
I
I/O read \ WB
Store
I/O read/write
Store/Load
I/O write \ WB
I/O read, load
Store
Load
I/O write