## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 20
Dam Sunwoo
University of Texas at Austin
Arm Research
(Many slides borrowed from
Prof. Onur Mutlu (ETH Zurich) with permission)

## Slide 2: Announcements
Review on Wednesday?

## Slide 3: Vector with Chaining Performance, 1 Memory Port
182 cycles
VLN = 50 ; 1
VST = 1 ; 1
V0 = A[0..VLN-1] ; 11 + VLN - 1
V1 = B[0..VLN-1] ; 11 + VLN - 1
V2 = V0 + V1 ; 4 + VLN - 1
V3 = V2 >> 1 ; 1 + VLN - 1
C[VST...VST+VLN-1] = V3 ; 11 + VLN – 1
V0 (Load)
V1 (Load)
V2 (Add)
V3 (Shift)
C (Store)
Q about overlapping 11-cycles of V1 Load?

## Slide 4: Assumptions for Cray-1
Cray-1 used SRAM for main memory (~8MB)
Each memory bank has single port
Example with Chaining with 2 load ports and 1 store port
  Assumed 2 load ports and 1 store port in each bank

## Slide 5: Recap: Banking in Cray-1
Bank
0
Bank
1
MDR
MAR
Bank
2
Bank
15
MDR
MAR
MDR
MAR
MDR
MAR
Data bus
Address bus
CPU

## Slide 6: Memory Initiation Rate
Memory speed must keep up with CPU speed!
  Interleave memory banks
To maintain initiation rate of 1, the number of banks must be at least the ratio of memory to processor cycle time.
  However, if processor make access in non-unit stride, it is possible to have bank conflicts.
  # banks >= mem_latency / cycle_time
  Cray: 50ns / 12.5ns = 4
  Why 16 banks?

## Slide 7: Memory Initiation Rate
In general, effective bandwidth (relative to 1 bank) is
  Number of banks / GCD(stride, number of banks)
  Example: stride = 1, number of banks = 16, 16/1 = 16
  Stride = 16, number of banks = 16, EB = 16/16 = 1
  Stride = 8, number of banks = 16, 16/8 = 2
  Stride = 3, number of banks = 16, 16/1 = 16
A performance-minded programmer will rearrange data to avoid bad strides (by padding etc)
Alternatively, prime number of banks is an hardware solution.
  Only have most serious problem when accessing at stride exactly equal to the number of banks
  Difficult to implement though.
    Must do real divisions instead of shifts

## Slide 8: Interleaving
When using multiple banks the address space needs to be partitioned between the banks
  Good way of doing it is to interleave banks across the address range
Which address bits should you use to interleave?
Why?

## Slide 9: Interleaving: One Uses MSB the other LSB to Interleave (word addressed)
0
1
2
3
4
5
6
7
000
001
010
011
100
101
110
111
0
1
2
3
4
5
6
7
0
2
4
6
1
3
5
7
Any other options? Why one over another?

## Slide 10: Multiple Memory Chips
X8
high
8
X8
low
8
16
MDR
15:1
CE
CE
WE
WE
0
logic
MAR
How are data wires hooked up?
How is address hooked up?
How is CE hooked up?
How is WE hooked up?
Can we build a banked memory system out of this?
  What needs to change?
  What do we lose?
Notes: 10

## Slide 11: DRAM Cell
11
What happens when you read?
Notes: 11

## Slide 12: DRAM Cell
12
What happens when you read?
Infineon 80nm
Notes: 12

## Slide 13: DRAM Refresh
Capacitor holding value leaks, eventually you will lose information (everything turns to 0)
How do you maintain the values in DRAM?
13
Notes: 13

## Slide 14: Simplified DRAM Internal Structure
14
Row
Column
RAS
CAS
Addr
Notes: 14

## Slide 15: Simplified DRAM Internal Structure
15
Row
Column
RAS
CAS
Addr
Notes: 15

## Slide 16: DRAM Chip
Simple diagram to convey meaning
Current interfaces more involved (more on this later)
16
address
n
CE
WE
k
CAS
RAS
Notes: 16

## Slide 17: DRAM Sense Amplifier
Initially, ACT at Vss (GND) and NLAT* held at Vcc/2
To read: Wordline pulled to Vcc+Vth, D1/D1* changes
To sense:
  First, NLAT* is pulled towards ground
  Then ACT is pulled towards Vcc

## Slide 18: DRAM Sense Amplifier
VCC
GND
GND
VCC
OR

## Slide 19: DRAM Array

## Slide 20: Accessing DRAM (RAS)
Operation Resource Utilization
Cycle
Activate
Row
Request
Data
request
data
Simplified Bank State Diagram
act
pre
wr
rd
Row decoder
Sense amplifier
Column decoder
DRAM
Memory array
bank 0

## Slide 21: Accessing DRAM (CAS)
Operation Resource Utilization
Row decoder
Sense amplifier
Column decoder
DRAM
Memory array
bank 0
request
data
Simplified Bank State Diagram
act
pre
wr
rd
Read
Row
Request
Data
Cycle

## Slide 22: Accessing DRAM (re-writing “lost” data)
Operation Resource Utilization
Precharge
Row
Request
Data
request
data
Simplified Bank State Diagram
act
pre
wr
rd
Row decoder
Sense amplifier
Column decoder
DRAM
Memory array
bank 0
Cycle

## Slide 23: DRAM RAS/CAS Summary
Assert RAS to specify row address
Assert CAS to specify column address
Why separate RAS/CAS?
Can pulse CAS to read more from the same row
  Faster
  Implications?
  Called Fast Page Mode
23
Notes: 23

## Slide 24: What to do while waiting for Act/Pre/…?
request
data
bank n-1
bank 1
Row decoder
Sense amplifier
Column decoder
DRAM
Memory array
bank 0

## Slide 25: DRAM Hierarchy/Banks
Row
Column
RAS
CAS
Bank[1:0]
Why have banks?
Cannot access banks back-to-back. Why?
Notes: 25

## Slide 26: Memory Bank Organization and Operation
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 27: Page Mode DRAM
A DRAM bank is a 2D array of cells: rows x columns
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for activate command

## Slide 28: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 29: 128M x 8-bit DRAM Chip

## Slide 30: DRAM Rank and Module
Rank: Multiple chips operated together to form a wide interface
All chips comprising a rank are controlled at the same time
  Respond to a single command
  Share address and command buses, but provide different data
A DRAM module consists of one or more ranks
  E.g., DIMM (dual inline memory module)
  This is what you plug into your motherboard
If we have chips with 8-bit interface, to read 8 bytes in a single access, use 8 chips in a DIMM

## Slide 31: A 64-bit Wide DIMM (One Rank)

## Slide 32: Generalized Memory Structure

## Slide 33: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column

## Slide 34: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 35: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
SPD (Serial Presence Detect):
Let system know what memory is present and what timings to use

## Slide 36: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 37: Rank
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS <0:1>
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 38: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 39: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 40: Breaking down a Bank
Bank 0
<0:7>
row 0
row 16k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>

## Slide 41: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Channel 0
DIMM 0
Rank 0
Mapped to

## Slide 42: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 43: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 44: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 45: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 1
. . .

## Slide 46: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8B

## Slide 47: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 48: Latency Components: Basic DRAM Operation
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank latency
  Simple CAS (column address strobe) if row is “open” OR
  RAS (row address strobe) + CAS if array precharged OR
  PRE + RAS + CAS (worst case)
DRAM → Controller transfer time
  Bus latency (BL)
Controller to CPU transfer time

## Slide 49: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in
Multiple independent channels serve the same purpose
  But they are even better because they have separate data buses
  Increased bus bandwidth
Enabling more concurrency requires reducing
  Bank conflicts
  Channel conflicts
How to select/randomize bank/channel indices in address?
  Lower order bits have more entropy
  Randomizing hash functions (XOR of different address bits)

## Slide 50: How Multiple Banks Help

## Slide 51: Even more memory
Memory channels
  Separate buses
  Kind of like Cray 1 banks
So now a deep hierarchy
  Channels
  Ranks
  Banks
  Rows
  Columns
  Bits
All of these some sort of “bank”
DRAM bank is internal
Ranks and channels external
Not quite pure random access

## Slide 52: Specifying a DRAM address
Channel
Rank
Bank
Row
Col
Granularity:
  Each chip address holds (width) bits
  So overall granularity is chips*width (rank width)
  But, burst mode so actual memory transfer block is bigger
How to interleave?

## Slide 53: Interleaving revisited
Bank conflicts
Row-buffer (DRAM page) locality
Channel balance
Ranks?
Access pattern impact?
  0, 1, 2, 3, 4, …
  0, 64, 128, …
  0, 7, 2, 9, 11, 15, 12, …

## Slide 54: Interleaving revisited (solutions)
Bank conflicts
Row-buffer (DRAM page) locality
Channel balance
Bit swizzling
  Example: Intel Nehalem (first Intel Core i7)
More sophisticated hashing
  Later Intel processors

## Slide 55: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 16K rows & 2K columns per bank
Row interleaving
  Consecutive rows of memory in consecutive banks
  Accesses to consecutive cache blocks serviced in a pipelined manner
Cache block interleaving
    Consecutive cache block addresses in consecutive banks
    64 byte cache blocks
    Accesses to consecutive cache blocks can be serviced in parallel
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits

## Slide 56: Bank Mapping Randomization
DRAM controller can randomize the address mapping to banks so that bank conflicts are less likely
Reading:
  Rau, “Pseudo-randomly Interleaved Memory,” ISCA 1991.
Column (11 bits)
3 bits
Byte in bus (3 bits)
XOR
Bank index (3 bits)

## Slide 57: Memory Modules (DIMMs)
Dual In-line Memory Module (DIMM)
  Standard memory interface today
Multiple chips on independent module
  Easy to build and maintain systems
DIMMs have one or more “ranks”
Rank is multiple chips that share same CE
x8
8
x8
8
addr
MAR
CE
CE
WE
WE
0
logic
x8
8
x8
8
CE
CE
WE
WE
1
Width?
Ranks?
Chips/rank?

## Slide 58: Even More Memory
x8
8
x8
8
addr
MAR
CE
CE
WE
WE
0
logic
x8
8
x8
8
CE
CE
WE
WE
1
Notes: 58

## Slide 59: Comparison Between Cray 1 and Modern DRAM
Cray 1 used simple memory arrays (not DRAM at the time)
  Each array could process one request at a time
  Each request took 4 CPU cycles (50ns)
  Used 16 banks to allow multiple outstanding requests and pipelining to keep the data bus busy
Modern DRAM chip internally has multiple banks (typically 8)
  Each bank has multiple arrays but all accessed together
  Each array accesses takes several DRAM cycles
  Banking works to keep DRAM chip data bus busy
Multiple ranks
  Multiple ranks are a way of adding capacity without changing the bus width or using narrower chips
  Can be thought of as adding more banks (multiply number of internal banks by number of ranks)

## Slide 60: Improving Memory Throughput/Bandwidth using Interleaving/Banking
Latency
  How long does it take to get from here to there
    and, maybe, back again
Throughput/Bandwidth
  How many things can be done in some unit of time
Memory has long latency and relatively throughput
  Early memory accesses could not be pipelined
    when servicing one operation, others must wait
How can throughput be increased?
  Interleaving/Banking
  Longer bursts – get more for each DRAM access
    RDRAM original approach
      RDRAM was not successful because of business issues and late supply, not the technology

## Slide 61: Even Higher Bandwidth (multiple channels)
What can we do if we want even higher bandwidth?
  Bus already utilized
Add more bus bandwidth
  Increase width or increase frequency
  Frequency already very high and accesses are wide
    Now at least 64B per access (512 bits)
Add more buses
  Each bus controlled separately and connects to multiple DRAM chips/ranks
  Each bus+controller called a channel

## Slide 62: Memory Interfaces
How much data per column command?
  Interface width (x4, x8, …)
    How much data per bus transfer
    Note: each column DRAM address refers to width bits
  Burst length (4, 8, …)
    How many bus transfers per CAS
DDRx
  Double-data rate – multiple data transfers per clock (rising and falling edge, or even faster)
  DDR, then DDR2, then DDR3 – just different standards for defining sizing, timing, and electrical parameters

## Slide 63: What Memory Should I Use?
Depends on access characteristics
  How often is it written?
  How often is it accessed in general?
  How fast should the accesses be?
    Latency? Bandwidth?
  What should the capacity be?
    Bytes? Kilobytes? Megabytes? Gigabytes? Terbytes?
  How long should the data last?
    Microseconds? Seconds? Years? Decades?
  Granularity of access
  Cost
    Dollars, watts or joules, …
Different memories optimized for different access types
  SRAM, DRAM, FLASH, STT-RAM, Phase Change, magnetic disk…

## Slide 64
Memory
Cheap
Efficient
Dense (high capacity)
Fast
Reliable
Notes: 30

## Slide 65
Latency impacted by cell access
denser/efficient  higher latency/lower BW
  Small cells  sensitive circuits  slow reads
  Writes even more complicated
  High BW needs more vias / wires/ circuits
+ latency
+ BW
– density
– cost – energy
– latency
– BW
+ density
+ cost + energy

## Slide 66
Memory system
  Modules, packages, components
  Arranged in a hierarchy
Each memory component
  Has hierarchy
  Has caching/buffering

## Slide 67
Latency + throughput + efficiency  parallelism

## Slide 68
Latency + throughput + efficiency  parallelism
Access cell

## Slide 69
Latency + throughput + efficiency  parallelism
Access many cells in parallel
Many pins in parallel

## Slide 70
Latency + throughput + efficiency  parallelism
Access even more cells in parallel
Many pins in parallel over multiple cycles

## Slide 71
Latency + throughput + efficiency  parallelism
Access even more cells in parallel
Many pins in parallel over multiple cycles

## Slide 72
Hierarchy + parallelism  potential waste