## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 22
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Exam 2
Yes, it was hard for everyone (and long)!

## Slide 3: Exam 2 statistics
Mean: 55.6
  Remember I said I would target an average of 50%
Median: 58
High: 88 (2)
Low: 14
Chart: Exam 2 - Histogram
| 11-20 | 21-30 | 31-40 | 41-50 | 51-60 | 61-70 | 71-80 | 81-90 | 91-100
 | 1 | 1 | 3 | 7 | 6 | 7 | 2 | 4 | 0
Chart: Exam 2 - Cumulative Distribution
| 11-15 | 16-20 | 21-25 | 26-30 | 31-35 | 36-40 | 41-45 | 46-50 | 51-55 | 56-60 | 61-65 | 66-70 | 71-75 | 76-80 | 81-85 | 86-90
 | 1 | 1 | 2 | 2 | 3 | 5 | 9 | 12 | 15 | 18 | 25 | 25 | 26 | 27 | 29 | 31

## Slide 4: Exam 2 – Per-problem breakdown
Chart: Exam 2 - Per Problem Average Score (Normalized)
| Prob1 | Prob2 | Prob3 | Prob4 | Prob5 | Total
 | 0.63484 | 0.8129 | 0.59032 | 0.54194 | 0.24516 | 0.55613

## Slide 5: Final Exam
Dec 14, Friday, 7-10pm
Time won’t be an issue! (3-hours)
Will be comprehensive
  Will include everything we discussed in class
Stay focused throughout remainder of semester
  Still have final exam, 2 regular labs, and grad lab!
I will take ”progress” into account for final grade assignment

## Slide 6: Guest Lecture
On December 5 (Wednesday) in normal class
Speaker: Hongsup Shin (Arm Research)
  Tentative Title: “A Practical Guide to Machine Learning”

## Slide 7: More Announcements
Please do eCIS (electronic Course Instructor Survey)
  Open through Dec 10, 2018 (I’ll keep reminding you!)
  https://youtu.be/TIU5_rtEEsY:
    short video on how to fill them out in a meaningful way
  https://utdirect.utexas.edu/ctl/ecis/index.WBX
Remember that this is my first course, so I’d really like to learn how I am doing and how to make my course better
  Please be specific!

## Slide 8: Today
Multi-Processing
Cache Coherency
Memory Consistency

## Slide 9: Organizations for ILP (for multiple ALUs)
Instruction-level parallelism is done by hardware or compiler
  Can be extracted from any code
  Limited by
    Visibility (instruction window)
    Fine-grained dependencies
    Unknown dependencies
      Loads
      Branches
      …

## Slide 10: Vectors (DLP for multiple ALUs)
sequencer
memory hierarchy
Local Mem
Local Mem
Local Mem
Local Mem

## Slide 11: How do we get more parallelism
Overcome frontend constraints
Overcome expensive centralized structures
Avoid limitations of SIMD/vectors
  Sometimes really do need different operations on different data
Make it the programmer’s problem

## Slide 12: MIMD machines (multiple-instruction multiple-data)
Multiple processors, each with own thread of control
  Or threads of control
Each thread can be
  Different program (multi programming)
    Easy parallelism because just about no communication
  Different aspects of same program
    Like client / server
    Or a graph of dependent tasks (dataflow)
  One integrated parallel program
    Single-program multiple data (SPMD)
Get around those nasty superscalar scaling issues
Different challenges from vectorization
  Easy to get some MIMD parallelism
  Not as easy to get a lot, but easier than with vectors

## Slide 13: MIMD (symmetric memory processing)
sequencer
memory hierarchy
scheduler
scheduler
scheduler
scheduler
sequencer
sequencer
sequencer

## Slide 14: MIMD (not symmetric)
sequencer
memory hierarchy
scheduler
scheduler
scheduler
scheduler
sequencer
sequencer
sequencer
memory hierarchy
memory hierarchy
memory hierarchy

## Slide 15: Communication
2 basic forms
  Message Passing
  Shared Memory
Can have both
2 Levels
  User level (what user sees)
  Architectural level (what is implemented in hardware)

## Slide 16: What is Message Passing?
Characterized by explicit send/receive
Carries any sort of data
  Pure data
  Instructions with data
  Instruction pointer
  Etc.

## Slide 17: What is Shared Memory?

## Slide 18: SMP/CMP: Simple Start
SMP: Symmetric Multi-Processing
CMP: Chip Multi-Processing
Each process runs as if on a single processor system
  except, can run on any processor
When swapped out, put into global system queue
One OS, run the same way as user processes
  any processor can run the OS
Helps latency or throughput or both?
18
Notes: 18

## Slide 19: SMP/CMP Problems
How to share memory?
  Most problems can be reduced to this one
How does OS run?
  multiple processors, processes!
  scheduling problems
    who runs where when?
How is parallel computation organized???
  A little more on that later
19
Notes: 19

## Slide 20: Coherent Caches
Cache contains subset of data in memory
Cache may contain more up-to-date data than memory
  can memory contain more up-to-date data than cache?
Coherency Problem!
What protocol to follow?
Processor
Cache
Memory

## Slide 21: Review: Loads, Stores and Buses
We know how to issue loads and stores
What happens afterwards?
  Check cache
  If not in cache (or while checking in cache) issue Read to memory bus
    Need Read for both load and store miss?
    Different Read for load than store?
Bus operations different than load/store operations!
Processor
Cache
Memory

## Slide 22: Coherent Caches
Cache contains subset of data in memory
Cache may contain more up-to-date data than memory
  can memory contain more up-to-date data than cache?
What if one processor’s cache has up-to-date value when the other issues a read to same location?
Coherency Problem!
Steps to follow to ensure coherence is called a coherence protocol
Processor
Cache
Memory
Processor
Cache

## Slide 23: Cache coherency
How can you ensure that you are always reading the latest value?
Proc 1 Proc 2
R0=M[10] M[10]=1

## Slide 24: Cache coherency and memory consistency
Need a global order for memory operations to ensure consistent view of memory (deal with conflicts)
Proc 1 Proc 2 Proc 3
MEM[10] = 11 MEM[10] = 21 R1 = MEM[10]
R0 = MEM[10] R0 = MEM[10] R2 = MEM[10]
MEM[10] = 12 MEM[10] = 22 R3 = MEM[10]
R1 = MEM[10] R1 = MEM[10]

## Slide 25: Cache Coherency (2)
Need a global order for memory operations to same address to ensure consistent view of memory
Bus can provide that ordering
  Only one transaction on the bus at any given time
Processors (caches) “snoop” all memory requests on bus
  Cache maintains coherence based on
    Memory operations originating from its node
      Different Read in response to a Store?
    Current state of its cache
    What it snoops

## Slide 26: MSI Protocol (writeback cache)
M
S
I
I/O read \ WB
Store
I/O read/write
Store/Load
I/O read/write \ WB
I/O read, load
Store
Load
I/O write

## Slide 27: MSI Protocol (writeback cache)
M
S
I
Other load\ WB
Own Store
Other load/store
Own Store/Load
Other Store\ WB
Other, Own load
Own Store
Own Load
Other Store

## Slide 28: Can We Improve MSI? No One Sharing?
Don’t have to invalidate others if modifying block that no one else has
Can reduce number of bus transactions compared to MSI protocol
How do we implement this?

## Slide 29: MESI Protocol (writeback cache)
M
E
I
Own Clean\ WB
Own Store
Other load/store
Own Store/Load
Other Store, Other Load-E\ WB
Own load
Own Store
Own Load-E
S
Other Load\ WB
Other, Own load
Other Store, Other Load-E
Other Store, Other Load-E
Other load
Own Load-E
Own Store

## Slide 30: Can We Improve MESI? Skip Memory?
MOESI
  Add Owned state
  Cache can reply with value on behalf of memory
  Owned can be dirty
MESIF (Intel)
  Cache can reply on behalf of memory, if clean

## Slide 31: What if we don’t have a single bus?
Distributed shared memory
Use “directory protocol”
  Can still implement MESI/MOESI/MESIF
Each memory location has a home node and directory to track its state and where the data lives
Conceptually shared memory over message passing
  Distributed shared memory
  Bus after memory yet still single address space
Many many complications and opportunities

## Slide 32: MIMD (not symmetric)
sequencer
memory hierarchy
scheduler
scheduler
scheduler
scheduler
sequencer
sequencer
sequencer
memory hierarchy
memory hierarchy
memory hierarchy

## Slide 33: Memory Consistency Model (Memory Ordering)
Order to one memory location is maintained due to bus
What about to multiple locations?
Memory consistency model
  Example: Sequential Consistency:
    order is arbitrary interleaving of program order per processor
  Proc 1 Proc 2
  M[10]=1 M[20]=1
  R0=M[20] R1=M[20]
Weaker models exist
  Order to different memory locations can get out of program order
  Add explicit memory synchronization instructions: “fences”

## Slide 34: Cache coherency and memory consistency
Need a global order for memory operations to ensure consistent view of memory (deal with conflicts)
Proc 1 Proc 2 Proc 3
MEM[10] = 11 MEM[11] = 21 R1 = MEM[10]
R0 = MEM[10] R0 = MEM[10] R2 = MEM[11] <- say this is 12
MEM[11] = 12 MEM[10] = 22 R3 = MEM[10] <- possible vals?
R1 = MEM[10] R1 = MEM[10]

## Slide 35: Mutual Exclusion
A property of concurrency control
One thread never enters its critical section at the same time that another concurrent thread its critical section
Must be free of deadlocks
Dekker’s algorithm
  First known correct solution to mutual exclusion problem
  Allows two threads to share a single-use resource without conflict
  Uses only shared memory for communication
  Guarantees:
    Mutual exclusion
    Freedom from deadlock
    Freedom from starvation

## Slide 36: Dekker’s Algorithm Pseudo-code
P0:
want_to_enter[0] = true
while want_to_enter[1] {
if turn != 0 {
want_to_enter[0] = false
while turn != 0 {
// busy wait
}
want_to_enter[0] = true
}
}
// critical section
…
turn = 1
want_to_enter[0] = false
// remainder section
P1:
want_to_enter[1] = true
while want_to_enter[0] {
if turn != 1 {
want_to_enter[1] = false
while turn != 1 {
// busy wait
}
want_to_enter[1] = true
}
}
// critical section
…
turn=0
want_to_enter[1] = false
// remainder section
Initially: want_to_enter[0] = false, want_to_enter[1] = false, turn = 0

## Slide 37: Memory Consistency Model (Memory Ordering)
Order to one memory location is maintained due to bus
What about to multiple locations?
Memory consistency model
  Example: Sequential Consistency:
    Order is arbitrary interleaving of program order per processor
    But, same ordering observed on all processors
  Proc 1 Proc 2
  M[10]=1 M[20]=1
  R0=M[20] R1=M[10]
  What are possible values for R0 and R1?

## Slide 38: Sequential Consistency Example
Valid orders
  1234
  1324
  1342
  3124
  3142
  3412
What are possible values for R0 and R1?
Invalid orders
  2134
  2143
  3214
  …
  Proc 1 Proc 2
  1: M[10]=1 3: M[20]=1
  2: R0=M[20] 4: R1=M[10]

## Slide 39: But wait, what about that LSQ?
OOO machines speculate on load/store order
How does this interact with consistency?
What about MSHRs and other write buffers?
Change the ordering model?
  How? New instructions needed?
Change how speculation is done?

## Slide 40: Total Store Order (x86)
Change the model but don’t add instructions
All others observe stores in a common order, but
Loads can be performed before others have observed a store
  Order within processor/core may be different from what others observe
  Proc 1 Proc 2
  M[10]=1 M[20]=1
  R0=M[20] R1=M[10]
Possible to have R0 = R1 = 0!

## Slide 41: Release Consistency and others
Add new “memory fence” instructions
Many variants, example:
  Acquire fence (as in acquire a lock)
  Release fence (as in release a lock)

## Slide 42: Release Consistency and others
Add new “memory fence” instructions
Many variants, example:
  Acquire fence (as in acquire a lock)
    Wait until all prior reads finish before doing any new memory operation
  Release fence (as in release a lock)
    Wait until all prior memory operations complete before any new reads

## Slide 43: An OS Issue: Paging
What if a page frame is paged back to disk?
  Shared page tables
  Coherence handles?
  Any other issues?
TLBs must be kept synchronized!
  TLB is a cache of virtual to physical translations
    explicitly controlled
  Yet another coherency problem!

## Slide 44: TLB Coherency Solution
When changing a TLB entry, flush other TLB’s that may contain same virtual to physical translation
  “TLB shootdown”
    Send Inter-processor interrupts (IPI) to all core
    Each core that receives IPI traps to S/W and invalidates TLB entry or flushes entire TLB (depending on platform)
Must also insure that all memory transactions already in progress must complete
  why?
Only afterwards can page be swapped

## Slide 45: MIMD (symmetric memory processing)
sequencer
memory hierarchy
scheduler
scheduler
scheduler
scheduler
sequencer
sequencer
sequencer

## Slide 46: Superscalar + multithreading (TLP for multiple ALUs)
scheduler
sequencer
memory hierarchy
sequencer

## Slide 47: Can we speculate on threads?
Yes!
But, need to have “heavy” recovery process
  LSQ and ROB not deep enough
Enter “transactional memory”