## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 23
Dam Sunwoo
University of Texas at Austin
Arm Research
(Some slides borrowed from Prof. Onur Mutlu)

## Slide 2: Announcements
Grad Lab
  Newer gcc available on LRC machines by loading modules
  See instructions available on Piazza
    Look for post titled “Error in building Champsim”

## Slide 3: Reminder!
Please do eCIS (electronic Course Instructor Survey)
  Open through Dec 10, 2018 (I’ll keep reminding you!)
  https://youtu.be/TIU5_rtEEsY:
    short video on how to fill them out in a meaningful way
  https://utdirect.utexas.edu/ctl/ecis/index.WBX
Remember that this is my first course, so I’d really like to learn how I am doing and how to make my course better
  Please be specific!

## Slide 4: Great textbook for Parallel Computer Architecture
“Parallel Computer Architecture: A Hardware/Software Approach”
  David E. Culler, Jaswinder Pal Singh
In case you want to learn more

## Slide 5: Coherent Caches
Cache contains subset of data in memory
Cache may contain more up-to-date data than memory
  can memory contain more up-to-date data than cache?
What if one processor’s cache has up-to-date value when the other issues a read to same location?
Coherency Problem!
Steps to follow to ensure coherence is called a coherence protocol
Processor
Cache
Memory
Processor
Cache

## Slide 6: Cache Coherency (2)
Need a global order for memory operations to same address to ensure consistent view of memory
Bus can provide that ordering
  Only one transaction on the bus at any given time
Processors (caches) “snoop” all memory requests on bus
  Cache maintains coherence based on
    Memory operations originating from its node
      Different Read in response to a Store?
    Current state of its cache
    What it snoops

## Slide 7: Coherence Options: Update vs. Invalidate
Update: push an update to all copies
  On write, broadcast data to sharers
Invalidate: Ensure there is one copy (local), then update it
  On write, broadcast invalidation of address to sharers
Trade-offs
  Update
    (+) If sharer set is constant and updates are infrequent, avoids cost of invalidate-reacquire (broadcast update pattern)
    (-) If data is re-written without intervening reads from other cores, updates were useless
    (-) Write-through policy -> bus becomes bottleneck
  Invalidate
    (+) After invalidation broadcast, core has exclusive access rights
    (+) Only cores that keep reading after each write retain a copy
    (-) If write contention is high, leads to ping-ponging (rapid mutual invalidation-reacquire)

## Slide 8: MSI Protocol (writeback cache)
M
S
I
Other load\ WB
Own Store
Other load/store
Own Store/Load
Other Store\ WB
Other, Own load
Own Store
Own Load
Other Store

## Slide 9: MSI Protocol (A different view)
A/B notation:
  A: Event (Proc or Bus)
  B: Action (bus transaction)
    ‘--’ means null action
BusRdX:
  Bus Read Exclusive
    aka Read For Ownership (RFO)
    aka Read with Intent to Modify (RWITM)
Flush:
  writeback of data
“upgrade”
“downgrade”
[Diagram from Culler/Singh 97]

## Slide 10: Can We Improve MSI? No One Sharing?
Don’t have to invalidate others if modifying block that no one else has
Can reduce number of bus transactions compared to MSI protocol
How do we implement this?

## Slide 11: MESI Protocol (writeback cache)
M
E
I
Own Clean\ WB
Own Store
Other load/store
Own Store/Load
Other Store, Other Load-E\ WB
Own load
Own Store
Own Load-E
S
Other Load\ WB
Other, Own load
Other Store, Other Load-E
Other Store, Other Load-E
Other load
Own Load-E
Own Store

## Slide 12: MESI Protocol (Illinois Protocol [ISCA 1984] )
S (shared signal)
  Determine on a BusRd if any other cache currently holds the data
    Wired-OR line
  BusRd(S):
    BusRd caused S to be asserted
  BusRd(S):
    BusRd didn’t cause S to be asserted
Flush’
  Flushed only if “cache-to-cache sharing” is in use
  Otherwise, no action (--)
  _
[Diagram from Culler/Singh 97]

## Slide 13: Some MESI Tradeoffs
Should a downgrade from M go to S or I?
  S: If data is likely to be reused (before it is written to by another processor)
  I: if data is likely to be not reused (before it written to by another)
Cache-to-cache transfer
  On a BusRd, should data come from another cache or memory
  Another cache
    May be faster, if memory is slow or highly contended
  Memory
    Simpler: no need to wait to see if cache has data first
    Less contention at the other caches
    Requires writeback on M downgrade (sometimes unnecessarily)

## Slide 14: Can We Improve MESI? Skip Memory?
MOESI
  Add Owned (O) state (dirty AND shared)
  Cache can reply with value on behalf of memory
    Owned cache line must respond with data
  Modified is only copy and dirty
  Owned is dirty. Owned has exclusive right to make changes
  Shared can be dirty. No permission to make changes
MESIF (Intel)
  Add Forward (F) state
    Special form of S state. Designated responder for requests for given line
  Cache can reply on behalf of memory, if clean
  F is clean (may be discarded at any time without notice)

## Slide 15: Snoop Filters
All snoopers must snoop bus transactions
  Snoopers then look up their corresponding cache tag to check whether it has the same cache block
  In many cases, caches do not have the cache block
    Well-optimized parallel program doesn’t share much data among threads
  Tag lookup disturbs cache accesses by CPU and incurs power consumption
Snoop filters can reduce unnecessary snooping
  Directory-based structures that have less lookup costs than cache lookup.
    Monitors all coherent traffic to keep track of coherency state of cache blocks
  Source filter
    Filters coherence requests before they reach interconnect
  Destination filter
    Filters from destination side of coherence transaction

## Slide 16: What if we don’t have a single bus?
Distributed shared memory
Use “directory protocol”
  Can still implement MESI/MOESI/MESIF
Each memory location has a home node and directory to track its state and where the data lives
Conceptually shared memory over message passing
  Distributed shared memory
  Bus after memory yet still single address space
Directory: Single point of serialization per block
  Snoopy Bus: Single point of serialization for all accesses
Many many complications and opportunities

## Slide 17: MIMD (not symmetric)
sequencer
memory hierarchy
scheduler
scheduler
scheduler
scheduler
sequencer
sequencer
sequencer
memory hierarchy
memory hierarchy
memory hierarchy

## Slide 18: Directory Coherence
Directory organization for Distributed Memory System
[Diagram from Culler/Singh 97]

## Slide 19: Directory Coherence Example
For each cache block, store P+1 bits in directory
  1 presence bit per cache (whether block is in cache)
  Exclusive bit: indicates cache has only copy and intends to write
    Can update without notifying others. May or may not be dirty.
  Exclusive bit for each block in each cache as well
  P0 P1 P2 P3
Initial state
P1 read miss
P3 read miss
P2 write miss
P3 write miss
P2 read miss
E: 0 | 0 | 0 | 0 | 0
E: 0 | 0 | 1 | 0 | 0
E: 0 | 0 | 1 | 0 | 1
E: 1 | 0 | 0 | 1 | 0
E: 1 | 0 | 0 | 0 | 1
E: 0 | 0 | 0 | 1 | 1
Invalidate P1 & P3
Exclusive bit set in P2 cache block
Req block from P2. Give block to P3
Excl bit set in P3. Invalidate P2

## Slide 20: Basic operation of Simple Directory
[Diagram from Culler/Singh 97]

## Slide 21: Snoopy Cache vs. Directory
Tradeoffs:
  Snoopy Cache
    (+) Miss latency (critical path) is short: miss -> bus transaction to memory
    (+) Global serialization is easy: bus provides this already (arbitration)
    (+) Simple: adapt bus-based uniprocessors easily
    (-) Relies on broadcast messages to be seen by all caches (in same order):
      single point of serialization (bus): not scalable
      need a virtual bus (or a totally-ordered interconnect)
  Directory
    (-) Adds indirection to miss latency (critical path): request -> dir. -> mem.
    (-) Requires extra storage space to track sharer sets
      Can be approximate (false positives are OK)
    (-) Protocols and race conditions are more complex (for high-performance)
    (+) Does not require broadcast to all caches
    (+) Exactly as scalable as interconnect and directory storage
      Much more scalable than bus

## Slide 22: Memory Consistency Model (Memory Ordering)
Order to one memory location is maintained due to bus
What about to multiple locations?
Memory consistency model
  Example: Sequential Consistency:
    Order is arbitrary interleaving of program order per processor
    But, same ordering observed on all processors
[Diagram from Culler/Singh 97]
Programmer’s abstraction of memory under sequential consistency

## Slide 23: Sequential Consistency Example
Valid orders
  1234
  1324
  1342
  3124
  3142
  3412
What are possible values for R0 and R1?
Invalid orders
  2134
  2143
  3214
  …
  Proc 1 Proc 2
  1: M[10]=1 3: M[20]=1
  2: R0=M[20] 4: R1=M[10]

## Slide 24: Cache coherency and memory consistency
Need a global order for memory operations to ensure consistent view of memory (deal with conflicts)
Proc 1 Proc 2 Proc 3
MEM[10] = 11 MEM[11] = 21 R1 = MEM[10]
R0 = MEM[10] R0 = MEM[10] R2 = MEM[11] <- say this is 12
MEM[11] = 12 MEM[10] = 22 R3 = MEM[10] <- possible vals?
R1 = MEM[10] R1 = MEM[10]

## Slide 25: Mutual Exclusion
A property of concurrency control
One thread never enters its critical section at the same time that another concurrent thread its critical section
Must be free of deadlocks
Dekker’s algorithm
  First known correct solution to mutual exclusion problem
  Allows two threads to share a single-use resource without conflict
  Uses only shared memory for communication
  Guarantees:
    Mutual exclusion
    Freedom from deadlock
    Freedom from starvation

## Slide 26: Dekker’s Algorithm Pseudo-code
P0:
want_to_enter[0] = true
while want_to_enter[1] {
if turn != 0 {
want_to_enter[0] = false
while turn != 0 {
// busy wait
}
want_to_enter[0] = true
}
}
// critical section
…
turn = 1
want_to_enter[0] = false
// remainder section
P1:
want_to_enter[1] = true
while want_to_enter[0] {
if turn != 1 {
want_to_enter[1] = false
while turn != 1 {
// busy wait
}
want_to_enter[1] = true
}
}
// critical section
…
turn=0
want_to_enter[1] = false
// remainder section
Initially: want_to_enter[0] = false, want_to_enter[1] = false, turn = 0

## Slide 27: But wait, what about that LSQ?
OOO machines speculate on load/store order
How does this interact with consistency?
What about MSHRs and other write buffers?
Change the ordering model?
  How? New instructions needed?
Change how speculation is done?

## Slide 28: Total Store Order (x86)
Change the model but don’t add instructions
All others observe stores in a common order, but
Loads can be performed before others have observed a store
  Order within processor/core may be different from what others observe
  Proc 1 Proc 2
  A: M[10]=1 X: M[20]=1
  B: R0=M[20] Y: R1=M[10]
Possible to have R0 = R1 = 0!

## Slide 29: Release Consistency and others
Add new “memory fence” instructions
  explicit memory synchronization instructions
Many variants, example:
  Acquire fence (as in acquire a lock)
  Release fence (as in release a lock)

## Slide 30: Release Consistency and others
Add new “memory fence” instructions
  explicit memory synchronization instructions
Many variants, example:
  Acquire fence (as in acquire a lock)
    Wait until all prior reads finish before doing any new memory operation
  Release fence (as in release a lock)
    Wait until all prior memory operations complete before any new reads

## Slide 31: Architectures have different ordering rules
[source: https://en.wikipedia.org/wiki/Memory_ordering ]

## Slide 32: An OS Issue: Paging
What if a page frame is paged back to disk?
  Shared pages
  Coherence handles?
  Any other issues?
TLBs must be kept synchronized!
  TLB is a cache of virtual to physical translations
    explicitly controlled
  Yet another coherency problem!

## Slide 33: TLB Coherency Solution
When changing a TLB entry, flush other TLBs that may contain same virtual to physical translation
  “TLB shootdown”
    Send Inter-processor interrupts (IPI) to all cores
    Each core that receives IPI traps to S/W and invalidates TLB entry or flushes entire TLB (depending on platform)
Must also insure that all memory transactions already in progress must complete
  why?
Only afterwards can page be swapped

## Slide 34: MIMD (symmetric memory processing)
sequencer
memory hierarchy
scheduler
scheduler
scheduler
scheduler
sequencer
sequencer
sequencer

## Slide 35: Superscalar + multithreading (TLP for multiple ALUs)
scheduler
sequencer
memory hierarchy
sequencer

## Slide 36: Taxonomy of Multithreading
Single Threaded
Coarse Grain Multithreaded
(CMT)
Fine Grain Multithreaded
(FMT)
Simultaneous Multithreaded
(SMT)
Task 1
Task 2
OS context switch
Cache miss
Cache miss
CPU cycles
- Only one program thread at a time
- Switch through OS scheduling
- Two threads running at same time
- Switch at cache miss
- Stalled cycles between switching
- Hide OS switch time & cache miss
- No stall cycles between thread switch
- Instructions from one thread executed each cycle
- Hide OS switch & cache miss & pipeline stall
- Instructions from different thread can be executed per cycle
- Hide OS switch & cache miss & pipeline stall
Issue0
Issue1
Issue0
Issue1
Issue0
Issue1
Issue0
Issue1

## Slide 37: Can we speculate on threads?
Yes!
But, need to have “heavy” recovery process
  LSQ and ROB not deep enough
Enter “transactional memory”
  Programmer specifies code to be executed atomically as transactions.
  Hardware/software guarantees atomicity for transactions.
  Optimistic concurrency
  Motivated by difficulty of lock-based programming