## Slide 1: EE 382N.1: Computer Architecture Fall 2018: Lecture 2
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Dam’s office hours:
  MW 6:30-7:30pm (after class) in classroom or EER 0.814D
  Or, by appointment
Don’t forget Lab #0
  set up environment and test submission
Survey #1 – Tell us about yourself (through Canvas)
Lab #1 is out
  Pair up if you wish
Problem Set #1 is out
Check Canvas / Piazza for announcements
  You can search for teammates on Piazza

## Slide 3: Review
What is architecture?
  Match requirements with technology under constraints
  Define system components and how they interface/interact
  Tradeoffs, tradeoffs, tradeoffs
    Know what they are and know how to decide
    Realize that tradeoffs change over time
    Creative solutions can avoid tough choices
Arch/microarch?
  Arch is always SW visible, microarch can be ignored by SW
  Ideal test: If can’t tell difference between two systems without measuring time or resources, then only differences are march
Class policies
  Do the homework (small groups), 6 + 1 labs (yourself), take the 2 mid-terms (in class) and the final, contribute to class
  Don’t cheat

## Slide 4: Outline
What is an ISA
Why ISA?
Creating ISAs
Implementing ISAs
Evaluating tradeoffs
  Amdahl’s Law

## Slide 5: Prof. Patt’s Layers (Recap)

## Slide 6: What is an ISA?
And why are there many?

## Slide 7: Instruction Set Architecture (Recap)
Instruction Set
  Load/Store memory
  Opcodes, Address Modes, Data Types
  Condition codes
  Format
Memory
  Address space
  Addressability
  Alignment
Priority/Privilege
Interrupt/Exception Handling
Arithmetic
I/O
Multi-threading support
Multiprocessor support

## Slide 8: What are instructions for?

## Slide 9: Why have instructions?
And what are the alternatives to having instructions?

## Slide 10: Why Have Instructions?
Alternatives
  Special purpose hardware
  Reconfigurable hardware (FPGAs)
  Minimize everything as much as possible?
Simplifies interface
  Software knows what is available
  Hardware knows what needs to be implemented
Abstraction protects software and hardware
  Software can run on new machines
  Hardware can run old software

## Slide 11: So what instructions should we have?

## Slide 12: Early Machines
Very limited resources
  Hundreds or thousands of words of memory
  A few thousand vacuum tubes
  Huge cost (millions back then)
Minimize everything as much as possible
  Instruction size
  Amount of memory/registers
  Size of ALU
  Number of ALU functions
  Parallelism

## Slide 13: Modern Machines
Some resources limited, others abundant
  Billions/Trillions of words of memory
  Billions of transistors
  Cost limitations
  Power limitations
Minimize cost, maximize usability

## Slide 14: Language/Application-Directed Architecture
ISA/Microarchitecture originally optimized for language/application
Examples include
  LISP: Symbolics 3600, TI Explorer
    Tags for GC, linked-list support, etc.
  C: auto-increment memory index registers
    *X++ = Y;
Other ways to implement language constructs
  Simpler ISA, map language onto ISA with compiler
How should performance be taken into account?
Debate was settled for a while, but perhaps being revisited?

## Slide 15: Characteristics of a Good ISA
Unambiguous
Expressive
  Easily describes all the algorithms that will run on this platform
Instructions are used
  Very complex instructions might not be used often
(Relatively) easy to compile
(Relatively) easy to implement well
Implementation provides good performance, cost, etc.
ISAs often highly reliant on microarchitecture and vice-versa
  Some ISAs easy to implement on some microarchitectures
  Some microarchitectures make some instructions easy to implement

## Slide 16: What’s in a computer?
Discussion (summarized later)
Computer building blocks

## Slide 17: Computer Building Blocks
Memory (storage)
  E.g., registers
  E.g., RAM
  E.g., disk
Computation
  Functional units in general
  ALUs
Control (when do things happen)
  E.g., decoder
  E.g., instruction sequencer
Communication
  E.g., bus
Notes: 17

## Slide 18: What tradeoffs are there related to an ISA?

## Slide 19: Tradeoffs
Fewer instructions
  Pros?
  Cons?
  There are 1 instruction ISAs
    subleq a, b, c ;
      Mem[b] = Mem[b] - Mem[a] ;if (Mem[b] ≤ 0) goto c
Number of registers per instruction
  Number of bits per instruction
  Number of registers to implement
  Zero, One, Two, Three, Four, …
Fixed verses Variable Length instructions
Notes: 19

## Slide 20: Number of Registers Per Instruction (Implied or Explicit): C = A + B
Zero
  Stack machine (HP calculators): implied addresses
  PUSH AddrA; PUSH AddrB; ADD; POP AddrC
One (implied)
  Accumulator-based machine
  LOAD AddrA; ADD AddrB; STORE AddrC
Two (same register, src and dest)
  One source is destination
  LOAD R1, AddrA; LOAD R2, AddrB;
  ADD R1, R2; STORE R1, AddrC
Three
  Current (D = S1 OP S2)
  LOAD R1, AddrA; LOAD R2, AddrB;
  ADD R3, R1, R2; STORE R3, AddrC
Four and above
Notes: Don’t spend too much time on this slide, will discuss later

## Slide 21: Tradeoffs Change Over Time
Technologies, abilities and concerns change
Early computers
  Number of devices
    Vacuum tubes expensive, unreliable, big, power hungry
Mainframes/Mini-Computers
  Code compatibility
  Number of devices
  System efficiency
    Multi-tasking operating systems
  Reliability
Personal Computers
  Code compatibility
  Cost
  Size
  Power
  Is number of devices/system efficiency as important???

## Slide 22: Evaluating Tradeoffs
Performance often inconsistent and hard to determine
Better for one application may be worse for another
  Ferrari versus Suburban
Even within the same category, differences
  CART versus Formula 1
Different parameters result in different optimal points
  Needs
  Algorithms
  Implementations
  Technologies

## Slide 23: Evaluating tradeoffs requires measurement
“If you can’t measure it, you can’t improve it” –P. Drucker
Also, you can’t objectively compare if you do not measure
So, what should we measure?
  Performance
    Execution time
    Instructions per Cycle (IPC)
  Cost: chip area
  Power / Energy
  Complexity
    Affects design time, validation time

## Slide 24: How much improvement is worthwhile?
Where should we target our improvement?

## Slide 25: Amdahl’s Law (performance example)
Unchanged time
Fraction sped up

## Slide 26: Example of Amdahl’s Law
New feature doubles floating point performance. What sort of overall performance boost?
What is fraction of floating point operations?
  100%: Speedup = (1/0.5) = 2.
  50%: Speedup = 1/((1-0.5)+0.5/2) = 1/(0.5 + 0.25) = 1/0.75 = 1.33

## Slide 27: Amdahl’s Law
Lesson: big performance boost of one area does not necessarily lead to overall performance boost
Diminishing returns
Applies to more than just performance:
  Power, cost, reliability …

## Slide 28: What Did We Learn?
ISAs
  Slowly changing definition of architecture
  Flexible and concise way of expressing programs
  Amenable to automatic tools
  Critical aspect of architecture
    Along with other aspects, ISAs define contract between HW and SW
    Abstraction protects both SW and HW
  Influenced by uarch and technology
Tradeoffs
  Depends on requirements and context
  Always attack the bottleneck
  Amdahl’s Law
Remember: Survey #1, Lab #0, Lab #1, Problem Set #1!