## Slide 1: EE 382N.1: Computer Architecture Fall 2018: Lecture 3
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Recap
ISA
Tradeoff
Amdahl’s law
  Always attack the bottleneck
Reminders:
  Questions on Piazza! (activity starting to ramp up)
  Survey #1: 30 respondents so far (please submit by tomorrow)
  Problem Set #1: Due 9/17 (Gradescope)
  Lab #1: Due 9/23
  Office hours: Please come see me after class first or by appointment

## Slide 3: Recap: Abstraction Layers

## Slide 4: Implementing ISAs: Microcode
Each instruction implemented by a finite state machine that controls the individual components within the processor
Each state executes one step of the instruction
  Consists of control (including NOP) for every functional unit
    Wide-word
  May be encoded to trade logic for microcode space
Really flexible
Quite simple
Resource efficient

## Slide 5: What’s in a computer?
Arithmetic logical units (ALUs)
Storage: registers and memory (and I/O)
Communication (buses)
Control

## Slide 6: uCoded Computer
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
Read/write + addr
Enable, write
Read/write
ALU Op | Shift
Notes: Animate the micro operations

## Slide 7: uCoded Computer
ADD DR, SR1, SR2
  Regs[SR1] -> A;
  Regs[SR2] -> B;
  ADD->ALU; ALU->Regs[DR]
  Fetch and execute next instruction
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Notes: Animate the micro operations

## Slide 8: uCoded Computer
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
Read/write + addr
Enable, write
Read/write
ALU Op | Shift
Notes: Animate the micro operations

## Slide 9: Compiler/ISA/MicroArch Interface
…
a = *(m1) + *(m2);
…
Program
Programming language
...
LDR R3, [R1]
LDR R4, [R2]
ADD R5, R3, R4
...
ISA
MAR<-SR2
B<-MEM
MAR<-SR1
A<-MEM
DR<-A+B
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
Microcode
Machine code
Execution
Compiler
Hardware

## Slide 10: Microcoded Machines Are “Good”
Area efficient
Easier to verify/maintain in some ways
Reuse components
  Memory
Use simple components
  One-ported register file
Single ALU
  Use same ALU for instruction address operations
Bit-serial ALUs, datapaths, etc.

## Slide 11: Where Does Microcode Live?
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
Microcode is in: Microcode store (inside control)
Embedded in the control signals

## Slide 12: Microcode Control
Microcoded computer interprets ISA
Microcode is a finite state machine
  Fetch_instruction macro
  Interpret_instruction macro
Microcode is an ISA interpreter/simulator!
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
Fetch/Parse
Instruction
Interpret
Instruction
Notes: To implement conditional instruction execution. Implementing a branch, or implementing a instruction that has conditional execution (predicated instructions)

## Slide 13: Another Way to View Microcode: A Program that Interprets Instructions
main() {
pc_type pc = 0;
inst_type inst;
while (true) {
  inst = fetch_instruction(pc);
  pc = interpret_instruction(inst);
}
}
inst_type fetch_instruction(pc_type pc) {
????
}
pc_type interpret_instruction(pc_type pc, inst_type inst) {
????
}
Notes: Return((inst_type)MEM[pc]);
Switch(inst) {
Case ADD:
R1 = REGS[inst.sr1];
R2 = REGS[inst.sr2];
REGS[inst.dr] = R1 + R2;
return(PC + 2);

## Slide 14: Each Interpret Instruction is a Different Path in Microcode State Machine
DR = SR1 + SR2
  A <- Regs[SR1];
  B <- Regs[SR2];
  ALU<- ADD; Regs[DR]<- ALU
Fetch/Parse
Instruction
Interpret
LD
Interpret
….
Interpret
ADD

## Slide 15: LC-3b Microcode
MAR<-PC
PC<-PC+2
MDR<-M
R
IR <- MDR
BEN<-IR[11]&N + IR[10]&Z + IR[9]&P
[IR[15:12]]
DR<-SR1+OP2*
setCC
DR<-SR1&OP2*
setCC
DR<-SR1 XOR OP2*
setCC
MAR<-LSHF(ZEXT[IR[7:0]],1)
MDR<-M[MAR]
R7<-PC
R
PC<-MDR
DR<-SHF(SR,A,D,amt4)
setCC
DR<-PC+LSHF(off9,1)
setCC
MAR<-B+off6
MDR<-M[MAR[15:1]’0]
R
DR<-SEXT[BYTE.DATA]
setCC
MAR<-B+LSHF(off6,1)
MDR<-M[MAR]
R
DR<-MDR
setCC
MAR<-B+LSHF(off6,1)
MDR<-SR
R
M[MAR]<-MDR
MAR<-B+off6
MDR<-SR[7:0]
R
M[MAR]<-MDR**
[IR[11]]
R7<-PC
PC<-BaseR
R7<-PC
PC<-PC+LSHF(off11,1)
PC<-BaseR
PC<-PC+LSHF(off9,1)
[BEN]
18
18
18
18
18
18
18
18
18
19
18
18
18
18
ADD
AND
XOR
TRAP
SHF
LEA
LDB
LDW
STW
JSR
JMP
BR
18,19
33
35
1
5
9
15
28
30
13
14
2
6
7
3
4
12
0
0
1
1
0
Notes
B+off6: Base + SEXT[offset6]
PC+off9: PC + SEXT[offset9]
*OP2 may be SR2 or SEXT[imm5]
**[15:8] or [7:0] depending on MAR[0]
STB

## Slide 16: Fetch/Parse/Dispatch Next Instruction?
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
PC
IR
uPC
0001
DR
ADD+
0
00
SR1
SR2
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
A, MAR <- PC
PC <- A+2
Loop until memory done
IR <- MEM; goto IR.Op
Notes: FetchNext:
PC->A
A+2->PC, MAR
Loop until memory done
MEM->IR; goto OP[IR]
What about branches?

## Slide 17: More Complex Instruction
ADD DR, SR1, SR2, SR3
Can transform to
  ADD DR1, SR1, SR2
  ADD DR, SR3, DR1
But wastes
  Instruction store (2 instructions)
  Registers (need DR1) (technically, could have reused DR)
  Slows things down
    3 micro ops + 3 micro ops + 2 fetch next (3 micro ops or so each)
      = 12 micro ops

## Slide 18: uCoded Computer
ADD DR, SR1, SR2, SR3???
  Regs[SR1] -> A;
  Regs[SR2] -> B;
  ADD->ALU; ALU->Regs[DR]; ALU->A;
  Regs[SR3] -> B;
  ADD->ALU; ALU->Regs[DR]
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Notes: Animate the micro operations

## Slide 19: What Did CISC Buy You?
CISC == Complex Instruction Set Architecture
Example: ADD DR, SR1, SR2, SR3
  5 micro ops + 1 fetch next
    8 micro ops compared to 12
    Speedup = 12/8 = 3/2 = 1.5
  Big performance improvement, no additional hardware
  Don’t forget Amdahl
Number of registers in opcode doesn’t matter!
Parse variable length instruction while processing instruction
But, at some point RISC (reduced instruction set computing)?
  RISC vs. CISC was a hot topic
  We’ll see why later on

## Slide 20: Microcode -> ISA Explosion
ROM became cheap and fast
  Large microcode store possible
Instructions easy to implement
  Doesn’t cost any additional hardware
ISAs start to accumulate instructions
Instructions quickly get out of hand
  Polynomial solve instruction in VAX
Variable length instructions
Addressing modes
But, need to continue to support those instructions
  Which could be a pain later!

## Slide 21: Why Microcode?

## Slide 22: Why Microcode?
Correctness
  Easier to implement ISA in software rather than hardware
  Why do we write software anyways?
Resources
  Without microcode need
  With microcode need

## Slide 23: Compiler/ISA/MicroArch Interface
…
a = *(m1++) + *(++m2);
…
Program
Programming language
...
ADD DR, MEM[SR1++] + MEM[++SR2]
...
ISA
A<-SR2
SR2,MAR<-A+1
B<-MEM
A, MAR<-SR1
SR1<-A+1
A<-MEM
DR<-A+B
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
Microcode
Machine code
Execution
Compiler
Hardware

## Slide 24: Compiler-ISA/MicroArch Interface
What is compiler’s job and what is microarchitecture’s job?
Early days
  Instructions easy to add
  Compilers bad
  Therefore, instructions more powerful
As time went on
  Compilers got better
  New microarchitectures
  Instructions balanced between compiler ability and ease of implementation
  Not all instructions very simple!
    Floating point
Now, adding more complex, powerful instructions
Notes: 24

## Slide 25: Flexibility + Impact of ISA on microarchitecture
25
Notes: 25

## Slide 26: Stack Machines
Like HP calculators (RPN)
Uses a stack as basic local storage element
  Implicit arguments
“0 address machine”
Still need to be able to read/write memory
  PUSH M
  POP M
Operations occur with no address/argument
26
PUSH 0x100
PUSH 0x104
ADD
POP 0x108
0x100
0x104
0x108
1
2
10
1
2
3
Notes: 26

## Slide 27: Stack Machines on Microcoded Engine
SP can be one of the registers
Can tailor HW to ISA
  Remove A and B (animation)
27
Reg
Memory
MAR
MDR
S
shift
A
B
ALU
PUSH 0x100
PUSH 0x104
ADD
POP 0x108
Stack
SP
Notes: 27

## Slide 28: LC-3b Microcode
MAR<-PC
PC<-PC+2
MDR<-M
R
IR <- MDR
BEN<-IR[11]&N + IR[10]&Z + IR[9]&P
[IR[15:12]]
DR<-SR1+OP2*
setCC
DR<-SR1&OP2*
setCC
DR<-SR1 XOR OP2*
setCC
MAR<-LSHF(ZEXT[IR[7:0]],1)
MDR<-M[MAR]
R7<-PC
R
PC<-MDR
DR<-SHF(SR,A,D,amt4)
setCC
DR<-PC+LSHF(off9,1)
setCC
MAR<-B+off6
MDR<-M[MAR[15:1]’0]
R
DR<-SEXT[BYTE.DATA]
setCC
MAR<-B+LSHF(off6,1)
MDR<-M[MAR]
R
DR<-MDR
setCC
MAR<-B+LSHF(off6,1)
MDR<-SR
R
M[MAR]<-MDR
MAR<-B+off6
MDR<-SR[7:0]
R
M[MAR]<-MDR**
[IR[11]]
R7<-PC
PC<-BaseR
R7<-PC
PC<-PC+LSHF(off11,1)
PC<-BaseR
PC<-PC+LSHF(off9,1)
[BEN]
18
18
18
18
18
18
18
18
18
19
18
18
18
18
ADD
AND
XOR
TRAP
SHF
LEA
LDB
LDW
STW
JSR
JMP
BR
18,19
33
35
1
5
9
15
28
30
13
14
2
6
7
3
4
12
0
0
1
1
0
Notes
B+off6: Base + SEXT[offset6]
PC+off9: PC + SEXT[offset9]
*OP2 may be SR2 or SEXT[imm5]
**[15:8] or [7:0] depending on MAR[0]
STB
Fetch?
Parse?
How parsed?

## Slide 29: Can This State Machine Actually Be Implemented in the Lecture Micro-Architecture?
29
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
Notes: No, because PC cannot be sent to MAR at the same time it is incremented. There is a single bus. Thus, the PC <- PC + 2 would take another state.

## Slide 30: Additional Control HW
S
shift
D-Memory
MAR
MDR
A
B
ALU
Regs
Control
30
PC
IR
A
B
ALU

## Slide 31: Multi-Ported Register File (2 Read/1Write)
31
S
shift
Memory
MAR
MDR
A
B
ALU
Regs
Benefits?
Need 3 ported Muxes?

## Slide 32: Implementing Microcode: Microcode Store
next
Datapath ctl
MAR
MDR
MemEn
MemRW
RegRW
A
B
ALUOp[2]
S
SHFT[3]
ALUOp[1]
ALUOp[0]
SHFT[2]
SHFT[1]
SHFT[0]
BusEnable?
NextState?
uPC
What is missing?
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
(LC-3b uses logic)
RegAddr
Notes: BusEnables are missing.
How do we get to the next state?

## Slide 33: Control
MAR<-PC
PC<-PC+2
MDR<-M[MAR]
R
IR <- MDR
BEN<-IR[11]&N + IR[10]&Z + IR[9]&P
[IR[15:12]]
MAR<-B+LSHF(off6,1)
MDR<-M[MAR]
R
DR<-MDR
setCC
18
LDW
18,19
33
35
6
uPC
Logic
n
p
z
IR
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
25
27
32
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
25
33
27
18
35
32
PC
LDW
DR
offset6
ADD
DR
SR
SR
LDW
DR
offset6
4
6
Microcode
Memory

## Slide 34: Table Representation of Memory-Based State Machine
Name | Actions | Next
START | PC <- 0 | Goto FETCH_NEXT
FETCH_NEXT | PC <- PC+2 | Goto FETCH
FETCH | MAR <- PC | Goto GET_INST
GET_INST | IR <- MEM | Goto DISPATCH
DISPATCH | --------- | Goto (IR.Op << 3)

## Slide 35: Adding Realism: Multiple ADDs How To Implement?
0001
DR
ADD+
0
00
0001
DR
1
SR1
SR2
imm5
SR1
ADD+
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0

## Slide 36: Adding Realism: Multiple ADDs How To Implement?
If (bit[5] == 0)
  REGS[DR] = REGS[SR1] + REGS[SR2];
Else
  REGS[DR] = REGS[SR1] + SEXT(imm5);
Setcc();
0001
DR
ADD+
0
00
0001
DR
1
SR1
SR2
imm5
SR1
ADD+
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
How to implement?
Mux second argument
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control

## Slide 37: Got here

## Slide 38: Branch (BRn LABEL)?
Regs
Memory
MAR
MDR
S
shift
A
B
ALU
Control
PC
Condition codes?
IR
uPC
Notes: If (n == 1) then goto T else goto FetchNext
T:
PC->A
Offset->B
A+B->PC; goto FetchNext

## Slide 39: Implementing ISA Branch using Microcode Branches
ISA branch sets PC differently, based on branch and condition
ISA can either have
  Two branch destinations
    If <conditional code> goto branch1 else goto branch2
  One branch destination and fall-through
    If <conditional code> goto branch else goto next_inst
Another tradeoff
  More microbranch destinations
  Or, more microinstructions
Note: microcode branches are the same, just at a lower level
  Set uPC differently, depending on branch and condition

## Slide 40: Additional Goto Field
next
Datapath
MAR
MDR
MemEn
MemRW
RegRW
A
B
ALUOp[2]
S
SHFT[3]
ALUOp[1]
ALUOp[0]
SHFT[2]
SHFT[1]
SHFT[0]
BusEn[3:0]
Control
N
Z
P
IR
PC
next

## Slide 41: Dual-Semantic Fields
next
MAR
MDR
MemEn
MemRW
RegRW
A
B
ALUOp[2]
S
SHFT[3]
ALUOp[1]
ALUOp[0]
SHFT[2]
SHFT[1]
SHFT[0]
BusEn[3:0]
Control
N
Z
P
IR
PC
next

## Slide 42: Control for Handling Branches
uPC
Logic
Datapath control
n
p
z
IR
Is Logic needed?
Does logic need PC?
Notes: No, can implement logic as lookup as well.
No, logic does not need PC

## Slide 43: Any Problems?
0001
SR1
ADD+
0
00
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
0001
DR
1
DR
SR2
imm5
SR1
ADD+
0101
SR2
AND+
0
00
0101
DR
1
SR1
DR
imm5
SR1
AND+
Notes: Fields have been changed. Moving second ADD to have “1” in bit 8 instead of bit 5 creates ambiguity. Careful mapping of fields makes parsing possible and easier

## Slide 44: What Did We Learn?
Microcoded microarch
  Simple and area efficient
  Just a big state machine for controlling minimal components
  Different instructions are different state chains
  Always go back to parse next
Flexible
  Can add instructions easily
  Can even support “incompatible” ISAs
A great way to start thinking about implementation
  Clear and simple
  Lots of room for improvement