## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 5
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Outline
Previously:
  Microcoded Processor Design
  Simple Pipelining
Today:
  Challenges in pipelining
  Branch prediction

## Slide 3: So far, added ports, and concept of pipeline
3
I-Memory
MAR
S
shift
D-Memory
MAR
MDR
A
B
ALU
Regs
Control
PC
IR
A
B
ALU

## Slide 4: Pipelining
Improve throughput by using otherwise unutilized hardware
  More hardware active at any given time

## Slide 5: A Little More Accurate View of Pipelined Processors
F
F
D
E
M
W
F
D
E
M
W
D
E
M
W

## Slide 6
MAR<-PC
PC<-PC+2
MDR<-M
R
IR <- MDR
BEN<-IR[11]&N + IR[10]&Z + IR[9]&P
[IR[15:12]]
DR<-SR1+OP2*
setCC
DR<-SR1&OP2*
setCC
DR<-SR1 XOR OP2*
setCC
MAR<-LSHF(ZEXT[IR[7:0]],1)
MDR<-M[MAR]
R7<-PC
R
PC<-MDR
DR<-SHF(SR,A,D,amt4)
setCC
DR<-PC+LSHF(off9,1)
setCC
MAR<-B+off6
MDR<-M[MAR[15:1]’0]
R
DR<-SEXT[BYTE.DATA]
setCC
MAR<-B+LSHF(off6,1)
MDR<-M[MAR]
R
DR<-MDR
setCC
MAR<-B+LSHF(off6,1)
MDR<-SR
R
M[MAR]<-MDR
MAR<-B+off6
MDR<-SR[7:0]
R
M[MAR]<-MDR**
[IR[11]]
R7<-PC
PC<-BaseR
R7<-PC
PC<-PC+LSHF(off11,1)
PC<-BaseR
PC<-PC+LSHF(off9,1)
[BEN]
18
18
18
18
18
18
18
18
18
19
18
18
18
18
ADD
AND
XOR
TRAP
SHF
LEA
LDB
LDW
STW
JSR
JMP
BR
18,19
33
35
1
5
9
15
28
30
13
14
2
6
7
3
4
12
0
0
1
1
0
STB
I-Memory
MAR
S
shift
D-Memory
MAR
MDR
A
B
ALU
Regs
Control
PC
IR
A
B
ALU
Fetch
Memory
Decode
Execute
Writeback

## Slide 7: Pipeline Execution Diagram
      time -->
Insts t0 t1 t2 t3 t4 t5 t6 t7 . . . .
Inst1 IF1 ID1 EX1 MA1 WB1
Inst2 IF2 ID2 EX2 MA2 WB2
Inst3 IF3 ID3 EX3 MA3 WB3
Inst4 IF4 ID4 EX4 MA4 WB4
Inst5 IF5 ID5 EX5 MA5 WB5
0x2
addr
inst
Instruction
Memory
Add
rd1
GPR File
rs1
rs2
ws
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
A
B
Y
R
IR
MD1
MD2
instruction decode & register ALU memory access write
fetch read -back
(IF) (ID) (EX) (MA) (WB)

## Slide 8: Resource Usage Diagram
    time -->
resources t0 t1 t2 t3 t4 t5 t6 t7 . . . .
  IF I1 I2 I3 I4 I5
  ID I1 I2 I3 I4 I5
  EX I1 I2 I3 I4 I5
  MA I1 I2 I3 I4 I5
  WB I1 I2 I3 I4 I5
0x2
addr
inst
Instruction
Memory
Add
rd1
GPR File
rs1
rs2
ws
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
A
B
Y
R
IR
MD1
MD2
instruction decode & register ALU memory access write
fetch read -back
(IF) (ID) (EX) (MA) (WB)

## Slide 9: Pipelined Instruction Interaction
Structural dependency (structural hazard)
  two instructions in pipeline need same resource
Data dependency (data hazard)
  instruction produces value needed by later instructions
Control dependency (control hazard)
  Instruction determines what next instruction is
    Branches
      Condition codes
    Traps
Dependencies sometimes called Hazards

## Slide 10: Reusing Resources (Memory) in a Pipeline Princeton-style Architecture
    time -->
resources t0 t1 t2 t3 t4 t5 t6 t7. . .
IF/MA I1 I2 I3 I1 I2 I3
ID I1 I2 I3
EX I1 I2 I3
WB I1 I2 I3
I4 cannot
be initiated
until t6 because
of a structural
hazard!
0x2
addr
inst
Instruction
Memory
Add
rd1
GPR File
rs1
rs2
ws
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
A
B
Y
R
IR
MD1
MD2
instruction decode & register ALU memory access write
fetch read -back
(IF) (ID) (EX) (MA) (WB)
the same.
(mem at MA)

## Slide 11: Resolving Structural Hazards Princeton-style Architecture
IR
inst
Instruction
Memory
rd1
GPR File
rs1
rs2
ws
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
1
3
we
A
B
MD1
Y
MD2
IR
IR
R
IR
nop
0x2
addr
Add
PC
Using
Mem ?
stall- fetch
    time -->
resources t0 t1 t2 t3 t4 t5 t6 t7 t8 t9 t10 t11 . . .
IF/MA I1 I2 I3 I1 I2 I3 I4 I5 I6 I4 I5 I6
ID I1 I2 I3 nop nop nop I4 I5 I6 nop nop
EX I1 I2 I3 nop nop nop I4 I5 I6 nop
WB I1 I2 I3 nop nop nop I4 I5 I6
CPI = 6 cycles / 3 instructions = 2 can we do better?

## Slide 12: Data Dependency Example
0x2
addr
inst
Instruction
Memory
Add
rd1
GPR File
rs1
rs2
ws
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
A
B
MD1
Y
MD2
IR
IR
IR
IR
R
...
r1 <-- r0 + 10
r4 <-- r1 + 17
...
Oops!

## Slide 13: Resolving Data Dependencies
Interlocks
  freeze earlier part of pipeline until data is available
Bypass
  if data is available somewhere in processor (but not written back yet), provide additional path to get that data

## Slide 14: Fixing Data Dependencies: Interlocks
...
r1 <-- r0 + 10
r4 <-- r1 + 17
...
0x2
addr
inst
Instruction
Memory
Add
rd1
GPR File
rr1
rr2
wr
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
A
B
MD1
Y
MD2
IR
IR
IR
IR
R
?
nop
Notes: This is as far as I got in Spring 2006

## Slide 15: Stalled Stages and Pipeline Bubbles
      time -->
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) r1 <-- r0 + 10 IF1 ID1 EX1 MA1 WB1
(I2) r4 <-- r1 + 17 IF2 ID2 ID2 ID2 ID2 EX2 MA2 WB2
(I3) IF3 IF3 IF3 IF3 ID3 EX3 MA3 WB3
(I4) stalled stages IF4 ID4 EX4 MA4 WB4
(I5) IF5 ID5 EX5 MA5 WB5
  time -->
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I3 I3 I3 I4 I5
ID I1 I2 I2 I2 I2 I3 I4 I5
EX I1 nop nop nop I2 I3 I4 I5
MA I1 nop nop nop I2 I3 I4 I5
WB I1 nop nop nop I2 I3 I4 I5
        nop: pipeline bubble
Resource
Usage

## Slide 16: Bypassing
      time -->
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) r1 <-- r0 + 10 IF1 ID1 EX1 MA1 WB1
(I2) r4 <-- r1 + 17 IF2 ID2 ID2 ID2 ID2 EX2 MA2 WB2
(I3) IF3 IF3 IF3 IF3 ID3 EX3 MA3 WB3
(I4) stalled stages IF4 ID4 EX4 MA4 WB4
(I5) IF5 ID5 EX5 MA5 WB5
      time -->
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) r1 <-- r0 + 10 IF1 ID1 EX1 MA1 WB1
(I2) r4 <-- r1 + 17 IF2 ID2 EX2 MA2 WB2
(I3) IF3 ID3 EX3 MA3 WB3
(I4) IF4 ID4 EX4 MA4 WB4
(I5) IF5 ID5 EX5 MA5 WB5
Is result of I1 available in time for I2 ?
If the result of I1 is available in time can we get it to I2 ?
If we can then some pipeline bubbles can be eliminated.

## Slide 17: Adding Bypasses
    ...
(I1) r1 <-- r0 + 10
(I2) r4 <-- r1 + 17
    ...
0x2
addr
inst
Instruction
Memory
Add
rd1
GPR File
rr1
rr2
wr
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
A
B
MD1
Y
MD2
IR
IR
IR
IR
R
bypass
?
I1
I2
Input == Output?
Of course you can add many
more bypasses!

## Slide 18: (Data) Dependencies (Hazards)
R == Read
W == Write
A == After
RAW
WAR?
WAW?
RAR?

## Slide 19: Conditional Branches
addr
inst
Instruction
Memory
rd1
GPR File
rr1
rr2
wr
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
0x2
Add
A
B
MD1
Y
MD2
IR
IR
IR
IR
R
M
Add
I2
I1
I1 098 ADD
I2 100 BRnzp 200
I3 102 XOR
I4 302 LDW
What’s Wrong?
NOP
Killed
Notes: 19

## Slide 20: Conditional Branches
addr
inst
Instruction
Memory
rd1
GPR File
rr1
rr2
wr
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
0x2
Add
A
B
MD1
Y
MD2
IR
IR
IR
IR
R
M
Add
I2
I1
I1 098 ADD
I2 100 BRn 200
I3 102 XOR KILLED
I4 104 STW KILLED
I5 302 LDW
Add
What’s Wrong?
Missing some stuff
See last slide and
add yourself
Notes: 20

## Slide 21: Branch Resolution Review
When do you know an instruction is a branch?
  Decode stage
  Might as well fetch next instruction
    Simplest form of branch prediction
When is a conditional branch resolved?
  Might not be resolved until previous instruction executed
    Until previous ALU/memory operation completed
    Might have to wait until ALU/memory stage!
Notes: 21

## Slide 22: Using Wasted Pipeline Slots
In pipelined machine, make a decision and go with it
  Branch prediction/speculation
  If you are wrong, clean up (kill instructions)
Mis-speculated branches create bubbles
  Wastes a pipeline slot
Any way to avoid wasting work???
Delay Slots/Branches
  Make branch decision when it’s possible to make the decision
  Potentially wasted instruction slots always executed
    Not the way an ISA “traditionally” works (one instruction completed before the next one starts)
Notes: 22

## Slide 23: Semantics of Delay slots
        time -->
instructions t0 t1 t2 t3 t4 t5 t6 t7 . . . .
I1 098: stw … IF1 ID1 EX1 MA1 WB1
I2 100: jump 200 IF2 ID2 EX2 MA2 WB2
I3 102: add ... IF3 ID3 EX3 MA3 WB3 kill !
I4 302: ldw ... IF4 ID4 EX4 MA4 WB4
I5 304: xor ... IF5 ID5 EX5 MA5 WB5
ISA semantics: no delay jumps
        time -->
instructions t0 t1 t2 t3 t4 t5 t6 t7 . . . .
I1 098: stw ... IF1 ID1 EX1 MA1 WB1
I2 100: jump 200 IF2 ID2 EX2 MA2 WB2
I3 102: nop ... IF3 ID3 EX3 MA3 WB3 delay slot!
I4 302: ldw ... IF4 ID4 EX4 MA4 WB4
I5 304: xor ... IF5 ID5 EX5 MA5 WB5
ISA semantics : delayed jumps
Notes: 23

## Slide 24: Delay Slots
Original code
98: R2 = R4 + R5
100: R0 = R1 - R2
102: R3 = R4 * R5
104: BRn 200
306: R0 = R3 & R4
1 Delay slot
98: R2 = R4 + R5
100: R3 = R4 * R5
102: BRn 200
104: R0 = R1 - R2
304: R0 = R3 & R4
24
Notes: 24

## Slide 25: More Delay Slots
2 Delay slots
Original code
98: R2 = R4 + R5
100: R0 = R1 - R2
102: R3 = R4 * R5
104: BRn 200
306: R0 = R3 & R4
25
Notes: 25

## Slide 26: Delay Slots
2 Delay slots
98: R3 = R4 * R5
100: BRn 200
102: R2 = R4 + R5
104: R0 = R1 - R2
302: R0 = R3 & R4
Original code
98: R2 = R4 + R5
100: R0 = R1 - R2
102: R3 = R4 * R5
104: BRn 200
306: R0 = R3 & R4
26
Notes: 26

## Slide 27: Even More Delay Slots?
3 Delay slots?
98: R3 = R4 * R5
100: BRn 200
102: R2 = R4 + R5
104: R0 = R1 - R2
NOP
302: R0 = R3 & R4
Original code
98: R2 = R4 + R5
100: R0 = R1 - R2
102: R3 = R4 * R5
104: BRn 200
306: R0 = R3 & R4
27
Notes: 27

## Slide 28: Even More Delay Slots?
Variable Delay slots
  “Prepare to branch”
  Specify number of delay slots in instruction
  Complications?
98: R3 = R4 * R5
100: BRn 200, 2
102: R2 = R4 + R5
104: R0 = R1 - R2
302: R0 = R3 & R4
Original code
98: R2 = R4 + R5
100: R0 = R1 - R2
102: R3 = R4 * R5
104: BRn 200
306: R0 = R3 & R4
28
Notes: 28

## Slide 29: Delay Slots: Architectural Analysis
Why have delay slots?
  hint: Consider instruction issue opportunities assuming 20% of instructions are branches
Delay slot tradeoffs
  use less/more hardware?
  simplifies/complicates control logic?
  affects clock time?
  simplifies/complicates ISA spec & programming?
Are they a good idea?
Split branches:
  Compute target
  Independent instructions
  Transfer control
29
Notes: 29

## Slide 30: Branch Prediction
Delay slots expose microarch considerations as architecture
Alternative: try to guess branches

## Slide 31: Branches in Modern Processors
IF
D0
D1
EX
MEM
WB
Branches not fully
resolved until EX
stage (dependencies)
If branches occur
every 6 or so
instructions, how
much of the pipeline
can be used?
Is superscalar/
superpipelining worth
it?

## Slide 32: Branch Target?
How do we determine the target of a branch?
  Past behavior
  How do we keep past behavior?
Where do we store past behavior?
  One possibility, doubles instruction read bandwidth
    Need to update
instruction word
Instruction
Memory
Branch target

## Slide 33: GOT HERE

## Slide 34: Branch Target Buffer
Often highly associative
IMEM
PC
k
entry PC
predicted
target
=
match
target

## Slide 35: How Does BTB Work?
Fetch accesses BTB
If BTB hits
  Need to determine whether to take branch: How?
Else
  next PC
What is BTB updated with?
  Only taken branches, next PC can be computed

## Slide 36: Static Branch Prediction
Rules of Thumb
  50% forward branches taken (if-then)
  90% of backward branches taken (loops)
Heuristics used by compiler to statically predict direct of branch
ISA can allow compiler to indicate probable direction of branch
  Motorola 88110
Can we use this in BTB?
  IBM RS/6000 passed conditional information to BTB as soon as possible to minimize branch stalls/maximize branch accuracy

## Slide 37: Branch Prediction Based on Branch History
Add one bit to processor state remembering if last branch was taken
  branch prediction (BP) bit
Guess branch direction based on BP bit
  Useful in simple loop
  When is it harmful in a loop?
2 bits?
  change after 2 consecutive mistakes?

## Slide 38: An Example of 2b Saturating Branch Prediction
Record the history of branches taken in BP bits and
use them to guess the branch direction
pred
taken
pred
taken
pred
taken
pred
taken
taken
taken
taken
taken
taken
taken
taken
taken
A single set of BP bits can be associated with the
entire program or with an individual instruction
One possible strategy

## Slide 39: Branch History Table
Whenever branch resolved, BP bits updated
Collisions possible (direct-mapped cache)
  important?
BPb
instruction word
Instruction Memory
PC
BP Buffer (2k entries)
k
Note: BP terms are poorly defined

## Slide 40: Combine BTB with BP bits?
If match fails, PC++ fetched
  eliminates false collisions
Consequences if no cache tag?
IMEM
BPb
PC
Branch Target Buffer (2k entries)
k
entry PC
predicted
target
=
match
target
BP

## Slide 41: What happens if we guess incorrectly?
Effects of speculative execution must be removed
  Use precise interrupt mechanism (ROB)
    Makes mechanism almost essential for modern microprocessors
  Mispredicted branch like branch caused an exception
    Kill instructions, including branch, re-execute branch
Hold off speculated instructions from modifying processor state

## Slide 42: Limitations on Speculative Execution
Speculation cannot go on forever
  hardware resources needed to keep state until branch fully resolved
  limit to total speculation before pipeline stalled
Still should try to limit number of branches
  software techniques
How good is the branch predictor?
  Latest greatest can get it right ~97+% of the time
    But much lower in some cases
  How can that be possible?

## Slide 43: Improve with Branch History
Branches are often correlated
  Direction of one branch determines another
  x = 0
  If (Condition1) x = 3
  If (Condition2) y = 19
  If (x <= 0) z = 13
  Condition1 branch not taken means (x <=0) branch taken

## Slide 44: Branch History: Patterns
Branch history can also capture patterns that are short enough to fit into the BHR
      For (i = 0; i < 4; ++i) {
        *a++ = 0;
      }
Correct pattern for PC == X is TTTN
  So, if you see TTT at PC == X, what should you predict?
Ideally, for each branch keep all possible histories and expected outcome
  impractical
R0 = 0
Label: *a = 0
a = a + 4
R0 = R0 + 1
cc = (R0 < 4)
X: BRcc Label

## Slide 45: Two-Level Prediction: Yeh and Patt
Branch history and branch address combined to index into Pattern History Table (PHT) of 2b saturating BPs
  2b used to predict branch direction
  When branch resolved, update 2b
1
1
0
0
1
1
1
PHT (2b)
BHR
[Yeh+, MICRO 1991]
1
0

## Slide 46: Global or Local BHR?
Global
  One register, much smaller
  Tracks global behavior
Local
  Requires multiple BHR
    Forms a Branch History Table (BHT)
  Can better track local behavior
  Faster convergence
  Used by Intel P6
1
1
0
0
1
0
1
PHT (2b)
1
0
1
0
1
1
0
0
BHT
1
1
0
0
1
1
1
0
0
1
1
1
0
0
1

## Slide 47: Alternate Implementations of Two-level Prediction
[Yeh+, ISCA 1992]

## Slide 48: Handling BHR Aliasing
BHR aliasing a big problem
  Combine with Br Addr
1
1
0
0
1
1
0
1
1
PHT (2b)
1
0
1
0
1
1
0
0
BHR
Branch Address
[Scott McFarling, 1993]
GSELECT
GSHARE

## Slide 49: How good does branch prediction need to be?
Misprediction penalty can be large (tens of cycles)
  Tied to pipeline depth
A few percentage improvement in branch prediction accuracy leads to much higher speed up
Will cover more modern branch predictors later in the semester if we have time!