## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 6
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Recap: Pipeline Execution Diagram
      time -->
Insts t0 t1 t2 t3 t4 t5 t6 t7 . . . .
Inst1 IF1 ID1 EX1 MA1 WB1
Inst2 IF2 ID2 EX2 MA2 WB2
Inst3 IF3 ID3 EX3 MA3 WB3
Inst4 IF4 ID4 EX4 MA4 WB4
Inst5 IF5 ID5 EX5 MA5 WB5
0x2
addr
inst
Instruction
Memory
Add
rd1
GPR File
rs1
rs2
ws
wd
rd2
we
Immed.
Extend
M
0
2
raddr
waddr
wdata
rdata
re
Data
Memory
ALU
algn
1
3
we
PC
A
B
Y
R
IR
MD1
MD2
instruction decode & register ALU memory access write
fetch read -back
(IF) (ID) (EX) (MA) (WB)

## Slide 3: Recap: Pipelined Instruction Interaction
Structural dependency (structural hazard)
  two instructions in pipeline need same resource
Data dependency (data hazard)
  instruction produces value needed by later instructions
Control dependency (control hazard)
  Instruction determines what next instruction is
Causes interlocks (stalls) in pipeline
  Bypassing can help with some data hazards
  Delay slots and branch prediction can help with control hazards

## Slide 4: Branch Prediction
Delay slots expose microarch considerations as architecture
Alternative: try to guess branches

## Slide 5: Branches in Modern Processors
IF
D0
D1
EX
MEM
WB
Branches not fully
resolved until EX
stage (dependencies)
If branches occur
every 6 or so
instructions, how
much of the pipeline
can be used?
Is superscalar/
superpipelining worth
it?

## Slide 6: Branch Target?
How do we determine the target of a branch?
  Past behavior
  How do we keep past behavior?
Where do we store past behavior?
  One possibility, doubles instruction read bandwidth
    Need to update
instruction word
Instruction
Memory
Branch target

## Slide 7: Branch Target Buffer
Often highly associative
IMEM
PC
k
entry PC
predicted
target
=
match
target

## Slide 8: How Does BTB Work?
Fetch accesses BTB
If BTB hits
  Need to determine whether to take branch: How?
Else
  next PC
What is BTB updated with?
  Only taken branches, next PC can be computed

## Slide 9: Static Branch Prediction
Rules of Thumb
  50% forward branches taken (if-then)
  90% of backward branches taken (loops)
Heuristics used by compiler to statically predict direct of branch
ISA can allow compiler to indicate probable direction of branch
  Motorola 88110
Can we use this in BTB?
  IBM RS/6000 passed conditional information to BTB as soon as possible to minimize branch stalls/maximize branch accuracy

## Slide 10: Branch Prediction Based on Branch History
Add one bit to processor state remembering if last branch was taken
  branch prediction (BP) bit
Guess branch direction based on BP bit
  Useful in simple loop
  When is it harmful in a loop?
2 bits?
  change after 2 consecutive mistakes?

## Slide 11: An Example of 2b Saturating Branch Prediction
Record the history of branches taken in BP bits and
use them to guess the branch direction
pred
taken
pred
taken
pred
taken
pred
taken
taken
taken
taken
taken
taken
taken
taken
taken
A single set of BP bits can be associated with the
entire program or with an individual instruction
One possible strategy

## Slide 12: Branch History Table
Whenever branch resolved, BP bits updated
Collisions possible (direct-mapped cache)
  important?
BPb
instruction word
Instruction Memory
PC
BP Buffer (2k entries)
k
Note: BP terms are poorly defined

## Slide 13: Combine BTB with BP bits?
If match fails, PC++ fetched
  eliminates false collisions
Consequences if no cache tag?
IMEM
BPb
PC
Branch Target Buffer (2k entries)
k
entry PC
predicted
target
=
match
target
BP

## Slide 14: What happens if we guess incorrectly?
Effects of speculative execution must be removed
  Use precise interrupt mechanism (ROB)
    Makes mechanism almost essential for modern microprocessors
  Mispredicted branch like branch caused an exception
    Kill instructions, including branch, re-execute branch
Hold off speculated instructions from modifying processor state

## Slide 15: Limitations on Speculative Execution
Speculation cannot go on forever
  hardware resources needed to keep state until branch fully resolved
  limit to total speculation before pipeline stalled
Still should try to limit number of branches
  software techniques
How good is the branch predictor?
  Latest greatest can get it right ~97+% of the time
    But much lower in some cases
  How can that be possible?

## Slide 16: Improve with Branch History
Branches are often correlated
  Direction of one branch determines another
  x = 0
  If (Condition1) x = 3
  If (Condition2) y = 19
  If (x <= 0) z = 13
  Condition1 branch not taken means (x <=0) branch taken

## Slide 17: Branch History: Patterns
Branch history can also capture patterns that are short enough to fit into the BHR
      For (i = 0; i < 4; ++i) {
        *a++ = 0;
      }
Correct pattern for PC == X is TTTN
  So, if you see TTT at PC == X, what should you predict?
Ideally, for each branch keep all possible histories and expected outcome
  impractical
R0 = 0
Label: *a = 0
a = a + 4
R0 = R0 + 1
cc = (R0 < 4)
X: BRcc Label

## Slide 18: Two-Level Prediction: Yeh and Patt
Branch history and branch address combined to index into Pattern History Table (PHT) of 2b saturating BPs
  2b used to predict branch direction
  When branch resolved, update 2b
1
1
0
0
1
1
1
PHT (2b)
BHR
[Yeh+, MICRO 1991]
1
0

## Slide 19: Global or Local BHR?
Global
  One register, much smaller
  Tracks global behavior
Local
  Requires multiple BHR
    Forms a Branch History Table (BHT)
  Can better track local behavior
  Faster convergence
  Used by Intel P6
1
1
0
0
1
0
1
PHT (2b)
1
0
1
0
1
1
0
0
BHT
1
1
0
0
1
1
1
0
0
1
1
1
0
0
1

## Slide 20: Alternate Implementations of Two-level Prediction
[Yeh+, ISCA 1992]

## Slide 21: Handling BHR Aliasing
BHR aliasing a big problem
  Combine with Br Addr
1
1
0
0
1
1
0
1
1
PHT (2b)
1
0
1
0
1
1
0
0
BHR
Branch Address
[Scott McFarling, 1993]
GSELECT
GSHARE

## Slide 22: How good does branch prediction need to be?
Misprediction penalty can be large (tens of cycles)
  Tied to pipeline depth
A few percentage improvement in branch prediction accuracy leads to much higher speed up
Will cover more modern branch predictors later in the semester if we have time!

## Slide 23: SIMD (original style) – single instruction multiple data
sequencer
memory hierarchy
Local Mem
Local Mem
Local Mem
Local Mem

## Slide 24: SIMD (vector style) – aka DLP (data-level parallelism)
sequencer
memory hierarchy
Local Mem
Local Mem
Local Mem
Local Mem

## Slide 25: More on vectors later
Extremely efficient architecture
Very prominent in lots of applications
  Scientific
  Media
  Graphics
  Machine learning
  …

## Slide 26: Multiple-Functional Units
Desire other operations
  floating point
  multi-cycle integer
  Load/store
  Branch
Don’t want them to all take the same amount of time
Multiple functional units = potential parallelism!
  can we run them simultaneously?
  does running them simultaneously have any performance benefit?
  what issues arise?
26
Notes: 26

## Slide 27: GOT HERE

## Slide 28: VLIW (Very Long Instruction Word)
Complexity?
Arch/uArch?
sequencer
memory hierarchy

## Slide 29: Superscalar (ILP)
Just uArch!
How is this done?
scheduler
sequencer
memory hierarchy

## Slide 30: Multiple-Functional Units
Desire other operations
  floating point
  multi-cycle integer
  Load/store
  Branch
Don’t want them to all take the same amount of time
Multiple functional units = potential parallelism!
  can we run them simultaneously?
  does running them simultaneously have any performance benefit?
  what issues arise?
30
Notes: 30

## Slide 31: Multiple Function Unit Datapath
31
IF
ID/
Reg
SCIU
BPU
FPU
MCIU
LSU
WB
SCIU = single cycle
integer unit
BPU = branch
processing unit
FPU = floating-point
unit
MCIU = multiple-cycle
integer unit
LSU = load-store unit
Functional units pipelined,
Partially pipelined, unpipelined
Different latencies (variable)
Issues?
Notes: 31

## Slide 32: New Dependencies/Hazards
Structural hazards at
  Write-back from variable latency functional units
  Functional units themselves?
Data Dependencies: R == Read, W == Write, A == After
  RAW
  WAR
  WAW
  RAR?
WAW hazards due to different FU latencies
  Will discuss WAR later
General solution?
  All hazards can still be resolved by interlocks
  when/how can interlocks be avoided is the question

## Slide 33: Structural Hazard at WB
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
r0 = r4 opmciu r3
r1 = r5 opsciu r5
r2 = r3 opsciu r7

## Slide 34: Variable Latency Issues: WB structural hazard
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
f0 = f1 opfpu f2
r0 = r4 opsciu r3
r1 = r5 opsciu r5

## Slide 35: Avoiding WB structural hazard
Provide more write-backs
  could provide maximum number (number of FUs)
  practical? implications? (register file)
Interlocks
  decode time?
  at WB stage?
    flow-control on functional units

## Slide 36: Unpipelined/Variable Latency Issues: FU structural hazard
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
r0 = r1 opmciu r2
r0 = r4 opmciu r3

## Slide 37: Avoiding FU hazard
Interlocks
  Since desired FU is blocked, and no other will do, instruction must wait
  Blocks instructions after it
Anything better?

## Slide 38: Variable Latency Issues: WAW Hazards
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
r0 = r1 opmciu r2
r0 = r4 opsciu r3

## Slide 39: Fixing WAW hazards
How?
Delay second operation
Don’t bother writing first write (that is available to write after the second write has completed)

## Slide 40: Long Latency / Unresolved Dependency Operations
Does a long latency operation (cache miss, long latency unpipelined ALU) guarantee that IPC will go below 1?
Does an unresolved dependency guarantee that IPC will go below 1?
NO to either!
Key is to keep on issuing instructions
  DON’T BLOCK IF AT ALL POSSIBLE (CANNOT GET BACK)
Anytime instruction is not issued on a cycle performance is guaranteed to be below 1
  Creates a bubble in the pipeline!
  Lesson in networking as well (“Head-of-Line Blocking”)

## Slide 41: In-Order Pipelines
Blocking entire pipeline if instruction stalls drastically reduces potential performance
  r0 = r1 + r2
  r3 = MEM[r0]
  r4 = r3 + r6
  r7 = r5 + r1
An instruction can block instructions behind it
  Even if there are no dependencies to future instructions

## Slide 42: Review
IPC of 1 requires N instructions processed in N cycles
  Which means we need to process an average of 1 instruction per cycle to get IPC == 1
In single issue machine, can issue at most 1 instruction per cycle
  must issue one instruction every cycle to have a chance of getting to IPC == 1
  Otherwise, you have issued (N – X) instructions in N cycles which will always average to less than 1
In other words, how do we avoid blocking?

## Slide 43: Avoiding long-latency cache miss stalls
Blocking entire pipeline if instruction stalls drastically reduces potential performance
  r0 = r1 + r2
  r3 = MEM[r0]
  r4 = r3 + r6
  r7 = r5 + r1
An instruction can block instructions behind it
  Even if there are no dependencies to future instructions
Can compiler fix this problem by reordering?
  r0 = r1 + r2
  r3 = MEM[r0]
  r7 = r5 + r1
  ….
  r4 = r3 + r6
What does this require?
Not a general solution

## Slide 44: Nonblocking caches
Allow operations to continue while servicing a miss
  Which operations?
What hardware is needed?
What is implied?
MSHRs
  Miss status holding/handling registers

## Slide 45: Limitations to Achieving Performance
In-order fetch/decode?
  Not if one can always fetch/decode one instruction per cycle
  What if next instruction cannot be executed (structural/data)?
    Look ahead for instructions that are ready (structural/data)
In-order execution?
  Will block all following instructions unless data is ready?
    What happens with nonblocking caches?
  Hazards create performance divots
    Compiler cannot remove all
    Legacy codes
  Must execute out of order to maintain performance

## Slide 46: In-Order Fetch/Decode, Out-of-Order Execution
Instructions examined and dispatched in order
  Need to maintain dependencies
Instructions executed when ready, regardless of dispatch order
  Stalls can be covered by parallel execution (executing more than one instruction at the same time)
Out-of-order writeback?
How can we implement this?
What new problems crop up?

## Slide 47: Some Terms: not everyone agrees on these terms
Fetch
  read value from instruction memory
Decode
  Translate value into instruction, potentially read ready registers
Dispatch/Issue
  Select functional unit, may buffer instruction, may wait for/read registers
Issue
  Initiate execution in the functional unit
Execute
Finish: finish execution (but don’t yet update arch state)
Complete (sometimes merged with Retire)
  Update architectural state
Retire
  Update memory

## Slide 48: Old and New Hazards Ahead!
Same hazards as for multiple-function units
  Structural hazards at write-back
  Structural hazards at execute stage
  WAW hazards
Potential new hazard: WAR
  Think about how they might occur

## Slide 49: WAR Hazard: How?
  A: f0 = f2 / f4 B: f10 = f0 + f8 C: f8 = f5 - f14
Multiply
Divide
Add
WB
D
F
Reg
File

## Slide 50: WAR Hazard: How?
A starts executing, slow
B stalled waiting for f0
C starts executing, completes before B starts executing
  Wants to writeback f8 before B reads! What to do???
  A: f0 = f2 / f4 B: f10 = f0 + f8 C: f8 = f5 - f14
Multiply
Divide
Add
WB
D
F
Reg
File

## Slide 51: Out-of-Order Execution
Separate structural hazards from data hazards
  one should not block the other
Check for structural hazards at issue
Data hazards resolved before actual execution

## Slide 52: 2 Out-of-Order Instruction Scheduling Techniques
Scoreboarding
  Central table with state of entire execution pipeline
  Registers read right before start of execution
Micro-dataflow (Tomasulo’s algorithm)
  Generally more distributed
  Eliminates a lot of problems (more later)

## Slide 53: Data Hazards Exercise
Where are the data hazards?
  A: f0 = f2 / f4 B: f10 = f0 + f8 C: f8 = f5 - f14 D: f0 = f8 + f14
Multiply
Divide
Add
WB
D
F
Reg
File