## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 7
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Lab 2 posted
  Due 11:59pm, Sep 30
Problem Set 2 posted
  Due 4:59pm, Oct 3
Old exams are posted on course webpage
How are we doing?
  Lectures
    Too fast? Too slow?
  Discussion Sections
  Assignments (Labs and Problem Sets)
  Should we run a survey?

## Slide 3: Recap and Outline
Recap: Branch Prediction
  Branch Target Buffer
  Static prediction
  Dynamic prediction
    2-bit saturating counter
    Two-level adaptive branch prediction
Outline
  Multiple Functional Units
  Scoreboarding for Out-of-Order Execution

## Slide 4: SIMD (original style) – single instruction multiple data
sequencer
memory hierarchy
Local Mem
Local Mem
Local Mem
Local Mem

## Slide 5: SIMD (vector style) – aka DLP (data-level parallelism)
sequencer
memory hierarchy
Local Mem
Local Mem
Local Mem
Local Mem

## Slide 6: VLIW (Very Long Instruction Word)
Complexity?
Arch/uArch?
sequencer
memory hierarchy

## Slide 7: Superscalar (ILP)
Just uArch!
How is this done?
scheduler
sequencer
memory hierarchy

## Slide 8: Multiple-Functional Units
Desire other operations
  floating point
  multi-cycle integer
  Load/store
  Branch
Don’t want them to all take the same amount of time
Multiple functional units = potential parallelism!
  can we run them simultaneously?
  does running them simultaneously have any performance benefit?
  what issues arise?
8
Notes: 8

## Slide 9: Multiple Function Unit Datapath
9
IF
ID/
Reg
SCIU
BPU
FPU
MCIU
LSU
WB
SCIU = single cycle
integer unit
BPU = branch
processing unit
FPU = floating-point
unit
MCIU = multiple-cycle
integer unit
LSU = load-store unit
Functional units pipelined,
Partially pipelined, unpipelined
Different latencies (variable)
Issues?
Notes: 9

## Slide 10: New Dependencies/Hazards
Structural hazards at
  Write-back from variable latency functional units
  Functional units themselves?
Data Dependencies: R == Read, W == Write, A == After
  RAW
  WAR
  WAW
  RAR?
WAW hazards due to different FU latencies
  Will discuss WAR later
General solution?
  All hazards can still be resolved by interlocks
  when/how can interlocks be avoided is the question

## Slide 11: Structural Hazard at WB
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
r0 = r4 opmciu r3
r1 = r5 opsciu r5
r2 = r3 opsciu r7

## Slide 12: Variable Latency Issues: WB structural hazard
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
f0 = f1 opfpu f2
r0 = r4 opsciu r3
r1 = r5 opsciu r5

## Slide 13: Avoiding WB structural hazard
Provide more write-backs
  could provide maximum number (number of FUs)
  practical? implications? (register file)
Interlocks
  decode time?
  at WB stage?
    flow-control on functional units

## Slide 14: Unpipelined/Variable Latency Issues: FU structural hazard
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
r0 = r1 opmciu r2
r0 = r4 opmciu r3

## Slide 15: Avoiding FU hazard
Interlocks
  Since desired FU is blocked, and no other will do, instruction must wait
  Blocks instructions after it
Anything better?

## Slide 16: Variable Latency Issues: WAW Hazards
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
r0 = r1 opmciu r2
r0 = r4 opsciu r3

## Slide 17: Fixing WAW hazards
How?
Delay second operation
Don’t bother writing first write (that is available to write after the second write has completed)

## Slide 18: Long Latency / Unresolved Dependency Operations
Does a long latency operation (cache miss, long latency unpipelined ALU) guarantee that IPC will go below 1?
Does an unresolved dependency guarantee that IPC will go below 1?
NO to either!
Key is to keep on issuing instructions
  DON’T BLOCK IF AT ALL POSSIBLE (CANNOT GET BACK)
Anytime instruction is not issued on a cycle performance is guaranteed to be below 1
  Creates a bubble in the pipeline!
  Lesson in networking as well (“Head-of-Line Blocking”)

## Slide 19: In-Order Pipelines
Blocking entire pipeline if instruction stalls drastically reduces potential performance
  r0 = r1 + r2
  r3 = MEM[r0]
  r4 = r3 + r6
  r7 = r5 + r1
An instruction can block instructions behind it
  Even if there are no dependencies to future instructions

## Slide 20: Review
IPC of 1 requires N instructions processed in N cycles
  Which means we need to process an average of 1 instruction per cycle to get IPC == 1
In single issue machine, can issue at most 1 instruction per cycle
  must issue one instruction every cycle to have a chance of getting to IPC == 1
  Otherwise, you have issued (N – X) instructions in N cycles which will always average to less than 1
In other words, how do we avoid blocking?

## Slide 21: Avoiding long-latency cache miss stalls
Blocking entire pipeline if instruction stalls drastically reduces potential performance
  r0 = r1 + r2
  r3 = MEM[r0]
  r4 = r3 + r6
  r7 = r5 + r1
An instruction can block instructions behind it
  Even if there are no dependencies to future instructions
Can compiler fix this problem by reordering?
  r0 = r1 + r2
  r3 = MEM[r0]
  r7 = r5 + r1
  ….
  r4 = r3 + r6
What does this require?
Not a general solution

## Slide 22: Nonblocking caches
Allow operations to continue while servicing a miss
  Which operations?
What hardware is needed?
What is implied?
MSHRs
  Miss status holding/handling registers

## Slide 23: Limitations to Achieving Performance
In-order fetch/decode?
  Not if one can always fetch/decode one instruction per cycle
  What if next instruction cannot be executed (structural/data)?
    Look ahead for instructions that are ready (structural/data)
In-order execution?
  Will block all following instructions unless data is ready?
    What happens with nonblocking caches?
  Hazards create performance divots
    Compiler cannot remove all
    Legacy codes
  Must execute out of order to maintain performance

## Slide 24: In-Order Fetch/Decode, Out-of-Order Execution
Instructions examined and dispatched in order
  Need to maintain dependencies
Instructions executed when ready, regardless of dispatch order
  Stalls can be covered by parallel execution (executing more than one instruction at the same time)
Out-of-order writeback?
How can we implement this?
What new problems crop up?

## Slide 25: Some Terms: not everyone agrees on these terms
Fetch
  read value from instruction memory
Decode
  Translate value into instruction, potentially read ready registers
Dispatch/Issue
  Select functional unit, may buffer instruction, may wait for/read registers
Issue
  Initiate execution in the functional unit
Execute
Finish: finish execution (but don’t yet update arch state)
Complete (sometimes merged with Retire)
  Update architectural state
Retire
  Update memory

## Slide 26: Old and New Hazards Ahead!
Same hazards as for multiple-function units
  Structural hazards at write-back
  Structural hazards at execute stage
  WAW hazards
Potential new hazard: WAR
  Think about how they might occur

## Slide 27: WAR Hazard: How?
  A: f0 = f2 / f4 B: f10 = f0 + f8 C: f8 = f5 - f14
Multiply
Divide
Add
WB
D
F
Reg
File

## Slide 28: WAR Hazard: How?
A starts executing, slow
B stalled waiting for f0
C starts executing, completes before B starts executing
  Wants to writeback f8 before B reads! What to do???
  A: f0 = f2 / f4 B: f10 = f0 + f8 C: f8 = f5 - f14
Multiply
Divide
Add
WB
D
F
Reg
File

## Slide 29: Data Hazards Exercise
Where are the data hazards?
  A: f0 = f2 / f4
  B: f10 = f0 + f8
  C: f8 = f5 - f14
  D: f0 = f8 + f14
Multiply
Divide
Add
WB
D
F
Reg
File
RAW
WAR
RAW
WAR?

## Slide 30: Out-of-Order Execution
Separate structural hazards from data hazards
  one should not block the other
Check for structural hazards at issue
Data hazards resolved before actual execution

## Slide 31: 2 Out-of-Order Instruction Scheduling Techniques
Scoreboarding
  Central table with state of entire execution pipeline
  Registers read right before start of execution
Micro-dataflow (Tomasulo’s algorithm)
  Generally more distributed
  Eliminates a lot of problems (more later)

## Slide 32: Scoreboarding
Allows instructions to execute out-of-order when necessary resources are available and there are no data dependencies
Every instruction goes through scoreboard
  In Decode/Dispatch/Issue
Structural hazards identified at dispatch time
  Structure is reserved at dispatch time
  Structural hazard stalls entire pipeline
Data dependencies identified at execute time
  Cannot execute until all data dependencies resolved
  data dependency stalls dependent instruction but not pipeline
CDC6600 by Cray
Notes: 32

## Slide 33: Scoreboard placement: Dispatch/Issue Logic
Registers
FP mult
FP mult
FP divide
FP add
Integer
Scoreboard
Data buses
Control and status
F
Notes: 33

## Slide 34: Scoreboard Execution Stages
Dispatch
  if FU/destination register free, dispatch instruction to FU
    Thus, reserving FU/destination register
  else stall entire pipeline
Read operands
  within functional unit, controlled by scoreboard
  when operands available, scoreboard instructs FU to read operands from registers and issue/execute
    registers not read until ready to execute: implications?
Execute
  when FU finished, notifies scoreboard
Write-back
  scoreboard indicates when to write-back
Notes: 34

## Slide 35: Resolving Data Hazards using Scoreboard
RAW
  read delayed until write completed to register
WAR
  write delayed until read completed
WAW
  second write instruction stalled at dispatch, stalling pipeline
Notes: 35

## Slide 36: Scoreboard: FU Status
name busy op dest src1 src2 opsread
  Int
  Mem
  Add
  Mult1
  Mult2
  Div
Each instruction consults/updates the scoreboard
Dispatch check FU/destination register: stall pipeline
Read check dest column for sources
Issue/Execute
Write-back check source columns for destination and
whether they have been read
Notes: 36

## Slide 37: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Registers, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | No |  |  |  |  | 
Mult1 | No |  |  |  |  | 
Mult2 | No |  |  |  |  | 
Div | No |  |  |  |  | 
37
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
Notes: 37

## Slide 38: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Register, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | No |  |  |  |  | 
Mult1 | No |  |  |  |  | 
Mult2 | No |  |  |  |  | 
Div | Yes | / | F0 | F2, ---, y | F4, ---, y | Yes
38
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
Notes: 38

## Slide 39: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Register, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | Yes | - | F10 | F0, Div, n | F8, ---, y | no
Mult1 | No |  |  |  |  | 
Mult2 | No |  |  |  |  | 
Div | Yes | / | F0 | F2, ---, y | F4, ---, y | Yes
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
Notes: 39

## Slide 40: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Register, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | Yes | - | F10 | F0, Div, n | F8, ---, y | no
Mult1 | Yes | * | F8 | F8, ---, y | F14,---, y | Yes
Mult2 | No |  |  |  |  | 
Div | Yes | / | F0 | F2, ---, y | F4, ---, y | Yes
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
What if the next instruction
writes to f0, f10 or f8?
Notes: 40

## Slide 41: Scoreboard Variation: Homework!
Don’t dispatch/issue to functional unit until operands read and issued with instruction
  eliminates WAR
  simplifies scoreboard
  reduces parallelism (why?)
What state is needed?
What does control logic look like?
Similar to our original multiple functional unit architecture
Notes: 41

## Slide 42: Nonblocking caches again
How do we extend the scoreboard with caches?
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
Hit
Miss

## Slide 43: Scoreboarding Review
Allows instructions to execute out-of-order when necessary resources are available and there are no data dependencies
Stalls front of pipeline if
  functional unit busy (deals with FU hazard)
  destination register busy (deals with WAW hazard)
Reads registers immediately before execution
  May need more register read ports
Every register writeback is performed
If pending reads of previous value of register, writeback stalled
  Otherwise, potential for WAR hazard