## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 8
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Survey #2 posted on Canvas (due Friday, 9/25)
  Tell us what you think about lectures and discussion sections

## Slide 3: Recap and Outline
Recap
  Can reduce bubbles by avoiding interlock stalls
    Add resources
    Add bypasses
    Speculate
    Change software
      Delay slots and rescheduling
  Multiple functional units add WAW and structural hazards
  Non-blocking caches
  In-order fetch+decode/dispatch, but out-of-order execution
    Also worry about WAR now
    Lost atomicity of instructions (precise interrupts/exceptions)
Outline
  Scoreboard algorithm
  Tomasulo’s algorithm

## Slide 4: Out-of-Order Execution
Separate structural hazards from data hazards
  one should not block the other
Check for structural hazards at issue
Data hazards resolved before actual execution

## Slide 5: 2 Out-of-Order Instruction Scheduling Techniques
Scoreboarding
  Central table with state of entire execution pipeline
  Registers read right before start of execution
Micro-dataflow (Tomasulo’s algorithm)
  Generally more distributed
  Eliminates a lot of problems (more later)

## Slide 6: Scoreboarding
Allows instructions to execute out-of-order when necessary resources are available and there are no data dependencies
Every instruction goes through scoreboard
  In Decode/Dispatch/Issue
Structural hazards identified at dispatch time
  Structure is reserved at dispatch time
  Structural hazard stalls entire pipeline
Data dependencies identified at execute time
  Cannot execute until all data dependencies resolved
  data dependency stalls dependent instruction but not pipeline
CDC6600 by Cray
Notes: 6

## Slide 7: Scoreboard placement: Dispatch/Issue Logic
Registers
FP mult
FP mult
FP divide
FP add
Integer
Scoreboard
Data buses
Control and status
F
Notes: 7

## Slide 8: Scoreboard Execution Stages
Dispatch
  if FU/destination register free, dispatch instruction to FU
    Thus, reserving FU/destination register
  else stall entire pipeline
Read operands
  within functional unit, controlled by scoreboard
  when operands available, scoreboard instructs FU to read operands from registers and issue/execute
    registers not read until ready to execute: implications?
Execute
  when FU finished, notifies scoreboard
Write-back
  scoreboard indicates when to write-back
Notes: 8

## Slide 9: Resolving Data Hazards using Scoreboard
RAW
  read delayed until write completed to register
WAR
  write delayed until read completed
WAW
  second write instruction stalled at dispatch, stalling pipeline
Notes: 9

## Slide 10: Scoreboard: FU Status
name busy op dest src1 src2 opsread
  Int
  Mem
  Add
  Mult1
  Mult2
  Div
Each instruction consults/updates the scoreboard
Dispatch check FU/destination register: stall pipeline
Read check dest column for sources
Issue/Execute
Write-back check source columns for destination and
whether they have been read
Notes: 10

## Slide 11: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Registers, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | No |  |  |  |  | 
Mult1 | No |  |  |  |  | 
Mult2 | No |  |  |  |  | 
Div | No |  |  |  |  | 
11
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
Notes: 11

## Slide 12: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Register, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | No |  |  |  |  | 
Mult1 | No |  |  |  |  | 
Mult2 | No |  |  |  |  | 
Div | Yes | / | F0 | F2, ---, y | F4, ---, y | Yes
12
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
Notes: 12

## Slide 13: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Register, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | Yes | - | F10 | F0, Div, n | F8, ---, y | no
Mult1 | No |  |  |  |  | 
Mult2 | No |  |  |  |  | 
Div | Yes | / | F0 | F2, ---, y | F4, ---, y | Yes
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
Notes: 13

## Slide 14: Scoreboard FU Status: Dynamically Constructed Dataflow Graph
Name | Busy? | Op | Dest | Source Register, Producer, Ready |  | Read?
Int | No |  |  |  |  | 
Add | Yes | - | F10 | F0, Div, n | F8, ---, y | no
Mult1 | Yes | * | F8 | F8, ---, y | F14,---, y | Yes
Mult2 | No |  |  |  |  | 
Div | Yes | / | F0 | F2, ---, y | F4, ---, y | Yes
  A: f0 = f2 / f4 B: f10 = f0 - f8 C: f8 = f8 * f14
What if the next instruction
writes to f0, f10 or f8?
Notes: 14

## Slide 15: Scoreboard Variation: Homework!
Don’t dispatch/issue to functional unit until operands read and issued with instruction
  eliminates WAR
  simplifies scoreboard
  reduces parallelism (why?)
What state is needed?
What does control logic look like?
Similar to our original multiple functional unit architecture
Notes: 15

## Slide 16: Nonblocking caches again
How do we extend the scoreboard with caches?
IF
ID/
Reg
SCIU
BPU
FPU
MCIU (3 cycles)
LSU
WB
FPU
FPU
Hit
Miss

## Slide 17: Scoreboarding Review
Allows instructions to execute out-of-order when necessary resources are available and there are no data dependencies
Stalls front of pipeline if
  functional unit busy (deals with FU hazard)
  destination register busy (deals with WAW hazard)
Reads registers immediately before execution
  May need more register read ports
Every register writeback is performed
If pending reads of previous value of register, writeback stalled
  Otherwise, potential for WAR hazard

## Slide 18: Micro-Dataflow (Tomasulo) Overview
Same goals as scoreboarding
  In-order fetch/decode, out-of-order execution to improve performance
  Let ready instructions bypass waiting instructions
  Enforce data dependencies (eliminate RAW hazards)
But, more distributed than scoreboarding
  Decisions can be made in distributed reservation stations
Address WAW hazards without stalling
Bake-in bypassing for better performance
Historical
  Robert Tomasulo came up with this algorithm for the IBM 360/91 floating point unit (released in 1966)
  Won the Eckert-Mauchly Award for this algorithm in 1997

## Slide 19: Tomasulo Paper
[https://people.eecs.berkeley.edu/~culler/courses/cs252-s05/papers/tomasulo.pdf]
[IBM Journal 1967]

## Slide 20: Doctor’s Office Analogy

## Slide 21: The Average American Doctor’s Office

## Slide 22: A French Doctor’s Office

## Slide 23: Of Course, You Could Require More Tests: You are Moved to Testing Station
Check
In
Waiting
Room
Doctor1
Test1
Test2
Get
File

## Slide 24: What Does this Have to Do with Computer Architecture? Simplified Tomasulo Pipeline
Fetch
Decode
FU1
FU2
FU3
Reg
Read

## Slide 25: Tomasulo Basic Operation
Fetch/Decode stages put decoded instructions along with any available operands into “reservation station”
  Fetch/Decode still proceed in-order, makes sure ISA semantics are maintained by seeing register usage in-order
  Registers read in-order IF data is available
  Reservation station either has copy of available data or gets data (somehow) while it is being produced
  When all data available, instruction can be executed
In-order Fetch/Decode decoupled from Out-of-Order Execute
Just like French doctor’s office!
  Test results (data) somehow get to patient (instruction), when all test results (data) available, patient can be seen by doctor (instruction can be executed)

## Slide 26: Register File
Each register has a presence bit indicating whether its value is present (valid) or not present (invalid)
If data invalid, value is being computed
  Tag is used as a placeholder for the value until it is computed
When is presence bit set to invalid?
Register file read returns either valid data or a tag
FU1
FU2
FU3
Reg
Read
S2
S0
S6
S1
R0
R1
R2
R3
Valid?
Value/tag
R0
R1
R2
R3
tag
value
valid?

## Slide 27: What Do You Use as a Tag? Register Name?
George Foreman named all 5 sons
“George Edward Foreman”
Name could be aliased!
Solution?
Give a number?

## Slide 28: Same Problem In Computers
A register contains different data at different times (R0)
  R0 = R1 / R2
  R0 = R0 + R5
  R0 = (R0)
  R0 = R0 + R0
Each instance of R0 is really a different variable
  Most of us would not write C code this way
  But, limited number of registers
Could hardware hand out new names? If so, how?

## Slide 29: Register Renaming
Registers dynamically renamed by hardware
  R0 = R1 / R2 RA = R1 / R2
  R1 = R0 + R5 RB = RA + R5
  R0 = (R6) RC = (R6)
Note: didn’t rename all source registers since we don’t know what their renamed names are

## Slide 30: Register Renaming Example
S2
S0
S6
S1
S4
S7
S3
S5
R0
R1
R2
R3
R4
R5
R6
R7
R0 = R1 + R2
R1 = R3 + R0
R0 = R6 + R7
R1 = (R0)
S2
S0
S6
S1
S4
S7
S3
S5
R0
R1
R2
R3
R4
R5
R6
R7
original

## Slide 31: Register Renaming Example
S2
S0
S2
S0
S6
S1
S4
S7
S3
S5
R0
R1
R2
R3
R4
R5
R6
R7
R0 = R1 + R2
R1 = R3 + R0
R0 = R6 + R7
R1 = (R0)
s8 = s0 + s6 ; R0 = s8
s9 = s1 + s8 ; R1 = s9
s10 = s3 + s5 ; R0 = s10
s11 = (s10) ; R1 = s11
S9
S8
S6
S1
S4
S7
S3
S5
R0
R1
R2
R3
R4
R5
R6
R7
original
S10
S11

## Slide 32: Register File
Each register has a presence bit indicating whether it’s value is present (valid) or not present (invalid)
If data invalid, value is being computed
  Tag is used as a placeholder for the value until it is computed
When is presence bit set to invalid?
Register file read returns either valid data or a tag
FU1
FU2
FU3
Reg
Read
S2
S0
S6
S1
R0
R1
R2
R3
Valid?
Value/tag
R0
R1
R2
R3
tag
value
valid?

## Slide 33: Register File Valid?
Set to invalid the moment dispatched as destination
  At that point no following instructions should read the old value
Set to valid during writeback/complete iff tag matches instructions and register file location
  Every instruction must maintain its original destination architectural register name
  Every instruction must maintain its tag

## Slide 34: More Registers without More Registers?
Rename registers effectively increase number of usable registers without increasing number of bits in instruction
  not quite as good. why?
Need some way to “reclaim” registers
Potential performance hit?

## Slide 35: Renaming and Hazards
Do WAW/WAR hazards occur after rename?
  No!
  New name (tag) for every register written
    Dependence based on tag, not register name
  Rename eliminates all hazards by renaming all destination registers and using new names for real dependencies
What if you run out of rename names?
  Standard solution (stall)

## Slide 36: Tomasulo Register Renaming Algorithm Intentional Error!
Dispatch in order
Dispatch (to RS) has a register rename table
  One entry per architectural register
  RenameTable[0..MAX_REG-1]
At dispatch do the following
  Rename every destination register with a tag
    Tag allocated, stored in rename table
      RenameTable[register] = tag
  IF value available read value from reg file ELSE
  Use tag instead of register names for source registers
    Tag = RenameTable[register]

## Slide 37: Tomasulo Register Renaming Algorithm: Corrected
Dispatch in order
Dispatch (to RS) has a register rename table
  One entry per architectural register
  RenameTable[0..MAX_REG-1]
At dispatch do the following
  IF value available read value from reg file ELSE
  Use tag instead of register names for source registers
    Tag = RenameTable[register]
  Rename every destination register with a tag
    Tag allocated, stored in rename table
      RenameTable[register] = tag

## Slide 38: New Pipeline?
Fetch
Decode
Dispatch+Rename
Execute/Mem
WB
How do we decouple IF/ID from EX/WB

## Slide 39: Reservation station entry: May be more than one per FU
Renamed instruction sent to reservation station and stored until all arguments are valid
  Op is operation (+, -, *, /)
  Valid bit indicates whether data or tag is valid
Tag is sent with data from functional units
  RS matches tags sent with data against valid tags to determine who needs data
  Maybe more than one RS entry needs data (why?)
0
1
Op
Src1
Data_valid
Data_valid
tag
tag
data
data
Src2
FU1
FU2
FU3
Reg
Read

## Slide 40: Common Data Bus in 360/91 (floating point path)
FP FU
FP FU
from memory
load
buffers
from instruction unit
FP registers
store buffers
to memory
operation bus
reservation
stations

## Slide 41: Figure from Original Paper

## Slide 42: Tomasulo Dispatch/Issue/Execute/Complete
If reservation station available before renaming
  Instruction + renamed operands (source value/tag) to reservation station
  Only rename if reservation station is available
Else????
When waiting for operand (implying tag in RS)
  Watch common data bus (CDB) for tag
  When tag seen, grab value
  When both operands available, instruction ready to be issued
Issue instruction to FU
After instruction finishes in FU
  Arbitrate for CDB
  Put tagged value onto CDB
  Register file on CDB
    Register contains 1 tag indicating latest value
    If latest value of register seen, write to register (and set valid bit)
  Reclaim rename tag
    no valid copy of tag in system!