## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 9
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Survey #2 results
  26 students responded (26/32 = 81% response rate)
  Thank you for providing honest feedback!

## Slide 3: Survey #2: How are we doing?

## Slide 4: Survey #2: How are we doing?

## Slide 5: Survey #2: How are we doing?

## Slide 6: Survey #2: How are we doing?

## Slide 7: Survey #2: How are we doing?

## Slide 8: Survey #2: How are we doing?
What other topics would you like covered?
  Real-world examples
  Recent architectural changes and contributions
  Breaking down an SoC
  Different generations of Intel processors
  TAGE branch predictors and other latest branch predictors
  GPU
  Non-von-Neumann architecture
  Machine Learning related topics
  Formal verification, Bluespec, RISC-V

## Slide 9: Survey #2: How are we doing?
Other comments (Most responses paraphrased. Removed compliments)
    “I worry that people who haven’t taken this class before are at a disadvantage”
  Lectures
    “Sometimes the lectures feel like the slide is simply being read rather than a story is being told.”
    Order of lectures sometimes feel out-of-order
    Want more details in slides
    Want some problem set type examples in class
  Assignments
    Want feedback on lab and assignments
    For labs, want more than one chance for testing our code
    “I don’t have a good C background which is making homework and labs quite difficult”
  Discussion Sections
    Want new content instead of recitation

## Slide 10: Scoreboarding Review
Allows instructions to execute out-of-order when necessary resources are available and there are no data dependencies
Stalls front of pipeline if
  functional unit busy (deals with FU hazard)
  destination register busy (deals with WAW hazard)
Reads registers immediately before execution
  May need more register read ports
Every register writeback is performed
If pending reads of previous value of register, writeback stalled
  Otherwise, potential for WAR hazard

## Slide 11: Tomasulo’s Algorithm Review
More distributed than scoreboarding
  Decisions can be made in distributed reservation stations
Address WAW hazards without stalling
  Register Renaming
Today:
  More details on Tomasulo
  Handling In-order Retirement (ROB)

## Slide 12: Review: Simplified Tomasulo Pipeline
Fetch
Decode
FU1
FU2
FU3
Reg
Read

## Slide 13: Register File
Each register has a presence bit indicating whether its value is present (valid) or not present (invalid)
If data invalid, value is being computed
  Tag is used as a placeholder for the value until it is computed
When is presence bit set to invalid?
Register file read returns either valid data or a tag
FU1
FU2
FU3
Reg
Read
R0
R1
R2
R3
tag
value
valid?

## Slide 14: Register File Valid?
Set to invalid the moment dispatched as destination
  At that point no following instructions should read the old value
Set to valid during writeback/complete iff tag matches instructions and register file location
  Every instruction must maintain its original destination architectural register name
  Every instruction must maintain its tag

## Slide 15: More Registers without More Registers?
Rename registers effectively increase number of usable registers without increasing number of bits in instruction
  not quite as good. why?
Need some way to “reclaim” registers
Potential performance hit?
Why can’t the compiler just use different registers?

## Slide 16: Renaming and Hazards
Do WAW/WAR hazards occur after rename?
  No!
  New name (tag) for every register written
    Dependence based on tag, not register name
  Rename eliminates all hazards by renaming all destination registers and using new names for real dependencies
What if you run out of rename names?
  Standard solution (stall)

## Slide 17: Tomasulo Register Renaming Algorithm Intentional Error!
Dispatch in order
Dispatch (to RS) has a register rename table
  One entry per architectural register
  RenameTable[0..MAX_REG-1]
At dispatch do the following
  Rename every destination register with a tag
    Tag allocated, stored in rename table
      RenameTable[register] = tag
  IF value available, read value from reg file ELSE
  Use tag instead of register names for source registers
    Tag = RenameTable[register]

## Slide 18: Tomasulo Register Renaming Algorithm: Corrected
Dispatch in order
Dispatch (to RS) has a register rename table
  One entry per architectural register
  RenameTable[0..MAX_REG-1]
At dispatch do the following
  IF value available read value from reg file ELSE
  Use tag instead of register names for source registers
    Tag = RenameTable[register]
  Rename every destination register with a tag
    Tag allocated, stored in rename table
      RenameTable[register] = tag

## Slide 19: New Pipeline?
Fetch
Decode
Dispatch+Rename
Execute/Mem
WB
How do we decouple IF/ID from EX/WB

## Slide 20: Common Data Bus in 360/91 (floating point path)
FP FU
FP FU
from memory
load
buffers
from instruction unit
FP registers
store buffers
to memory
operation bus
reservation
stations

## Slide 21: Figure from Original Paper

## Slide 22: Reservation station entry: May be more than one per FU
Renamed instruction sent to reservation station and stored until all arguments are valid
  Op is operation (+, -, *, /)
  Valid bit indicates whether data or tag is valid
Tag is sent with data from functional units
  RS matches tags sent with data against valid tags to determine who needs data
  Maybe more than one RS entry needs data (why?)
0
1
Op
Src1
Data_valid
Data_valid
tag
tag
data
data
Src2
FU1
FU2
FU3
Reg
Read

## Slide 23: Reservation Station Design Options
RS can be distributed or centralized
Distributed RS (separate RS per FU)
  Can only contain fields pertaining to specific functional unit (branch, store, ..)
  Simpler control and routing
  Number of ports can be low
Centralized RS (shared RS for all FUs)
  RS entries not statically partitioned
    Can adapt better to different instruction mixes
FU1
FU2
FU3
Reg
Read
FU1
FU2
FU3
Reg
Read

## Slide 24: Tomasulo Dispatch/Issue/Execute/Complete
If reservation station available before renaming
  Instruction + renamed operands (source value/tag) to reservation station
  Only rename if reservation station is available
Else????
When waiting for operand (implying tag in RS, not value)
  Watch common data bus (CDB) for tag
  When tag seen, grab value
  When both operands available, instruction ready to be issued
Issue instruction to FU
After instruction finishes in FU
  Arbitrate for CDB
  Put tagged value onto CDB
  Register file on CDB
    Register contains 1 tag indicating latest value
    If latest value of register seen, write to register (and set valid bit)
  Reclaim rename tag
    no valid copy of tag in system!

## Slide 25: Nonblocking Caches
Needed to allow “memory parallelism”
  Concurrent requests to memory so that OOO isn’t blocked
  Concurrent requests to utilize throughput optimizations in mem
Miss Status Holding(Handling) Registers (MSHRs)
  Track each outstanding memory operation
  Fixed number of outstanding misses at each level
  Multiple requests can potentially be serviced by same entry
  Implies data returns out of order – need an ID and buffers at all levels where non-blocking allowed
CPU
L1$
L2$
Mem
MSHR

## Slide 26: Out-of-Order Completion
Does it matter?
During normal program run, it doesn’t matter if instructions get out-of-order!
When does it matter?
  Precise exceptions
    What if operation faults (divide by zero, page fault)?
      traditionally, kill instructions behind, let instructions ahead go
      fix problem in software
      resume faulting instruction or one after
    Out-of-order means following instructions may have already completed
26
Notes: 26

## Slide 27: Out-of-Order Completion => In-Order Retirement
What do we need to do?
  Provide appearance that instructions write-back (retire) to architectural state in dispatch order
    Real registers
    Memory
  Must provide way to use non-retired state
    Tomasulo already supports that
  But, does Tomasulo allow us to “uncomplete” a completed instruction?
Need two things
  Track what is oldest instruction and newest write to a reg
  Provide ability to “rollback” to a specific un-retired instruction
27
Notes: 27

## Slide 28: Determining Order Reorder Buffer == Completion Buffer
Reorder buffer tracks all outstanding instructions in issue order
  Determines when instruction becomes oldest
  Retires oldest instruction(s) by copying pending value to architectural register file
If need to rollback to oldest instruction, throw away
Bread crumbs to determine state of each instruction
  Similar to scoreboard
28
Notes: 28

## Slide 29: Out-of-Order Execution => In-Order State Update
One possible strategy
  Architectural registers
    Consistent with in-order execution
  AND separate rename registers
    Hold non-completed values
29
B
A
R0
R1
R2
R3
0
1
2
3
Tag
value
T
T
F
F
committed
A
B
C
D
10
11
12
13
F
T
F
F
valid
What registers are architectural registers?
Can R3’s value be read? If so, what is it?
Can R0’s value be read? If so, what is it?
Can R2’s value be read? If so, what is it?
How many rename registers required?
“RAT”
Register Alias Table
Value
E
15
F
F
18
F
G
25
F
Notes: 29

## Slide 30: Possible Reorder Buffer – Implemented as Circular Buffer
30
Issued
Done
Inst address
Arch Reg
Valid
1
0
0x0100
---
1
0
0
0x0200
B
1
1
1
0x0204
A
1
0
0
0
0
0
0
0
head
tail
When can an instruction retire?
What do you do?
How do you read a register that hasn’t committed to arch state?
Rename
Reg
R5
R3
---
Notes: 30

## Slide 31: Possible Reorder Buffer – Implemented as Circular Buffer
31
Issued
Done
Inst address
Arch Reg
Valid
1
0
0x0100
---
1
0
0
0x0200
Value
1
1
1
0x0204
Value
1
0
0
0
0
0
0
0
head
tail
When can an instruction retire?
What do you do?
How do you read a register that hasn’t committed to arch state?
Actual
Physical
R5
R3
---
Notes: 31

## Slide 32: Shadow Memory Buffers/Store Buffers
Uncommitted executed memory writes are blocked to a write buffer until instruction is committed
  Loads must be short-circuited from buffer
When instruction is oldest, writes either
  Allowed to proceed to be written to memory or
  Canceled
Store buffers are essentially renamed registers for memory locations
  Any issues?
Also known as the Load/Store Queue (LSQ)
Also known as Memory Ordering Buffer (MOB)

## Slide 33: Shadow Memory Buffers/Store Buffers
Store  Load is potential RAW! True data flow
Store  Store is potential WAW
  What about WAR?
Don’t want to stall on every memory operation
Rules for “memory disambiguation”
Loads (most relaxed)
  Load can bypass any store known to not be to overlapping location
    Careful about word size
    Typically need to know addresses of load and all prior stores, unless:
  Load can immediately “execute” when closest store to same address has a value (in store buffer)
Stores (most relaxed)
  Store can write to memory when all older store addresses known

## Slide 34: Where is the Reorder Buffer?
Fetch
Decode
Rename/ROB/ MOB/RS
RS/Schedule
Execute/Mem
WB
Retire
Retire stage also known as commit or gradute

## Slide 35: Alternative: Explicit Register Renaming
No architectural registers, only physical registers
Use more physical registers than ISA supports
Supports in-order view of register values
Single register file, simpler
Used in MIPS R10000, Alpha 21264, and with many modern processors
Architectural register mapping is a lookup table
  Committed or uncommitted
  Valid or not
  Can committed be invalid?
C
U
C
U
R0
R1
R2
R3
P0
P7
P3
P2
Committed
Tag
Uncommitted
Tag
T
F
T
T
Valid?
P4
P1
P5
P6
value
P0
P1
P2
P3
P4
P5
P6
P7
Commited?

## Slide 36: Tradeoffs of Explicit Register Renaming (Physical Register Files)
Pros:
  Register file can be smaller than ROB
    Not all instructions write to registers
  Data values not duplicated
    Otherwise, data can be in RS, Arch reg file, ROB, rename table, etc.
  Simpler register file design
    Only one read and write path for register data
Cons:
  Always need to look up PRF to access value
    Indirection implies higher latency

## Slide 37: Reorder Buffer with Explicit Register Renaming
Tag points to physical register
When instruction commits, binding between arch register and physical register is committed
  In register rename table
000
Completed?
001
010
011
100
101
110
111
Other
Stuff
dest
reg
phy
reg
Notes: If registers read at dispatch, then deallocate physical register when the corresponding arch register is overwritten. If read right before issue, then cannot deallocate until all pending reads to that physical register have completed.

## Slide 38: When Are Explicit Rename Registers Deallocated?
Assume want to support precise exceptions
  Darn precise exceptions, always complicating things
Cannot deallocate every register
  Some are the architectural registers
Only deallocate register if not going to be used again
  How do you know when it won’t be used again?

## Slide 39: Solution 1
C
U
C
U
R0
R1
R2
R3
P0
P17
P3
P2
T
F
T
T
P4
P18
P30
P1
000
F
Completed?
R1
001
010
011
100
101
110
111
Other
Stuff
dest
reg
T
R1
T
R3
F
R1
P7
P8
P1
P18
phy
reg
As instruction retires,
previously committed phys reg can be reclaimed
Requires read/modify/write of committed entry in rename table
Committed
Tag
Uncommitted
Tag
Valid?
Commited?
RAT
ROB
Notes: Looking at R1, P17 is committed. Instruction 000, 001 and 011 reused R1, renaming to P7, P8 and P18 respectively. Upon commit of 000, would need to write P7 into the Committed field of R0.

## Slide 40: Solution 1a
Keep old physical register name in ROB
  Can reclaim as instruction retired
  Avoid read/modify/write in rename table
000
Completed?
001
010
011
100
101
110
111
Other
Stuff
arch
reg
new
phy
reg
old
phy
reg

## Slide 41: Where is the Reorder Buffer?
Fetch
Decode
Rename/ROB/ MOB
RS/Schedule
Execute/Mem
WB
Retire
Retire stage also known as commit or graduate
Dispatch
Dispatch possibly separate from Rename/ROB. But then need to check physical register at dispatch again.

## Slide 42: Putting it all together
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical Registers
LSQ
Reservation stations
Architectural
registers

## Slide 43: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 44: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 45: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 46: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 47: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 48: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 49: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 50: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 51: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 52: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 53: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 54: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 55: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 56: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 57: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations