## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 10
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Lab 3 posted – Due Oct 21, 2018 at 11:59pm
  Cycle-accurate simulator of LC-3b
  Individual
PS #3 – Will be posted soon (Due Oct 17 before class)
PS #1 – check Gradescope for scores
Exam 1
  5pm on Wednesday, Oct 10 in class
  Will cover everything we learned including today’s lecture
  Open-book including lecture notes (No internet searches or communication!)
Monday, Oct 8
  Q&A: Review topics based on request
  Otherwise, will talk about Physical Memory

## Slide 3: Tomasulo Dispatch/Issue/Execute/Complete
If reservation station available before renaming
  Instruction + renamed operands (source value/tag) to reservation station
  Only rename if reservation station is available
Else????
When waiting for operand (implying tag in RS)
  Watch common data bus (CDB) for tag
  When tag seen, grab value
  When both operands available, instruction ready to be issued
Issue instruction to FU
After instruction finishes in FU
  Arbitrate for CDB
  Put tagged value onto CDB
  Register file on CDB
    Register contains 1 tag indicating latest value
    If latest value of register seen, write to register (and set valid bit)
  Reclaim rename tag
    no valid copy of tag in system!

## Slide 4: Register File Valid?
Set to invalid the moment dispatched as destination
  At that point no following instructions should read the old value
Set to valid during writeback/complete iff tag matches instructions and register file location
  Every instruction must maintain its original destination architectural register name
  Every instruction must maintain its tag

## Slide 5: Determining Order Reorder Buffer == Completion Buffer
Reorder buffer tracks all outstanding instructions in issue order
  Determines when instruction becomes oldest
  Retires oldest instruction(s) by copying pending value to architectural register file
If need to rollback to oldest instruction, throw away
Bread crumbs to determine state of each instruction
  Similar to scoreboard
5
Notes: 5

## Slide 6: Out-of-Order Execution => In-Order State Update
One possible strategy
  Architectural registers
    Consistent with in-order execution
  AND separate rename registers
    Hold non-completed values
6
B
A
R0
R1
R2
R3
0
1
2
3
Tag
value
T
T
F
F
committed
A
B
C
D
10
11
12
13
F
T
F
F
valid
What registers are architectural registers?
Can R3’s value be read? If so, what is it?
Can R0’s value be read? If so, what is it?
Can R2’s value be read? If so, what is it?
How many rename registers required?
“RAT”
Value
E
15
F
F
18
F
G
25
F
Notes: 6

## Slide 7: Possible Reorder Buffer – Implemented as Circular Buffer
7
Issued
Done
Inst address
Arch Reg
Valid
1
0
0x0100
---
1
0
0
0x0200
B
1
1
1
0x0204
A
1
0
0
0
0
0
0
0
head
tail
When can an instruction retire?
What do you do?
How do you read a register that hasn’t committed to arch state?
Rename
Reg
R5
R3
---
Notes: 7

## Slide 8: Possible Reorder Buffer – Implemented as Circular Buffer
8
Issued
Done
Inst address
Arch Reg
Valid
1
0
0x0100
---
1
0
0
0x0200
Value
1
1
1
0x0204
Value
1
0
0
0
0
0
0
0
head
tail
When can an instruction retire?
What do you do?
How do you read a register that hasn’t committed to arch state?
Actual
Physical
R5
R3
---
Notes: 8

## Slide 9: Nonblocking Caches
Needed to allow “memory parallelism”
  Concurrent requests to memory so that OOO isn’t blocked
  Concurrent requests to utilize throughput optimizations in mem
Miss Status Holding(Handling) Registers (MSHRs)
  Track each outstanding memory operation
  Fixed number of outstanding misses at each level
  Multiple requests can potentially be serviced by same entry
  Implies data returns out of order – need an ID and buffers at all levels where non-blocking allowed
CPU
L1$
L2$
Mem
MSHR

## Slide 10: Shadow Memory Buffers/Store Buffers
Uncommitted executed memory writes are blocked to a write buffer until instruction is committed
  Loads must be short-circuited from buffer
When instruction is oldest, writes either
  Allowed to proceed to be written to memory or
  Canceled
Store buffers are essentially renamed registers for memory locations
  Any issues?
Also known as the Load/Store Queue (LSQ)
Also known as Memory Ordering Buffer (MOB)

## Slide 11: Shadow Memory Buffers/Store Buffers
Store  Load is potential RAW! True data flow
Store  Store is potential WAW
  What about WAR?
Don’t want to stall on every memory operation
Rules for “memory disambiguation”
Loads (most relaxed)
  Load can bypass any store known to not be to overlapping location
    Careful about word size
    Typically need to know addresses of load and all prior stores, unless:
  Load can immediately “execute” when closest store to same address has a value (in store buffer)
Stores (most relaxed)
  Store can write to memory when all older store addresses known

## Slide 12: Where is the Reorder Buffer?
Fetch
Decode
Rename/ROB/ MOB/RS
RS/Schedule
Execute/Mem
WB
Retire
Retire stage also known as commit or gradute

## Slide 13: Alternative: Explicit Register Renaming
No architectural registers, only physical registers
Use more physical registers than ISA supports
Supports in-order view of register values
Single register file, simpler
Used in MIPS R10000, Alpha 21264, and with many modern processors
Architectural register mapping is a lookup table
  Committed or uncommitted
  Valid or not
  Can committed be invalid?
C
U
C
U
R0
R1
R2
R3
P0
P7
P3
P2
Committed
Tag
Uncommitted
Tag
T
F
T
T
Valid?
P4
P1
P5
P6
value
P0
P1
P2
P3
P4
P5
P6
P7
Committed?

## Slide 14: Tradeoffs of Explicit Register Renaming (Physical Register Files)
Pros:
  Data values not duplicated
    Otherwise, data can be in RS, Arch reg file, ROB, rename table, etc.
  Simpler control for register reads and writes
    Only one read and write path for register data
Cons:
  Always need to look up PRF to access value
    Indirection implies higher latency

## Slide 15: Reorder Buffer with Explicit Register Renaming
Tag points to physical register
When instruction commits, binding between arch register and physical register is committed
  In register rename table
000
Completed?
001
010
011
100
101
110
111
Other
Stuff
dest
reg
phy
reg
Notes: If registers read at dispatch, then deallocate physical register when the corresponding arch register is overwritten. If read right before issue, then cannot deallocate until all pending reads to that physical register have completed.

## Slide 16: When Are Explicit Rename Registers Deallocated?
Assume want to support precise exceptions
  Darn precise exceptions, always complicating things
Cannot deallocate every register
  Some are the architectural registers
Only deallocate register if not going to be used again
  How do you know when it won’t be used again?

## Slide 17: Solution 1
C
U
C
U
R0
R1
R2
R3
P0
P17
P3
P2
T
F
T
T
P4
P18
P30
P1
000
F
Completed?
R1
001
010
011
100
101
110
111
Other
Stuff
dest
reg
T
R1
T
R3
F
R1
P7
P8
P1
P18
phy
reg
As instruction retires,
previously committed phys reg can be reclaimed
Requires read/modify/write of committed entry in rename table
Committed
Tag
Uncommitted
Tag
Valid?
Committed?
RAT
ROB
Notes: Looking at R1, P17 is committed. Instruction 000, 001 and 011 reused R1, renaming to P7, P8 and P18 respectively. Upon commit of 000, would need to write P7 into the Committed field of R1.

## Slide 18: Solution 1a
Keep old physical register name in ROB
  Can reclaim as instruction retired
  Avoid read/modify/write in rename table
000
Completed?
001
010
011
100
101
110
111
Other
Stuff
arch
reg
new
phy
reg
old
phy
reg

## Slide 19: Where is the Reorder Buffer?
Fetch
Decode
Rename/ROB/ MOB
RS/Schedule
Execute/Mem
WB
Retire
Retire stage also known as commit or graduate
Dispatch
Dispatch possibly separate from Rename/ROB. But then need to check physical register at dispatch again.

## Slide 20: Putting it all together
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical Registers
LSQ
Reservation stations
Architectural
registers

## Slide 21: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 22: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 23: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 24: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 25: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 26: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 27: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 28: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 29: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 30: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 31: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 32: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 33: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 34: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 35: Putting it all together (one option)
Fetch
Decode
Rename
ROB
RS
Execute/Mem
WB
Retire
RAT
Physical registers
Arch registers
LSQ
Reservation stations

## Slide 36: OOO Branches?
Program counter register
Condition codes register
Exceptions and interrupts

## Slide 37: Pipeline review
Pipelining is all about exploiting parallelism
  Execute multiple instructions in parallel
  Keep all hardware stages busy
  Maintain dependencies as expressed by sequential program
Implicit parallelism, or
Instruction level parallelism (ILP)
Pipelining inherently trades off latency for throughput
  Also adds complexity

## Slide 38: Exploiting ILP
Superscalar
  issue more than 1 instruction per cycle
    Duplication of hardware resources such as functional units, register file ports, memory ports....
Superpipelining
  Deeply pipelined execution unit with higher clock rate
    utilizing same hardware more aggressively
Combination (most current processors)
38
Notes: 38

## Slide 39: SuperScalar and Superpipelined
39
A
B
C
D
E
F
A
B
C
D
E
F
A
B
C
D
E
F
Equal steady
state throughput
between superscalar
and superpipelining
(same number of
overlapped operations)
longer startup for
superpipeline. Effects on
branches??
Notes: 39

## Slide 40: Some Real World Examples
Let’s take a look at how everything we learned about core microarchitecture is applied in a real life
  Pipelining
  Out-of-Order execution
    Register renaming, reservation stations, register file design
Disclaimer
  These designs are shown for education purposes only
  The following designs are shown just to illustrate how the concepts we learned are applied in real designed
  This is not a confirmation of any of the exact designs or parameters
  All diagrams are based on publicly accessible papers or articles

## Slide 41: Intel Pentium Pro (P6) (1995)
Figure courtesy of Prof. Wen-mei Hwu, University of Illinois

## Slide 42: Intel Pentium 4 (Netburst) (2000)
[Hinton et al., “The Microarchitecture of the Pentium 4 Processor,” Intel Technology Journal, 2001.]

## Slide 43: Pentium Pro vs. Pentium 4
Pointers to architectural
register values

## Slide 44: DEC Alpha 21264 (1996)
Kessler, “The Alpha 21264 Microprocessor,” IEEE Micro, March-April 1999.

## Slide 45: Intel Nehalem (2008)
[source: Wikipedia]

## Slide 46: Intel Skylake (2015)
[source: https://www.nextplatform.com/2017/08/04/drilling-xeon-skylake-architecture/ ]

## Slide 47: Arm Cortex-A76 (2018)
[source: https://images.anandtech.com/galleries/6373/02_Cortex-A76%20Deep%20Dive%20Final_NoWM_12.png]