## Slide 1: 382N.1: Computer Architecture Fall 2018: Lecture 19
Dam Sunwoo
University of Texas at Austin
Arm Research

## Slide 2: Announcements
Reminder: Lab #4 due this weekend
Problem Set #5 just posted
  Due Nov 15 at 11:59pm (to help you with exam prep)
Reminder: Exam #2: Nov 19 (in class)
Reminder: No class on Nov 21 (day before Thanksgiving)

## Slide 3: Recap and Outline
Recap
  I/O
  Bus
  Interconnection Networks
Outline
  Vector processors

## Slide 4: Single instruction multiple data (SIMD)
sequencer
memory hierarchy
Local Mem
Local Mem
Local Mem
Local Mem

## Slide 5: SIMD (vector style) – aka DLP (data-level parallelism)
sequencer
memory hierarchy
Local Mem
Local Mem
Local Mem
Local Mem

## Slide 6: SIMD vs. Vector Processors
Code
  LD VR <- A[3:0]
  ADD VR = VR + 1
  MUL VR = VR * 2
  ST A[3:0] <- VR
LD0
ADD0
MUL0
ST0
LD1
ADD1
MUL1
ST1
LD2
ADD2
MUL2
ST2
LD3
ADD3
MUL3
ST3
LD0
LD1
LD2
LD3
ADD0
ADD1
ADD2
ADD3
MUL0
MUL1
MUL2
MUL3
ST0
ST1
ST2
ST3
PE0
PE1
PE2
PE3
LD
ADD
MUL
ST
Time
Different op in same space
Different op at same time
Same op at same time
Same op in same space
SIMD
Vector

## Slide 7: Cray-1 (1976)
http://www.flickr.com/photos/laughingsquid/102686307/

## Slide 8: Cray-1
From Cray-1 paper (1977)

## Slide 9: Cray-1 (1976)
Single Port
Memory
(320MW/sec)
16 banks of
64-bit word
+
8-bit SECDED
(A0)
( (Ah) + j k m )
64
T Regs
(A0)
( (Ah) + j k m )
64
B Regs
4 Instruction
Buffers
64-bitx16
NIP
LIP
CIP
S0
S1
S2
S3
S4
S5
S6
S7
A0
A1
A2
A3
A4
A5
A6
A7
Si
Tjk
Ai
Bjk
FP Add
FP Mul
FP Recip
Int Add
Int Logic
Int Shift
Pop Cnt
Sj
Si
Sk
Addr Add
Addr Mul
Aj
Ai
Ak
processor cycle 12.5 n seconds memory cycle 50 n seconds
V Regs
(64x64)
V Regs
(64x64)
V Regs
(64x64)
V Regs
(64x64)
V Regs
(64x64)
V Regs
(64x64)
V Regs
(64x64)
V Regs
(64x64)
Vec Add
Vec Logic
Vec Shift
Pop Cnt

## Slide 10: Memory Initiation Rate
Memory speed must keep up with CPU speed!
  Interleave memory banks
To maintain initiation rate of 1, the number of banks must be at least the ratio of memory to processor cycle time.
  However, if processor make access in non-unit stride, it is possible to have bank conflicts.

## Slide 11: Memory Initiation Rate
In general, effective bandwidth (relative to 1 bank) is
  Number of banks / GCD(stride, number of banks)
  Example: stride = 1, number of banks = 16, 16/1 = 16
  Stride = 16, number of banks = 16, EB = 16/16 = 1
  Stride = 8, number of banks = 16, 16/8 = 2
  Stride = 3, number of banks = 16, 16/1 = 16
A performance-minded programmer will rearrange data to avoid bad strides (by padding etc)
Alternatively, prime number of banks is an hardware solution.
  Only have most serious problem when accessing at stride exactly equal to the number of banks
  Difficult to implement though.
    Must do real divisions instead of shifts

## Slide 12: Memory Bandwidth Needed
Pipelined vector add
  read two arguments, write one result back each cycle
    3 memory references / cycle
Cray-1, cycle time is 12.5ns (80MHz)
  3W * 80MHz = 240 M Words / sec
  each word, 64b
  8B * 240M/sec ~= 2GB/sec (Cray-1 actually higher at 320MW/sec)
  Extremely fast for the time, not too bad even today
Pentium 4, cycle time is 0.2778ns (3.6GHz)
  3W * 3.6GHz = 10.8GW/sec
  Each word, 64b
  8B * 10.8G/sec = 86.4GB/sec
  Pentium 4 has 800Mb/sec * 64b bus = 6.4GB/sec peak (never achievable)
    Not very balanced

## Slide 13: Performance of Cray-1
Memory bandwidth limiting factor for Cray-like vector machines
  Cray-1 Peak Performance
    240 MFlops
  Cray-1 Sustained Performance
    80 MFlops steady-state
  Cray-1 Realistic Performance
    20-30 MFlops, including scalar portions

## Slide 14: Cray-1 Packaging
Shaped in a partial cylinder, 4.5’ in diameter, 6.5’ high
3 90-degree arc segments, 4 columns per segment
144 modules per column
2 circuit board per module with up to 144 IC’s each
modules are mounted on copper heat transfer plate
All plates are connected to vertical aluminum bars with pipes carrying freon
Plates are kept at 25 degree Celsius and IC’s run in the 50 degree range
  2 25-ton compressors are needed

## Slide 15: Cray-2 (1985)
16 gate arrays, sub-nanosecond delay ECL logic
14 Columns in 300-degree arc
112 cm high and 133 cm in diameter
All circuits are immersed in inert fluorocarbon
Power supplies and plumbing at the base of the machine

## Slide 16: Cray-2 from Musee des Arts and Metiers, Paris, France (http://www.arts-et-metiers.net/)

## Slide 17: Cray-2

## Slide 18: Modern Cray Boards: Cray X2 (Black Widow) (2007)
100 GFLOPS
“Fat Tree” interconnect

## Slide 19: NEC SX-9 (100 GFLOPS, 256GB bandwidth) (2008)

## Slide 20: Post-K Supercomputer with Arm (2018)
slides from Fujitsu

## Slide 21: And why they are still important – GPUs
GPUs have >10X better performance and efficiency compared to CPUs

## Slide 22: Vector Machine Organization
Typically contains separate vector unit and scalar unit
  Still need to do scalar computation
Two classes (by memory access pattern)
  Vector-register (vector analog of load-store architectures): all memory accesses go to vector registers and arithmetic operations are between vector registers
  Memory-memory: vector operands and target are in memory

## Slide 23: Implementing Vector Ops
Many identical arithmetic units
  Data parallel
  Pros? Cons?
Several highly pipelined arithmetic units
  Identical
  Heterogeneous
  Pros? Cons?
Mix?
(Vector Length = 4) in all cases here
A
A
A
A
B
B
B
B
C
C
C
C
Op
Op
Op
Op
A
A
A
A
B
B
B
B
C
C
C
C
Op
A
A
A
A
B
B
B
B
C
C
C
C
Op
Op
(SIMD)
(4-deep
Pipeline)
Vector Lane / Pipe

## Slide 24: Vector Machine: Performance Basics
The contributions to run time of an instruction are
  startup-time: depth of the pipeline
  initiation rate: rate at which instructions enters the pipeline
    # lanes
Under simplistic assumptions:
  The time to complete a vector operation of length n is
    startup-time + (n-1) / initiation rate

## Slide 25: Vector Speedup
Given 75% vectorizable code and vector/scalar performance ratio of 5:1
  What is the single node speedup through vectorization?
Amdahl’s Law
  Speedup = Tori/Tnew
  Tnew = (.75 * 1/5) + (.25 * 1/1) = 0.4
  Therefore, speedup = 1/0.4 = 2.5

## Slide 26: Goal: don’t stop the pipeline
What about control flow?
  Branches
  Address calculation
  …
What happens when one vector instruction finishes?

## Slide 27: But what about actual branches?
Scalar code executes on separate “pipe”
Control runs ahead of vector unit
  Resolve branches and addresses decoupled from vector pipe
  Only stop if depend on vector results!

## Slide 28: But what about actual branches?
Scalar code executes on separate “pipe”
Control runs ahead of vector unit
  Resolve branches and addresses decoupled from vector pipe
  Only stop if depend on vector results!
[AMD Fusion System Architecture]

## Slide 29: Strip-Mining
Analogy from mining
  Cut rock above an ore deposit in long ‘strips’
  This uncovers ore, which is then removed
  When the deposits in a strip are exhausted, another strip is dug beside it
  The ‘overburden’ (waste removed to access the ore) from each strip is used to fill the previous one

## Slide 30: Strip-Mining in Vector Processing (aka Loop Sectioning)
The vector length required by the program is generally different than full vector length of the machine
Typically, vector machine allows the program to specify the length of the operation in a hardware register
Thus to operate on a large vector (VL > MVL), one first performs a partial vector operation, followed by N number of full length operations. (Strip-Mining)
  Introduces additional overhead (branches and controls) to overall runtime. (estimated vector performance must account for this)
  Cray and Fujitsu vector machines rely on compiler to strip-mine
  Hitachi S810/20 implements strip mining in hardware

## Slide 31: Strip Mining
ALU

## Slide 32: Status and Condition Codes
Scalar machines
  Record status in special registers and provide instructions for test and branch
  Provide test for special values
Vector machines
  Vector of condition codes
    One vector per condition code? Wasteful
  Possibilities
    Record first anomaly, then number of same
    Provide vector test instructions for equal, <, >, etc.
    Define weird vector values for overflow and other exceptions

## Slide 33: Estimating Performance
Telement : time per macro op for a sequence of ops
Tloop : strip mining cost per loop iteration
Tstart : startup cost per loop iteration
Tbase: the initial cost to setup the whole operation
MVL: Machine Vector Length
N: number of elements
Total runtime
  Tn = Tbase + ceiling(n/MVL) * (Tloop + Tstart) + n * Telement
Average time per element is Tn/n which accounts for the real-life overhead to run the code

## Slide 34: Vector Instruction Design
Two options
  Design for highly overlapped execution of vector instructions using multiple pipelines
    results from one pipeline can be feed into another pipeline as operands using “chaining”
    pipeline scheduling done by hardware
  No overlapped vector instructions
    opcode determines static scheduling of pipelines
    proliferation of opcodes: VectorAdd&Mul, etc

## Slide 35: Chaining
Similar to bypassing from basic RISC pipeline
  Removes interlocks between interdependent instructions.
Chaining connects the output of one functional unit to the input of the next.
  Can chain to/from memory, ALUs, etc
  Essentially, pipelining

## Slide 36: Example Code
Scalar
  For I = 0 to 49
  C[i] = (A[i] + B[i]) / 2
Vector
  VLN = 50 ; 1
  VST = 1 ; 1
  V0 = A[0..VLN-1] ; 11 + VLN - 1
  V1 = B[0..VLN-1] ; 11 + VLN - 1
  V2 = V0 + V1 ; 4 + VLN - 1
  V3 = V2 >> 1 ; 1 + VLN - 1
  C[VST...VST+VLN-1] = V3 ; 11 + VLN – 1
Performance
  Assume LD/ST takes 11 cycles, ADD 4 cycles, SHIFT 1 cycle (pipelined)
  Compare no-chaining, chaining, chaining + 2 read/1 write port

## Slide 37: Scalar Performance
Scalar code
R0 = 50 ; 1
R1 = A ; 1
R2 = B ; 1
R3 = C ; 1
X: R4 <- MEM[R1++] ; 11 (auto-increment)
R5 <- MEM[R2++] ; 11
R6 = R4 + R5 ; 4
R7 = R6 >> 1 ; 1
MEM[R3++] = R7 ; 11
DECBNZ R0, X ; 2 (decrement and branch if not zero)
304 dynamic instructions
Perf with 1 mem bank and in-order:
4 + 50*40 = 2004 cycles
Perf with 16 mem banks / in-order:
4 + 50*30 = 1504 cycles
Why 16 banks?

## Slide 38: Vector with No-Chaining Performance
285 cycles
VLN = 50 ; 1
VST = 1 ; 1
V0 = A[0..VLN-1] ; 11 + VLN - 1
V1 = B[0..VLN-1] ; 11 + VLN - 1
V2 = V0 + V1 ; 4 + VLN - 1
V3 = V2 >> 1 ; 1 + VLN - 1
C[VST...VST+VLN-1] = V3 ; 11 + VLN – 1

## Slide 39: Vector with Chaining Performance, 1 Memory Port
182 cycles
VLN = 50 ; 1
VST = 1 ; 1
V0 = A[0..VLN-1] ; 11 + VLN - 1
V1 = B[0..VLN-1] ; 11 + VLN - 1
V2 = V0 + V1 ; 4 + VLN - 1
V3 = V2 >> 1 ; 1 + VLN - 1
C[VST...VST+VLN-1] = V3 ; 11 + VLN – 1
V0 (Load)
V1 (Load)
V2 (Add)
V3 (Shift)
C (Store)

## Slide 40: Chaining, 2 Load/1 Store Ports
79 cycles
V0 (Load)
V1 (Load)
VLN = 50 ; 1
VST = 1 ; 1
V0 = A[0..VLN-1] ; 11 + VLN - 1
V1 = B[0..VLN-1] ; 11 + VLN - 1
V2 = V0 + V1 ; 4 + VLN - 1
V3 = V2 >> 1 ; 1 + VLN - 1
C[VST...VST+VLN-1] = V3 ; 11 + VLN – 1
V2 (Add)
V3 (Shift)
C (Store)

## Slide 41: Vector Mask Control
Example:
  loop: if a[i] then b[i]=a[i]+b[i]
  goto loop
The conditional statement can be achieved by using “vector mask” control. VM is a bit mask of the length of the MVL
When VM is used, only the operation on positions corresponding to bits set in the VM are executed.
  All are executed, only some are not propagated
Usage: compressing, conditional execution

## Slide 42: Memory Specification
Which n locations in memory contain vector?
  contiguous
    need to specify base and length
    memory interleaving works well
  column of matrix (stored in row-major order)
    base, length, stride
    address generation must perform add
    stride multiple of interleave factor?
  diagonal of matrix
    stride increases by one each time

## Slide 43: Sparse Addressing Patterns
Sparse address patterns can arise due to
  data dependent operations (conditionals)
  vectors where most of the elements are zero
  indirect table lookup
Techniques for sparse addressing
  associate bit-vector or index-vector with vector
  use bit or index vector to perform operations like selective store, compression, expansion

## Slide 44: Scatter / Gather
Scatter / Gather operations often implemented in hardware to handle sparse matrices
Loads and stores use an index vector which is added to the base register to generate the addresses
Functional Description:
  Gather
    for (i=0; i<N; ++i)
    x[i] = y[ idx[i] ];
  Scatter
    for (i=0; i<N; ++i)
    y[ idx[i] ] = x[i];