## Slide 1: Lecture 24
Dam Sunwoo
Arm Research
EE382N.1 Fall 2018
Heterogeneous Multi-Processing
Security (Side-Channel Attacks)

## Slide 2: Announcements
Lab 6 posted:
  Due 12/12 (Wed), 11:59pm
Grad Lab new deadline:
  Due 12/17 (Mon), 11:59pm
Will post all scores (exams, labs, problem sets) on Canvas soon
Guest Lecture on Wednesday
  Hongsup Shin on “A Practical Guide to Machine Learning”
  I won’t be here
Course Instructor Survey
  https://utdirect.utexas.edu/ctl/ecis/
  Closes on Dec 10

## Slide 3: Last time
Cache Coherency
  MSI
  MESI
  MOESI
  MOSIF
Memory Consistency
  Sequential Consistency
  Mutual Exclusion – Dekker’s Algorithm
  Relaxed Consistency

## Slide 4: Dekker’s Algorithm Pseudo-code
P0:
want_to_enter[0] = true
while want_to_enter[1] {
if turn != 0 {
want_to_enter[0] = false
while turn != 0 {
// busy wait
}
want_to_enter[0] = true
}
}
// critical section
…
turn = 1
want_to_enter[0] = false
// remainder section
P1:
want_to_enter[1] = true
while want_to_enter[0] {
if turn != 1 {
want_to_enter[1] = false
while turn != 1 {
// busy wait
}
want_to_enter[1] = true
}
}
// critical section
…
turn=0
want_to_enter[1] = false
// remainder section
Initially: want_to_enter[0] = false, want_to_enter[1] = false, turn = 0

## Slide 5: Review: Relaxed ordering and Dekker’s algorithm
P0 P1
F[0] = 0 F[1] = 0
… …
A: F[0] = 1 (ST) X: F[1] = 1 (ST)
B: if (F[1] == 0) (LD) Y: if (F[0] == 0) (LD)
… …
Let’s assume stores can be buffered
Order that P0 thinks happened?
Order that P1 thinks happened?
What are the sequentially consistent orders?

## Slide 6: So far, mostly focused on performance
Many other issues to think about
  Power
  Area
  Efficiency
  Security
  Reliability
  …

## Slide 7: Processor Trends

## Slide 8: Measurement
Measure of performance:
  Execution Time
  IPS: Instructions Per Second
    Assuming program
  FLOPS: Floating Point Operations Per Second
    For scientific computation
  Benchmark scores
Measure of power / energy efficiency
  Performance per Watt
  Cost of powering the CPU outweighs the cost of the CPU itself for large-scale systems
  Power efficiency is a first-class design constraint for most domains! (Not just hand-held devices)

## Slide 9: Power Management
Dynamic power (switching power) in static CMOS gates
  P = C •V2 • f
  C: Capacitance being switched
  V: Supply Voltage
  f: switching frequency
DVFS (Dynamic Voltage and Frequency Scaling)
  Dynamically adjust voltage and frequency to save power when performance is not needed
  Cluster-level or per-core
Performance
Power

## Slide 10: Heterogeneous Multi-Processing
Aka Asymmetric Multi-Processing
Arm big.LITTLE
Many mobile SoCs employ this technology
  Samsung Exynos
  Qualcomm Snapdragon
  Apple A series

## Slide 11: Arm big.LITTLE and DVFS
LITTLE cores can be more efficient at low performance levels than big cores

## Slide 12: CPU Migration
Cortex-A15/Cortex-A7 system is designed to migrate in less than 20,000-cycles, or 20-microSeconds with processors operating at 1GHz.

## Slide 13: How Many (Symmetric) Cores per Chip?
Each Chip Bounded to N BCEs (for all cores)
Each Core consumes R BCEs
Assume Symmetric Multicore = All Cores Identical
Therefore, N/R Cores per Chip — (N/R)*R = N
For an N = 16 BCE Chip:
Sixteen 1-BCE cores
Four 4-BCE cores
One 16-BCE core
“Amdahl’s Law in the Multicore Era”
[Hill 2008]

## Slide 14: Performance of Symmetric Multicore Chips
Serial Fraction 1-F uses 1 core at rate Perf(R)
Serial time = (1 – F) / Perf(R)
Parallel Fraction uses N/R cores at rate Perf(R) each
Parallel time = F / (Perf(R) * (N/R)) = F*R / Perf(R)*N
Therefore, w.r.t. one base core:
Symmetric Speedup =
1
+
1 - F
Perf(R)
F * R
Perf(R)*N
Enhanced Cores speed Serial & Parallel
Assume Perf(R) = Square Root of R

## Slide 15: Symmetric Multicore Chip, N = 16 BCEs
F=0.5, Opt. Speedup S = 4 = 1/(0.5/4 + 0.5*16/(4*16))
Need to increase parallelism to make multicore optimal!
Chart: R BCEs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
0.5 | 1.8824 | 2.5142 | 2.9171 | 3.2 | 3.4073 | 3.5629 | 3.681 | 3.7712 | 3.84 | 3.892 | 3.9308 | 3.959 | 3.9785 | 3.9911 | 3.9979 | 4
(16 cores)
(8 cores)
(2 cores)
(1 core)
F=0.5
R=16,
Cores=1,
Speedup=4
(4 cores)

## Slide 16: Symmetric Multicore Chip, N = 16 BCEs
Chart: R BCEs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
0.5 | 1.8824 | 2.5142 | 2.9171 | 3.2 | 3.4073 | 3.5629 | 3.681 | 3.7712 | 3.84 | 3.892 | 3.9308 | 3.959 | 3.9785 | 3.9911 | 3.9979 | 4
0.9 | 6.4 | 6.6551 | 6.4448 | 6.1538 | 5.8651 | 5.5988 | 5.3585 | 5.1426 | 4.9485 | 4.7732 | 4.6144 | 4.4698 | 4.3375 | 4.216 | 4.1038 | 4
At F=0.9, Multicore optimal, but speedup limited
Need to obtain even more parallelism!
F=0.5
R=16,
Cores=1,
Speedup=4
F=0.9, R=2, Cores=8, Speedup=6.7

## Slide 17: Symmetric Multicore Chip, N = 16 BCEs
Chart: R BCEs
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
0.5 | 1.8824 | 2.5142 | 2.9171 | 3.2 | 3.4073 | 3.5629 | 3.681 | 3.7712 | 3.84 | 3.892 | 3.9308 | 3.959 | 3.9785 | 3.9911 | 3.9979 | 4
0.9 | 6.4 | 6.6551 | 6.4448 | 6.1538 | 5.8651 | 5.5988 | 5.3585 | 5.1426 | 4.9485 | 4.7732 | 4.6144 | 4.4698 | 4.3375 | 4.216 | 4.1038 | 4
0.975 | 11.6364 | 9.6287 | 8.3347 | 7.4419 | 6.7824 | 6.2707 | 5.8591 | 5.5189 | 5.2316 | 4.9849 | 4.77 | 4.5806 | 4.4121 | 4.261 | 4.1243 | 4
0.99 | 13.913 | 10.5736 | 8.8539 | 7.767 | 7.0014 | 6.4249 | 5.9707 | 5.6008 | 5.2922 | 5.0295 | 4.8024 | 4.6035 | 4.4274 | 4.2701 | 4.1284 | 4
0.999 | 15.7635 | 11.2351 | 9.1977 | 7.9761 | 7.1397 | 6.5211 | 6.0397 | 5.6512 | 5.3292 | 5.0566 | 4.822 | 4.6173 | 4.4366 | 4.2756 | 4.1309 | 4
F matters: Amdahl’s Law applies to multicore chips
MANY Researchers should target parallelism F first
F1, R=1, Cores=16, Speedup16

## Slide 18: Asymmetric (Heterogeneous) Multicore Chips
Symmetric Multicore Required All Cores Equal
Why Not Enhance Some (But Not All) Cores?
For Amdahl’s Simple Software Assumptions
  One Enhanced Core
  Others are Base Cores
How?
  <fill in favorite micro-architecture techniques here>
  Model ignores design cost of asymmetric design
How does this effect our hardware model?

## Slide 19: How Many Cores per Asymmetric Chip?
Each Chip Bounded to N BCEs (for all cores)
One R-BCE Core leaves N-R BCEs
Use N-R BCEs for N-R Base Cores
Therefore, 1 + N - R Cores per Chip
For an N = 16 BCE Chip:
Symmetric: Four 4-BCE cores
Asymmetric: One 4-BCE core
& Twelve 1-BCE base cores

## Slide 20: Performance of Asymmetric Multicore Chips
Serial Fraction 1-F same, so time = (1 – F) / Perf(R)
Parallel Fraction F
  One core at rate Perf(R)
  N-R cores at rate 1
  Parallel time = F / (Perf(R) + N - R)
Therefore, w.r.t. one base core:
Asymmetric Speedup =
1
+
1 - F
Perf(R)
F
Perf(R) + N - R

## Slide 21: Asymmetric Multicore Chip, N = 256 BCEs
21
11/30/18
Wisconsin Multifacet Project
Number of Cores = 1 (Enhanced) + 256 – R (Base)
How do Asymmetric & Symmetric speedups compare?
Chart: R BCEs
(256 cores)
(1+252 cores)
(1+192 cores)
(1 core)
(1+240 cores)
Notes: LogTM: Log-based Transactional Memory
11/30/18
UW-Madison Architecture Seminar
21

## Slide 22: Recall Symmetric Multicore Chip, N = 256 BCEs
Chart: R BCEs
Recall F=0.9, R=28, Cores=9, Speedup=26.7

## Slide 23: Symmetric vs. Asymmetric
Asymmetric has higher potential under these assumptions
Chart: Symmetric
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
f=0.999 | 203.9841 | 160.6205 | 120.4139 | 87.7882 | 63.0542 | 44.9403 | 31.9043 | 22.6048 | 16
f=0.99 | 72.1127 | 79.7442 | 78.5276 | 69.0913 | 55.6522 | 42.2942 | 31.068 | 22.4034 | 16
f=0.975 | 34.7119 | 43.3579 | 49.7087 | 50.9914 | 46.5455 | 38.5148 | 29.7674 | 22.0755 | 16
f=0.9 | 9.6604 | 13.2131 | 17.5342 | 22.0755 | 25.6 | 26.6205 | 24.6154 | 20.5704 | 16
f=0.5 | 1.9922 | 2.8065 | 3.9385 | 5.4854 | 7.5294 | 10.0566 | 12.8 | 15.0849 | 16
Chart: Asymmetric
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
f=0.999 | 203.9841 | 216.5252 | 225.5773 | 230.6084 | 230.1887 | 220.9093 | 195.3125 | 137.7552 | 16
f=0.99 | 72.1127 | 91.3482 | 112.3894 | 133.646 | 152.5 | 164.513 | 161.2903 | 125.1541 | 16
f=0.975 | 34.7119 | 46.5225 | 61.2048 | 78.5796 | 97.6 | 115.4084 | 125 | 108.5977 | 16
f=0.9 | 9.6604 | 13.4708 | 18.6765 | 25.6783 | 34.8571 | 46.3037 | 58.8235 | 65.3634 | 16
f=0.5 | 1.9922 | 2.8129 | 3.9688 | 5.5938 | 7.871 | 11.0417 | 15.3846 | 20.9279 | 16
n = 256, perf(r) = sqrt(r)
f: Fraction that is parallelizable
BCE: Base Core Equivalent
n BCE: Total budget (area, power, ..)
Symmetric
(16 1-BCE cores)
Symmetric
(4 4-BCE cores)
Asymmetric
(1 4-BCE core + 12 1-BCE cores)
This model assumed either completely serial or completely parallel (nothing in-between)

## Slide 24: Specialization
Different instances of resources (e.g., cores) can be optimized for different types of workloads or satisfying different requirements or goals.
Heterogeneity enables specialization and customization
Examples
  Asymmetric multi-processing (big.LITTLE)
  CPU-GPU
  Accelerators
  Heterogeneous memory systems
  …

## Slide 25: Security Side-Channel Attacks
(Some slides from Hugo Vincent and Jaekyu Lee)

## Slide 26: Introduction
Performance has been the top priority in processor development.
Until recently, security attacks are
  From physical devices e.g. electromagnetic, eavesdropping, implanting bugs.
  Software bugs or malicious attacks.
And now processors expose severe security vulnerability.
  Spectre, Meltdown, Foreshadow
Paul Kocher “Insecurity cost will exceed other benefits”.
Notes: As we know, for last decades, we have been mostly focusing on improving performance.
And until recently, people usually think security attacks are implanting bugs to monitor and steal secrets and buggy programs and malicious software-based attacks.
However, from Spectre, Meltdown, Foreshadow, and many other variations, processors exposed significant security vulnerability.
And here is the quote from Paul Kocher, xxx

## Slide 27: What’s wrong with this code?
For performance, we want to fail fast, and not do work that won’t effect the result
For security, we don’t want an attacker to be able to deduce any information about the correct password
  This code fails fast (the length check, then the character-by-character checking)
  An attacker can precisely time execution to infer something about the control flow through it
  Attacker can determine the length of the correct password in at most n guesses, then each character of the password successively in at most 28 x n guess

## Slide 28: Side Channels?
Computers are physical objects, and computation has physical side effects
Power consumption differences (e.g., due to to different instruction mix, or even due to Hamming weight of the operands, etc.)
  Including proxies for power consumption (audible noise in a power supply, etc.)
Electromagnetic emanations (closely related to power consumption, but less invasive, and in some cases can be easier to target specific victim code or IP block)
Temperature, photo-electric effects, etc. – although typically harder to exploit in practice
Requires extra equipment and/or invasive hardware access

## Slide 29: Side-Channels in Microarchitecture
Microarchitects aggressively optimize for performance, and this, too, has side effects
  Anywhere resources can be shared:
    cache lines, issue slots in the pipeline, etc.
  Anywhere the hardware can fail fast:
    Branching, prefetching, early termination in multipliers / dividers, etc.
These are called microarchitectural side channels, and they are an increasingly important security threat, since the attack can be performed purely in software

## Slide 30: Microarchitectural side-channel
Idea is to measure something non-functional about the execution
  Timing, power, etc.
The attack looks something like this:
  Model / guess-timate what the victim code might be doing (e.g., rough pseudocode of algorithm), such that you could predict how the non-functional measurement varied as a function of the secret
  Pick a candidate value for the secret (key, password, plaintext, etc.)
  Predict the measurement you expect for that secret using the model
  Run the experiment & test the hypothesis
  Choose a new candidate value based on what you measured, with reference to you model
  Iterate until you have the whole secret

## Slide 31: Common Mitigations
“Constant-time code”
Try to trick the compiler and processor into not leaking information
  Libraries of “gadgets” or code fragments for common operations on sensitive data
  Does a *lot* of extra work
  Hamstrings the compiler and the processor
  Often in performance-critical loops

## Slide 32: Measuring through side-channels

## Slide 33: Historical Cache (Timing) Attacks
Prime+Probe
2005
Evict+Reload
2015
XLATE+Probe
2018
Flush+Flush
2016
Flush+Reload
2014
Evict+Time
2006

## Slide 34: Recent Side-Channel Attacks
Spectre v1
Spectre v2
Spectre v3 (Meltdown)
Spectre v3a
Spectre v4
JAN
MAY
Spectre v1.1
Spectre v1.2
ret2spec
SpectreRSB
NetSpectre
JUL
ForeShadow
AUG
Lazy FP state restore
JUN
What’s Next?

## Slide 35: Prime+Probe (Single-core)
Set 0
Way 0
Way 1
Way 2
Way 3
Set 1
A[0]
A[2]
A[4]
A[6]
A[1]
A[3]
A[5]
A[7]
// Victim runs its algorithm.
access(x)
access(y)
access(z)
A[0]
A[2]
A[4]
A[6]
A[1]
A[3]
Victim
A[7]
// Attacker knows A[5] is evicted.
// Attacker can infer “some address” that is mapped to Set 1 was accessed by the Victim.
// Attacker first fills (Prime) the cache for A[0-7].
// Evict A[5] based on cache replacement policy.

## Slide 36: Prime+Probe (Multi-core)
Set 0
Way 0
Way 1
Way 2
Way 3
Set 1
A[0]
A[2]
A[4]
A[6]
A[1]
A[3]
A[5]
A[7]
// Victim runs its algorithm in core 1.
A[5] = 1
A[0]
A[2]
A[4]
A[6]
A[1]
A[3]
Victim
A[7]
// Attacker precisely knows A[5] is evicted.
// Attacker first fills (Prime) the cache for A[0-7] in core 0.
// Due to cache coherence, A[5] copy in core 0 will be invalidated.

## Slide 37: Flush+Reload
Set 0
Way 0
Way 1
Way 2
Way 3
Set 1
// Victim runs its algorithm.
access(A[4])
A[4]
// Attacker flushes the entire cache.
// Attacker knows A[4] was brought by the victim.

## Slide 38: Cache Timing Attacks: Prime+Probe and Flush+Reload
Set 0
Way 0
Way 1
Way 2
Way 3
Set 1
A[0]
A[2]
A[4]
A[6]
A[1]
A[3]
A[5]
A[7]
A[0]
A[2]
A[4]
A[6]
A[1]
A[3]
A[5]
A[7]
Way 0
Way 1
Way 2
Way 3
A[4]
Fill (Prime) the cache with A[0-7].
Flush the cache.
A[5] is evicted based on replacement policy.
A[4] is installed by the victim.
Measure A[0-7] access latency.
A[5] takes longer due to miss.
Measure A[0-7] access latency.
A[4] takes shorter due to hit.
Some address that is mapped to set 1 was accessed by the victim.
A[4] is accessed by the victim
Attacker
Victim
Attacker
Extraction
Prime+Probe
Flush+Reload
Initial cache state.
Initial cache state.
Notes: Let me explain conventional cache timing attacks, namely prime and probe and flush and reload.
Here is the initial state of the cache, which has 2 sets and 4 ways.
First attacker fills the cache with the data in prime+probe, but cache is flushed in flush+reload.
Attacker lets victim run its code. As a result, line is evicted in left, and line is newly installed in right.
Finally, attacker measures the access latency. In prime+probe, A[5] takes longer due to the eviction and attackers identify that some address that is mapped to set 1 was accessed by the victim.
On the other hand, in flush+reload, A[4] takes shorter and attacker knows A[4] is accessed by the victim.

## Slide 39: Threat/Attack Model
Speculative cache fill
Preparation
Attack
Extraction
Evict line
Detect miss
Prime+Probe
Fill line
Detect hit
Flush+Reload Evict+Reload
Spectre
Meltdown
Index search
Fill (Prime) cache
Flush (Evict) cache
(Maliciously) train
branch predictor
Prepare page fault handler

## Slide 40: Spectre v1 (Bound Check Bypass)
// Spectre PoC code
uint8_t temp = 0;
if (secret_index < arr1_size) {
val1 = arr1[secret_index];
val2 = arr2[val1 * 16];
temp &= val2;
}
// cache timing attack
for (ii = 0; ii < 64; ++ii) {
temp &= arr2[ii * 16];
}
Bound check to enforce correct execution.
Maliciously train branch predictor so that out-of-bound index can bypass.
Speculatively read secret data.
Convert secret data into searchable index.
Speculative fill.
Cache timing attack (Flush+Reload).
Branch misprediction identified @exec.
Instructions flushed, but cache unchanged.
Notes: Spectre exploits speculative execution. Here is the PoC code.
With a given index, in the normal condition, code within if clause never executed.
However, branch predictor can be maliciously trained so that out-of-bound array access can be executed.
In the next line, secret data is speculative read.
Then, secret data is converted into extractable index, which will be speculatively written into the cache.
Later, once branch misprediction is identified, these wrong-path instructions are flushed, but cache state will not be reverted.
Finally, through flush+reload timing attack, secret data can be extracted.

## Slide 41: Comparing Meltdown vs. Spectre

## Slide 42: Software Mitigation for Spectre
New barrier!
  For Arm: CSDB
    Don’t allow speculative execution across this barrier (under certain conditions)
Works, but..
  Still need to modify program to insert these
    Existing code will need to change
    Need to remember to insert these for sensitive code
  Barriers will impact performance
    What is the common case?

## Slide 43: Hardware Mitigation for Spectre
The abstraction between architecture and microarchitecture is compromised!
Naïve approach -> Be conservative and don’t allow much speculation
  Huge impact on performance!
Need to rethink we approach hardware design fundamentally!
  Very active area for research