## Slide 1: Modern Microarchitecture and Future Directions
EE382N.1 Lecture 26
Dam Sunwoo
Arm Research
The University of Texas at Austin

## Slide 2: Reminders
How was the guest lecture on Machine Learning?
Lab 6
  Due Dec 12 (Wednesday), 11:59pm
Final Exam
  December 14 (Friday), 7-10pm
  ECJ 1.214 (NOT OUR USUAL CLASSROOM)
Grad Lab
  Due Dec 17 (Monday), 11:59pm

## Slide 3: Modern Microarchitecture

## Slide 4: Trace Cache (Intel Pentium 4)
Cache that stores dynamic stream of instructions (trace)
Increases instruction fetch bandwidth (less breaks)
[Rotenberg+, MICRO 1996]
MICRO Test of Time Award in 2015

## Slide 5: Micro-operation Cache (MOP/uOP Cache)
Store uops of decoded instructions
No need to decode again if found in the uop cache
Supposedly used in Intel Sandy Bridge and successive microarchitectures and AMD Zen
[Solomon+, ISLPED 2001]
[Anandtech]

## Slide 6: Reprise: Two-Level Branch Prediction
Branch history and branch address combined to index into Pattern History Table (PHT) of 2b saturating BPs
  2b used to predict branch direction
  When branch resolved, update 2b
1
1
0
0
1
1
1
PHT (2bc)
BHR
[Yeh+, MICRO 1991]
1
0
[GSHARE]
[Scott McFarling, 1993]

## Slide 7: Perceptron Branch Predictor
Perceptron: single-layer neural network
  binary linear classifier
Applied to branch prediction
  Alternative to two-bit counter
[Jimenez+, HPCA 2001]

## Slide 8: TAGE Branch Predictor
(partially) TAgged GEometric history length branch prediction
Exponentially longer (folded) history for high-order tables
Cascaded structure gives priority to matches with longer history
Efficient usage of tables with combination of short and long histories
  Only use long history when it matters
[Seznec+, JILP 2006]

## Slide 9: Data Prefetching
Regular patterns
  Next-line
  Stride
  …
Jouppi’s “Stream Buffer”
  Each stream buffer holds one stream of sequentially prefetched cache lines
  Can have multiple streams
  Can have prefetch storage separate from cache
[Jouppi, ISCA 1990]

## Slide 10: Best-Offset (BO) Prefetcher
Periodically train to find “best-offset” to prefetch from a given set of candidate offsets
[Michaud, HPCA 2016]
Winner of DPC2 (2015)
462.libquantum
470.lbm
459.GemsFDTD
433.milc

## Slide 11: Spatial Memory Streaming (SMS) Prefetcher
Identify irregular spatial patterns to prefetch (many instances of same structure in data)
Patterns within region represented by bitvector
[Somogyi+, ISCA 2006]

## Slide 12: Markov Prefetcher
Correlation-based Prefetching
  Each table entry holds list of addresses that have immediately followed the current miss address in the past
Length of correlated streams can vary from two to several hundred
  Large storage needed
[Joseph+, ISCA 1997]
(figure from [Nesbit+, HPCA 2004])

## Slide 13: Global History Buffer (GHB)
Maintain large FIFO history buffer
Buffer can be too large to fit on-hip
[Nesbit+, HPCA 2004]

## Slide 14: Irregular Stream Buffer (ISB)
Remap irregular address stream into sequential structural address space
Synchronize on-chip metadata based on TLB residency
[Jain+, MICRO 2013]

## Slide 15: Prefetcher Metrics / Parameters
Accuracy
  Used prefetches / sent prefetches
Coverage
  Prefetched misses / all misses
Timeliness
  On-time prefetches / used prefetches
Traffic
  Memory bandwidth consumed with prefetcher / without prefetcher
Prefetch distance (lookahead)
  How for ahead of the demand stream
Prefetch degree
  How many prefetches per demand access

## Slide 16: Cache Replacement
LRU: Least Recently Used
RRIP: Re-reference Interval Prediction [Jaleel+, ISCA 2010]
SHiP: Signature-based Hit Predictor [Wu+, MICRO 2011]
Hawkeye: Learn per-PC cache behavior by applying Belady’s OPT on previous accesses [Jain+, ISCA 2016], Winner of CRC2 (2017)

## Slide 17: Value Prediction
Predict data values within core
Speculatively breaks true data dependency to increase ILP in OOO cores
  “branch prediction but for values”
Proposed by 4 independent groups in mid-90’s
  AMD, Technion, CMU, Wisconsin
No known commercial implementation (yet)
Gaining some interest
[Lipasti+, MICRO 1996]
MICRO Test of Time Award 2017

## Slide 18: Intel Nehalem (2008)
[source: Wikipedia]

## Slide 19: Intel Skylake (2015)
[source: https://www.nextplatform.com/2017/08/04/drilling-xeon-skylake-architecture/ ]

## Slide 20: Arm Cortex-A76 (2018)
[source: https://images.anandtech.com/galleries/6373/02_Cortex-A76%20Deep%20Dive%20Final_NoWM_12.png]

## Slide 21: Future Directions

## Slide 22: What have we learned?
From Lecture 1…

## Slide 24: Course Schedule from Lecture 1
We covered all topics!

## Slide 25: Back to the Abstraction Layers

## Slide 26: Challenges (some old and some new)
Moore’s law slowing down / ending
Memory wall
Limited ILP
Power wall
Multi-core / Many-core scalability
Parallel programming still difficult
Security exploits in microarchitecture
…
Even more dependency on a better architecture than ever!

## Slide 27: New Technologies and Opportunities
New memory technologies
3D IC technology
Non-von-Neumann architectures
Specialization
  Machine learning
  Accelerators / domain-specific computation
  Generalization of specialization
Applying ML to architecture
Reconfigurable computing (in the cloud)
Security and Privacy for everything
And beyond…
  Superconducting Electronics – Very high frequencies and efficiencies may be possible
  Quantum Computing
  …

## Slide 28: Fundamentals don’t change
Everything is a trade-off!
Single-threaded performance always important (remember Amdahl’s law)
Tricks of the trade (from Mattan)
  Locality: when things are nearby, they are cheaper and faster
    Hierarchy
  Parallelism: do more at the same time
    Pipelining, Multiple functional units
  Reordering: schedule operations to maximize efficiency
    OOO processing, memory scheduling
  Speculation: learn from the past to predict the future
    Branch prediction, prefetching
  Heterogeneity: if one component isn’t perfect, use multiple types
    Memory heterogeneity, big.LITTLE processing, accelerators

## Slide 29: Other classes to learn more
Yale Patt:
  EE382N.19 Microarchitecfture
Mattan Erez:
  EE382N.22 Computer Architecture – User System Interplay
  EE382N.20 Computer Architecture – Parallelism and Locality
Calvin Lin:
  CS395T: Prediction Mechanisms in Computer Architecture
Lizy John:
  EE382N: Superscalar Microprocessor Architecture
  EE382N: Computer Performance Evaluation and Benchmarking
In general, I recommend having a good breadth of knowledge in layers around your focus layer
  For computer architecture / microarchitecture:
  VLSI courses, Operation Systems, Compiler, Security, Machine Learning …

## Slide 30: Related Conferences to Keep Track of State-of-the-Art
ISCA: Computer Architecture
MICRO: Microarchitecture
HPCA: High Performance Computer Architecture
ASPLOS: Architectural Support for Programming Languages and Operation Systems
PACT: Parallel Architectures and Compilation Techniques
CGO: Code Generation and Optimization
PLDI: Programming Language Design and Implementation
SC: SuperComputing
ICS: SuperComputing
ISPASS: Performance Analysis
IISWC: Workload Characterization
SIGMETRICS: Computer Systems Performance Evaluation
….

## Slide 31: Computer Architecture Competitions
Championship Branch Prediction
  CBP1 – 2004
  CBP2 – 2006
  CBP3 – 2011
  CBP4 – 2014
  CBP5 – 2016
Data Prefetching Championship
  DPC1 – 2009
  DPC2 – 2015
Cache Replacement Championship
  CRC1 – 2010
  CRC2 – 2017
Championship Value Prediction
  CVP1 – 2018
2019?

## Slide 32: Questions…on anything?
This lecture or any of the past lectures?
Any feedback is also welcome
Technical or non-technical?
Architecture research?
Career advice?
Industry vs. Academia?
To do Ph.D or not?

## Slide 33: Good luck and stay in touch!
Final reminder for eCIS:
  Today is the last day (Dec 10)!
  https://utdirect.utexas.edu/ctl/ecis/index.WBX
Contact info:
  Email: Dam.Sunwoo@arm.com
  Feel free to add me on LinkedIn